## Slide 1
CCNA 200-301 V2.0
02
The Physical Layer and Cable Faults
Part I — Foundations
EXAM TOPICS
1.1
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 2: The Physical Layer and Cable Faults. Blueprint topics: 1.1.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
• Select the right medium — copper, multimode fibre, single-mode fibre — for a given distance and speed.
• Read the interface counters that expose a physical fault, and say which counter implicates which cause.
• Diagnose the classic faults: duplex mismatch, speed mismatch, wrong cable type, bad pin-out, dirty or over-long fibre, and a transceiver operating outside its optical budget.
• Distinguish a port that is down from a port that is up and damaging traffic — the second is far more dangerous.
Notes: The Physical Layer and Cable Faults 1.1

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Chapter 1 for the layered model and the idea of a collision domain.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
twisted pair
Cat5e/Cat6
multimode
single-mode
SFP
attenuation
auto-negotiation
duplex mismatch
CRC error
runt
giant
late collision
input error
pin-out
straight-through
crossover
Auto-MDIX
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
Read the topic wording
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
This is what the blueprint actually asks for
Topic 1.1 says diagnose interface and cable issues, and then names them: “collisions, errors, mismatched duplex, speed, distance, interface, signal levels, pin out, and cable types”. That list is a syllabus in itself. You will not be asked to describe a cable; you will be shown counters and asked what is wrong.

## Slide 7
Choosing the medium
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1

## Slide 8
DEFINITION
Bits per second, and why it is not bytes
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Link speeds are always quoted in bits per second: 1 Gbps is one thousand million bits each second. File sizes are quoted in bytes, and a byte is eight bits.
So a 1 Gbps link moves at most about 125 megabytes per second, not 1000 — divide by eight. The lower-case b means bits and the upper-case B means bytes, which is the entire difference between Mbps and MBps.
Two further distinctions worth having straight from the start:
• Bandwidth is the rated capacity of the link — what it could carry.
• Throughput is what you actually got, after overhead, contention, errors and whatever the far end could manage.
Throughput is always lower, and a user reporting “slow” is reporting throughput. Nothing in this chapter changes bandwidth; several things in it quietly destroy throughput.

## Slide 9
DEFINITION
Duplex, and attenuation
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Duplex is who may transmit, and when.
• Half duplex — one end at a time, like a walkie-talkie. If both transmit at once the signals overlap and the frames are destroyed; that overlap is a collision, and each end is expected to detect it, back off and retry.

## Slide 10
DEFINITION
Duplex, and attenuation (continued)
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
• Full duplex — both ends at once, on separate pairs of wires, like a telephone call. Collisions are impossible, so a full-duplex port that reports collisions is telling you something is badly wrong. That is the single most useful sentence in this chapter.
Modern switched links are full duplex, and both ends normally agree on it through auto-negotiation — a brief exchange when the link comes up in which each end states what it can do and both pick the best they share.
Attenuation is separate and simpler: a signal loses strength with distance and through material. Every distance limit in the table below is really an attenuation limit — the point at which the far end can no longer reliably tell a 1 from a 0.

## Slide 11
CONCEPT
Distance is a fault, not a preference
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
The exam names distance as a diagnosable issue for a reason. Exceed the reach of a medium and the link does not fail cleanly — it comes up and then corrupts frames, which shows as climbing CRC errors rather than a down port. A 95 m run that works in winter and fails in summer is a real phenomenon, and the answer is fibre, not another patch lead.

## Slide 12
The counters that name the fault
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1

## Slide 13
VERIFY
show interfaces GigabitEthernet0/1
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
SW1#
GigabitEthernet0/1 is up, line protocol is up (connected)
Hardware is Gigabit Ethernet, address is 00d0.58a1.0201
MTU 1500 bytes, BW 1000000 Kbit, DLY 10 usec
Full-duplex, 1000Mb/s, media type is 10/100/1000BaseTX
5 minute input rate 41000 bits/sec, 12 packets/sec
284517 packets input, 39281044 bytes, 0 no buffer
Received 1204 broadcasts (0 multicasts)
0 runts, 0 giants, 0 throttles
0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored
271033 packets output, 33771201 bytes, 0 underruns
0 output errors, 0 collisions, 0 interface resets
0 late collision, 0 deferred
Notes: A straight-through cable connects pin 1 to pin 1; a crossover swaps the transmit and receive pairs. Historically you needed a crossover between two devices of the same kind — switch to switch, PC to router — and a straight-through between unlike devices. Auto-MDIX makes the switch detect and correct this itself, and it is on by default on every modern platform. It is still examinable because it fails in two situations: when a port has been hard-coded to a speed and duplex (Auto-MDIX requires auto-negotiation to be on), and on older or simulated gear. If a link between two switches will not come up and both ends are hard-coded, the pin-out is a live suspect.

## Slide 14
CONCEPT
The duplex mismatch, in one paragraph
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Auto-negotiation lets two ports agree on speed and duplex. If one end is set to duplex full by hand and the other is left on auto, the auto end cannot detect duplex, falls back to half, and you have a mismatch. The half-duplex end listens before transmitting and treats simultaneous transmission as a collision; the full-duplex end transmits whenever it likes. The link stays up. It just loses a percentage of every conversation, and the symptom the user reports is “the network is slow”, not “the network is down”.
The fix is to set both ends the same way. The rule of thumb is: leave both on auto, or hard-code both. Never one of each.
Notes: That is a healthy port: every error counter zero, full duplex, and the speed matching the media. Learn what this looks like, because you diagnose by difference.

## Slide 15
CONFIGURE
A hard-coded access port, both ends matching
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
IOS · configuration mode
interface GigabitEthernet0/1
description Link to SW2 - speed and duplex fixed at both ends
speed 1000
duplex full
no shutdown

## Slide 16
VERIFY
show interfaces GigabitEthernet0/25 transceiver
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
SW1#
Optical Optical
Temperature Voltage Tx Power Rx Power
Port (Celsius) (Volts) (dBm) (dBm)
--------- ----------- ------- -------- --------
Gi0/25 33.2 3.31 -2.4 -28.9
Notes: Topic 1.1 names signal levels. On a fibre link the transceiver reports how much light it is transmitting and receiving, in dBm, and a receive level below the optic’s sensitivity produces exactly the same symptom as a bad copper cable — a link that is up with climbing CRC errors.

## Slide 17
COMMON PITFALLS · Fibre and signal levels
Common pitfalls
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
• Replacing the cable first. It is the most expensive check in time and the least likely single cause on a link that has been working. Read the counters first: they tell you which of six causes it is.
• Treating “up/up” as healthy. A port can be up, passing traffic, and corrupting five per cent of it. The exam will show you exactly this and expect you not to declare it fine.
• Hard-coding one end. The commonest way to create a duplex mismatch is to fix one side “to be safe”.
• Reading raw totals instead of a rate. Counters accumulate since the last clear. Ten thousand CRC errors over two years is noise; ten thousand since yesterday is a fault. Use clear counters and watch.
Notes: A receive power of -28.9 dBm against a typical sensitivity of about -23 dBm means the link is starved of light. Causes, in the order worth checking: a dirty or unseated connector, a bend or break in the fibre, too many patch panels, a run longer than the optic supports, or a single-mode optic on multimode fibre.

## Slide 18
BREAK & FIX · SYMPTOM
Chapter 2
“The file server is slow, but it is not down”.
A user copies a large file and gets a fraction of the expected throughput. Ping succeeds with no loss. You look at the access port:
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1

## Slide 19
BREAK & FIX · YOUR MOVE
Chapter 2
“The file server is slow, but it is not down”.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 20
BREAK & FIX · EVIDENCE
Chapter 2
show interfaces GigabitEthernet0/7 | include duplex|collision|CRC
SW1#
Half-duplex, 100Mb/s, media type is 10/100/1000BaseTX
14432 input errors, 118 CRC, 0 frame, 0 overrun, 0 ignored
0 output errors, 89211 collisions, 0 interface resets
2244 late collision, 0 deferred
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 2
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Notes: The elimination matters as much as the answer.

## Slide 22
BREAK & FIX · DIAGNOSIS
Chapter 2
Why it is doing that
Diagnosis. The port is half duplex at 100 Mbps on gigabit-capable media, with a very large collision count and — decisively — late collisions. Late collisions on a modern switched link are the signature of a duplex mismatch: the far end is transmitting full duplex while this end still listens before sending. The small CRC count is a consequence of the collisions, not a separate cable fault.
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1

## Slide 23
BREAK & FIX · THE FIX
Chapter 2
And the lesson
Fix. Find the server NIC setting. It has almost certainly been hard-coded to full duplex while the switch port was left on auto. Set both ends to auto, or both to speed 1000 / duplex full, then clear counters and confirm the errors stop climbing. If they do not, now suspect the cable.
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1

## Slide 24
LAB · PACKET TRACER
Reading a broken link
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Topology. Two 2960 switches connected by one link; a PC on each.
1. Cable SW1 Gi0/1 to SW2 Gi0/1. Confirm both PCs can ping each other, then run show interfaces Gi0/1 on both and record the speed, duplex and every error counter while the link is healthy.
2. On SW1 only, set speed 100 and duplex half. Leave SW2 on auto.
3. Generate traffic between the PCs. Record what changes on each side. Which counter moved first?

## Slide 25
LAB · PACKET TRACER
Reading a broken link (continued)
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
4. Repeat with SW1 at duplex full and SW2 on auto — the classic mismatch. Note that the link stays up.
5. Extension. Without looking at your own configuration, hand the topology to a partner, have them introduce one fault from this chapter, and diagnose it from show output alone in under three minutes.
Verification. You should be able to state, from counters only, whether a link is healthy, mismatched, or physically damaged.

## Slide 26
CHECKPOINT 1 of 3
A gigabit link is up. collisions is increasing and the interface reports full duplex. What single conclusion can you draw, and why is it certain?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 27
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
A gigabit link is up. collisions is increasing and the interface reports full duplex. What single conclusion can you draw, and why is it certain?
That the two ends disagree about duplex. It is certain because a full duplex link cannot have collisions — there is no shared medium to collide on. The counter can only be incrementing because the local end is actually running half duplex, or because the far end is and is causing them.

## Slide 28
CHECKPOINT 2 of 3
A fibre link shows Rx power of -31 dBm against a sensitivity of -23 dBm. Give three causes in the order you would check them.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 29
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
A fibre link shows Rx power of -31 dBm against a sensitivity of -23 dBm. Give three causes in the order you would check them.
In order: a dirty or damaged connector; the wrong optic or wavelength for the distance; and excessive length or a bad splice. Check the cheapest first — clean the connector before ordering hardware.

## Slide 30
CHECKPOINT 3 of 3
Why is a port that is administratively down easier to deal with than one that is up with rising CRC errors?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 31
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
Why is a port that is administratively down easier to deal with than one that is up with rising CRC errors?
Because it is unambiguous. Administratively down is a decision somebody made, recorded in the configuration, and reversible with one command. A port that is up with rising CRC errors is intermittently working, so traffic is partly passing, users report “slow” rather than “down”, and the cause could be cable, connector, optic, EMI or duplex.

## Slide 32
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
• Copper is 100 m, full stop. Multimode reaches a campus; single-mode reaches a city. Exceeding a medium’s reach corrupts frames rather than dropping the link.
• Diagnose from counters, not from intuition. CRC without collisions points at the cable; collisions on a full-duplex link point at duplex; late collisions are close to proof of a duplex mismatch.
• Set both ends of a link the same way — both auto, or both fixed.
• “Up/up” does not mean healthy. The dangerous fault is the one that passes most traffic and damages the rest.

## Slide 33
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 2. The Physical Layer and Cable Faults
1.1
• On fibre, read show interfaces …{} transceiver. Light levels are a diagnosable fault the blueprint names explicitly.

## Slide 34
Where we got to
• Copper is 100 m, full stop. Multimode reaches a campus; single-mode reaches a city. Exceeding a medium’s reach corrupts frames rather than dropping the link.
• Diagnose from counters, not from intuition. CRC without collisions points at the cable; collisions on a full-duplex link point at duplex; late collisions are close to proof of a duplex mismatch.
• Set both ends of a link the same way — both auto, or both fixed.
• “Up/up” does not mean healthy. The dangerous fault is the one that passes most traffic and damages the rest.
NEXT
Chapter 3 — Ethernet, Frames and Switching