## Slide 1
CCNA 200-301 V2.0
06
TCP, UDP and the Diagnostic Toolkit
Part I — Foundations
EXAM TOPICS
2.4
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 6: TCP, UDP and the Diagnostic Toolkit. Blueprint topics: 2.4.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
• Explain what a port number identifies, and recognise the well-known ports that appear in access lists and in fault reports.
• Choose correctly between TCP and UDP behaviour when reasoning about a symptom.
• Use ping, extended ping and traceroute deliberately, varying source, size and count to test a specific hypothesis.
• Read packet capture output well enough to say which direction failed.
Notes: TCP, UDP and the Diagnostic Toolkit 2.4

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Chapter 4 for addressing, Chapter 3 for what a switch does with a frame.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
port
socket
TCP
UDP
three-way handshake
acknowledgement
retransmission
well-known port
ephemeral port
ICMP
echo request
TTL
extended ping
traceroute
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
The toolkit is the exam
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
This is what the blueprint actually asks for
Topic 2.4 names the tools by name: “show commands (including show logs), ping, extended ping, trace route, and packet capture output”. It is one of the eight troubleshoot topics, and the tools in it are how you will answer the other seven. Learn them as instruments, not as trivia.

## Slide 7
CONCEPT
TCP or UDP, and what each failure looks like
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
TCP establishes a connection with a three-way handshake — SYN, SYN-ACK, ACK — numbers every byte, acknowledges what arrives and retransmits what does not. It costs latency and gains reliability.
UDP sends and forgets. No handshake, no acknowledgement, no retransmission. It is right for anything where a late packet is worse than a lost one, and for short exchanges where a handshake would double the cost — which is why DNS and DHCP use it.
The diagnostic value is in how they fail. A blocked TCP port produces a connection timeout or refusal — something definite. A blocked UDP port often produces nothing at all, because there was never going to be an acknowledgement. “It just hangs” points at UDP or at a one-way path; “connection refused” means something answered and said no.
Notes: An IP address identifies a host. A port number identifies which program on that host. Together they form a socket, and a conversation is defined by four things: source address, source port, destination address, destination port. Client programs use a high-numbered ephemeral port as their source. This is why a return packet is not simply “port 80” — it is addressed to whatever ephemeral port the client opened, and why stateless access lists need care (Chapter 24).

## Slide 8
Ping, and how to ping deliberately
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 9
VERIFY
ping 192.168.20.10
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
R1#
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 192.168.20.10, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/2/4 ms
Notes: Ping sends an ICMP echo request and waits for a reply. It proves that a path exists in both directions — a point worth dwelling on, because a successful ping rules out far more than a failed one confirms.

## Slide 10
CONCEPT
The extended ping is the one that finds faults
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
A plain ping from a router sources the packet from the exit interface. That is often not the address you care about. Extended ping lets you set the source, and this single option answers the commonest routing question: “does the far end have a route back to this subnet?”
Run ping with no arguments to enter the extended dialogue.

## Slide 11
VERIFY
ping
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
R1#
Protocol [ip]:
Target IP address: 192.168.30.10
Repeat count [5]: 100
Datagram size [100]: 1500
Timeout in seconds [2]:
Extended commands [n]: y
Source address or interface: 192.168.20.1
Type of service [0]:
Set DF bit in IP header? [no]: yes
Sweep range of sizes [n]:
Sending 100, 1500-byte ICMP Echos to 192.168.30.10, timeout is 2 seconds:
Packet sent with a source address of 192.168.20.1
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
Success rate is 100 percent (100/100), round-trip min/avg/max = 1/3/12 ms

## Slide 12
Traceroute
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 13
VERIFY
traceroute 192.168.30.10
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
R1#
Type escape sequence to abort.
Tracing the route to 192.168.30.10
1 10.0.12.2 4 msec 1 msec 1 msec
2 10.0.23.3 8 msec 5 msec 4 msec
3 * * *
4 * * *
Notes: Source address — test the return path for a specific subnet. Repeat count — 100 pings exposes intermittent loss that five will miss. Datagram size with DF bit set — finds MTU problems. If 1500 fails and 1400 succeeds, something on the path cannot carry a full-size frame. Traceroute sends packets with deliberately small TTL values. The first router decrements TTL to zero, discards the packet and reports back; the second does the same for TTL 2, and so on. The result is a list of hops.

## Slide 14
WATCH OUT
Where a traceroute stops is not always where the fault is
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Asterisks mean no reply from that hop. That can mean the fault is there — or that the hop is configured not to reply, or that the return path from that hop is broken while the forward path is fine. A traceroute that dies at hop 3 narrows the search to hop 3 onwards; it does not convict hop 3. Confirm with an extended ping sourced from an address the far end should know.

## Slide 15
Reading a capture
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 16
VERIFY
show capture BUF
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
SW1#
1 0.000000 192.168.20.10 -> 192.168.30.10 ICMP Echo request id=1 seq=1
2 2.001113 192.168.20.10 -> 192.168.30.10 ICMP Echo request id=1 seq=2
3 4.002240 192.168.20.10 -> 192.168.30.10 ICMP Echo request id=1 seq=3

## Slide 17
COMMON PITFALLS · Reading a capture
Common pitfalls
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
• Treating a failed ping as proof of a broken forward path. Ping needs both directions. Half the time the forward path is fine.
• Pinging from the wrong source. A router pinging from its exit interface tests a path the users never take.
• Concluding from five packets. Intermittent loss needs a hundred.
• Forgetting that ICMP may be filtered. Plenty of hosts and firewalls drop echo requests by policy. “It does not ping” is not the same as “it is down”.
Notes: Three requests, no replies. That is a one-way path: the packets are leaving and arriving, but nothing is coming back. The fault is on the return path or at the destination host, and it is emphatically not the local switch — which is exactly the conclusion the capture is there to let you draw.

## Slide 18
BREAK & FIX · SYMPTOM
Chapter 6
Web server reachable by IP, refuses connections by name and port.
Users cannot load an internal site. From a workstation, ping 10.20.5.40 succeeds with 0% loss. Browsing to the address times out.
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 19
BREAK & FIX · YOUR MOVE
Chapter 6
Web server reachable by IP, refuses connections by name and port.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 20
BREAK & FIX · DIAGNOSIS
Chapter 6
Why it is doing that
Diagnosis. Ping proves layer 3 connectivity in both directions, so addressing, masks, routing and the physical path are all sound. The failure is above layer 3 — either the service is not listening, or something is filtering TCP 443 specifically. A timeout rather than a refusal points at a filter: a closed port on a live host normally answers with a reset.
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 21
BREAK & FIX · THE FIX
Chapter 6
And the lesson
Fix. Test the port rather than the host. From a router on the path, an extended ping cannot help — it is ICMP only — so use telnet 10.20.5.40 443: a blank screen means the port is open, a refusal means closed, and a hang means filtered. Then walk the access lists on the path (Chapter 24). Do not touch addressing; the ping already cleared it.
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4

## Slide 22
LAB · PACKET TRACER
Diagnose with intent
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Topology. Two routers back to back, one LAN each, one PC per LAN.
1. Address everything and confirm end-to-end ping between the PCs.
2. From R1, run a plain ping to the far PC, then an extended ping sourced from the LAN interface. Explain why the second is the more useful test.
3. Remove the return route on R2. Predict what a ping from PC-A will show, and what a traceroute will show, before testing.
4. Restore the route. Now set the far LAN interface MTU to 1400, and use an extended ping with size 1500 and the DF bit set. Record the result.
5. Run a hundred-packet ping and record whether any loss appears.

## Slide 23
LAB · PACKET TRACER
Diagnose with intent (continued)
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
6. Extension. Have a partner break one thing — an address, a mask, a route or an interface — and identify which, using only ping, extended ping and traceroute, in under five minutes.

## Slide 24
CHECKPOINT 1 of 3
A ping returns U.U.U. What has happened, and why is that more useful than five dots?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 25
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
A ping returns U.U.U. What has happened, and why is that more useful than five dots?
U is an ICMP destination-unreachable reply. Something on the path actively told you it could not deliver — so the packet was routed, and a device took responsibility. Five dots means silence, which could be anything from a dropped packet to an ACL to a dead host. A reply is always more informative than a timeout.

## Slide 26
CHECKPOINT 2 of 3
Why does an extended ping with a specified source often succeed when a plain ping from the same router fails?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 27
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
Why does an extended ping with a specified source often succeed when a plain ping from the same router fails?
Because a plain ping is sourced from the exit interface’s address, which the far end may have no route back to. Sourcing from a LAN interface or loopback uses an address the far end’s routing table knows about.

## Slide 28
CHECKPOINT 3 of 3
A traceroute shows three hops then asterisks. List three different explanations.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 29
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
A traceroute shows three hops then asterisks. List three different explanations.
Any of: an ACL blocking the probes; a device configured not to send ICMP time-exceeded messages; asymmetric return path with no route back; a firewall dropping the traffic; or the destination genuinely unreachable beyond that hop.

## Slide 30
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 6. TCP, UDP and the Diagnostic Toolkit
2.4
• A port identifies the program; address plus port is a socket.
• TCP handshakes, acknowledges and retransmits; UDP does none of it. Their failure modes differ, and the difference is diagnostic.
• Ping tests both directions at once. A success rules out a great deal; a failure convicts nothing on its own.
• Extended ping sets the source, size and DF bit — it is the tool that finds return-path and MTU faults.
• Traceroute narrows the search; it does not name the culprit.
• A capture showing requests and no replies is a one-way path.

## Slide 31
Where we got to
• A port identifies the program; address plus port is a socket.
• TCP handshakes, acknowledges and retransmits; UDP does none of it. Their failure modes differ, and the difference is diagnostic.
• Ping tests both directions at once. A success rules out a great deal; a failure convicts nothing on its own.
• Extended ping sets the source, size and DF bit — it is the tool that finds return-path and MTU faults.
NEXT
Chapter 7 — The IOS Command Line