## Slide 1
CCNA 200-301 V2.0
09
Edge-Host Connectivity: PoE, Voice, APs and IoT
Part II — Switching and Network Access
EXAM TOPICS
2.2
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 9: Edge-Host Connectivity: PoE, Voice, APs and IoT. Blueprint topics: 2.2.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
• Configure an access port correctly for each of the five device types the blueprint names.
• Explain how a data VLAN and a voice VLAN share one cable, and why that is not a trunk in the ordinary sense.
• Configure and verify Power over Ethernet, including budget and per-port limits.
• Diagnose the faults peculiar to edge ports: a phone that gets no power, an AP that sees only one VLAN, and a device in the wrong VLAN because it was plugged into the wrong socket.
Notes: Edge-Host Connectivity: PoE, Voice, APs and IoT 2.2

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Chapter 8 for VLANs and access ports. Chapter 7 for interface ranges.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Power over Ethernet
PoE, PoE+, UPoE
power budget
voice VLAN
data VLAN
standalone AP
controller-based AP
LWAPP/CAPWAP
IoT appliance
errdisable
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
Read topic 2.2 carefully — it lists the devices
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
This is what the blueprint actually asks for
Topic 2.2 is “configure Layer 2 switch port attributes for edge-host connectivity (VLAN, PoE, port channel, and LACP)” and then names five categories: desktops, printers and IoT appliances; wireless access points, standalone and controller-based; VoIP phones; virtualised hosts; and network appliances. The exam expects a different port configuration for several of them, so learn them as five cases rather than one.

## Slide 7
Power over Ethernet
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 8
DEFINITION
PoE
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Power over Ethernet delivers electrical power over the same twisted pair that carries data, so a phone, camera or access point needs one cable rather than two. The switch negotiates with the device and supplies only what it asks for.

## Slide 9
WATCH OUT
The budget is the constraint, not the port
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
A switch has a total power budget shared across all ports — often far less than the number of ports times the maximum per port. A 24-port PoE+ switch with a 370 W budget cannot deliver 30 W to all 24. When the budget is exhausted the switch stops powering new devices, so the symptom is “the phone I plugged in this morning works, the one I plugged in this afternoon does not”, and nothing in the port configuration looks wrong.
Check show power inline before you check anything else.

## Slide 10
CONFIGURE
PoE on an access port
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
IOS · configuration mode
interface GigabitEthernet0/10
description AP in the east corridor
switchport mode access
switchport access vlan 10
! auto is the default: negotiate and give the device what it asks for.
power inline auto
! Cap a port that must never take more than a phone's worth.
! power inline auto max 15400
no shutdown
!
! Never power this port -- a data-only port that must not energise.
interface GigabitEthernet0/24
power inline never

## Slide 11
VERIFY
show power inline
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
SW1#
Available:370.0(w) Used:71.5(w) Remaining:298.5(w)
Interface Admin Oper Power Device Class Max
(Watts)
--------- ------ ---------- ------- ------------------- ----- ----
Gi0/1 auto on 6.3 IP Phone 7960 2 15.4
Gi0/2 auto on 6.3 IP Phone 7960 2 15.4
Gi0/10 auto on 28.6 AIR-AP2802I 4 30.0
Gi0/11 auto off 0.0 n/a n/a 30.0
Gi0/24 never off 0.0 n/a n/a 0.0

## Slide 12
Voice VLANs: two VLANs, one cable
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 13
Voice VLANs: two VLANs, one cable
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
One cable, two VLANs, and no trunk. The phone tags its own traffic and passes the PC’s through untouched.
Notes: Read the top line first. Remaining is what decides whether the next device you plug in will power up at all. An IP phone has a small switch inside it: the cable from the wall goes into the phone, and the PC plugs into the back of the phone. Both need network access, and they should not be in the same VLAN — voice needs its own subnet for quality and for security.

## Slide 14
CONCEPT
How one access port carries two VLANs
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
The port is configured with a data VLAN and a voice VLAN. The switch tells the phone, over CDP or LLDP-MED, which VLAN ID to tag its own traffic with. The phone tags voice frames and passes the PC’s frames through untagged.
So the switch sees tagged voice traffic and untagged data traffic on one access port. Strictly this is a trunk carrying two VLANs, but it is configured as an access port and Cisco calls it a multi-VLAN access port. Do not configure switchport mode trunk here — the voice VLAN command does what is needed, and a real trunk would change how the PC’s untagged traffic is handled.

## Slide 15
CONFIGURE
A desk port for a phone with a PC behind it
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
IOS · configuration mode
interface GigabitEthernet0/1
description Desk 1 - phone with PC daisy-chained
switchport mode access
switchport access vlan 10
switchport voice vlan 30
! The PC should forward immediately rather than waiting for
! spanning tree -- see chapter on Rapid PVST+.
spanning-tree portfast
power inline auto
no shutdown

## Slide 16
VERIFY
show interfaces GigabitEthernet0/1 switchport
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
SW1#
Name: Gi0/1
Switchport: Enabled
Administrative Mode: static access
Operational Mode: static access
Access Mode VLAN: 10 (Staff)
Voice VLAN: 30 (Voice)

## Slide 17
Access points, standalone and controller-based
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 18
WATCH OUT
The most common AP misconfiguration
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Configuring a lightweight AP’s port as a trunk, or a standalone AP’s port as an access port. Both leave the AP reachable — it will get an address and appear healthy — while clients on some or all SSIDs get nothing. If wireless users on one SSID work and another SSID does not, look at the switch port before you touch the wireless configuration.
Notes: The blueprint distinguishes the two, and the distinction changes the port configuration completely.

## Slide 19
CONFIGURE
Both kinds of access point
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
IOS · configuration mode
! Lightweight AP: one access port in the AP management VLAN.
! Client traffic is tunnelled to the controller, so no client
! VLANs need to exist on this switch at all.
interface GigabitEthernet0/10
description Lightweight AP - CAPWAP to WLC
switchport mode access
switchport access vlan 50
power inline auto
spanning-tree portfast
!
! Standalone AP: a trunk, because the AP bridges each SSID
! into a different VLAN and tags them itself.
interface GigabitEthernet0/11
description Standalone AP - SSIDs in VLANs 10 and 20
switchport trunk encapsulation dot1q
switchport mode trunk
switchport trunk native vlan 50
switchport trunk allowed vlan 10,20,50
power inline auto

## Slide 20
Printers, IoT appliances and virtualised hosts
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 21
COMMON PITFALLS · Printers, IoT appliances and virtualised hosts
Common pitfalls
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
• PortFast on a port that leads to a switch. PortFast skips the spanning tree listening and learning states. On an edge port that is correct; on a port leading to another switch it can create a loop. Use BPDU guard alongside it (Chapter 12).
• Assuming the phone’s PC port is in the voice VLAN. It is not — untagged traffic from the PC lands in the data VLAN, which is the whole point.
• Ignoring the power class. A class 4 device on a switch with only 802.3af ports will not power up, however correct the configuration looks.
• Trunking to a lightweight AP. See the warning above.
Notes: Printers and IoT appliances — ordinary access ports. Put them in their own VLAN: they are rarely patched, often speak plaintext protocols, and are a favourite foothold. Add port security (Chapter 25) because they never move. Virtualised hosts — a server running virtual machines usually needs a trunk, because each VM may sit in a different VLAN and the hypervisor’s virtual switch tags accordingly. This is the one “end device” that is not an access port. Network appliances — firewalls, load balancers and the like. Read the vendor’s requirement; most want a trunk, some want several access ports.

## Slide 22
BREAK & FIX · SYMPTOM
Chapter 9
Half the wireless users work; the other half get no address.
Users on the Staff SSID are fine. Users on Guest associate to the wireless network but never receive an IP address. The AP is reachable and its configuration has not changed.
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 23
BREAK & FIX · YOUR MOVE
Chapter 9
Half the wireless users work; the other half get no address.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 24
BREAK & FIX · EVIDENCE
Chapter 9
show interfaces GigabitEthernet0/11 trunk
SW1#
Port Mode Encapsulation Status Native vlan
Gi0/11 on 802.1q trunking 50
Port Vlans allowed on trunk
Gi0/11 10,50
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 25
BREAK & FIX · YOUR MOVE
Chapter 9
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Notes: The elimination matters as much as the answer.

## Slide 26
BREAK & FIX · DIAGNOSIS
Chapter 9
Why it is doing that
Diagnosis. This is a standalone AP, correctly trunked, but the allowed VLAN list carries 10 and 50 only. VLAN 20 — the Guest SSID’s VLAN — is not permitted on the trunk, so Guest clients associate at the radio (which the AP handles alone) and then have no path to the DHCP server. Association succeeding while addressing fails is the signature of a VLAN that does not reach the wire.
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 27
BREAK & FIX · THE FIX
Chapter 9
And the lesson
Fix. Add the missing VLAN to the trunk: switchport trunk allowed vlan add 20. Note add — without it you replace the whole list and drop VLANs 10 and 50, taking down the users who were working. Confirm with show interfaces trunk, then have a Guest client renew.
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2

## Slide 28
LAB · PACKET TRACER
Wire an edge properly
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Topology. One PoE switch; an IP phone with a PC behind it; a lightweight AP; a printer.
1. Create VLANs 10 (Staff), 20 (Guest), 30 (Voice), 50 (AP-Mgmt) and 60 (Printers).
2. Configure the phone port with data VLAN 10, voice VLAN 30, PortFast and PoE. Verify both VLANs appear on the one port.
3. Configure the AP port as an access port in VLAN 50 with PoE.
4. Configure the printer port in VLAN 60 with PortFast.
5. Run show power inline and record the budget, the used figure and the class of each powered device.
6. Set power inline never on the printer port and observe what happens to a PoE device moved there.

## Slide 29
LAB · PACKET TRACER
Wire an edge properly (continued)
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
7. Extension. Change the AP to standalone: reconfigure its port as a trunk carrying VLANs 10, 20 and 50, and explain in one sentence why the two AP types need opposite port configurations.

## Slide 30
CHECKPOINT 1 of 3
An IP phone powers up and works; a PC plugged into the back of it gets an address in VLAN 10. Which VLAN carries the phone’s own traffic, and how did the phone learn to use it?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 31
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
An IP phone powers up and works; a PC plugged into the back of it gets an address in VLAN 10. Which VLAN carries the phone’s own traffic, and how did the phone learn to use it?
The voice VLAN, tagged. The phone learned its VLAN ID from CDP or LLDP-MED advertised by the switch. The PC’s traffic stays untagged in the data VLAN, which is why one cable carries both.

## Slide 32
CHECKPOINT 2 of 3
A new AP will not power on. show power inline shows the port auto/off and Remaining:4.2(w). What is wrong?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 33
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
A new AP will not power on. show power inline shows the port auto/off and Remaining:4.2(w). What is wrong?
The switch has only 4.2 W of power budget left, which is not enough for the AP. This is a budget problem, not a port problem — the port is willing (auto) and the supply cannot meet the request. Add a power supply, move the AP, or free capacity elsewhere.

## Slide 34
CHECKPOINT 3 of 3
Why does a lightweight AP need only one VLAN on its switch port when it serves four SSIDs?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 35
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
Why does a lightweight AP need only one VLAN on its switch port when it serves four SSIDs?
Because it tunnels all client traffic to the wireless controller inside CAPWAP. The SSID-to-VLAN mapping is done by the controller, so the switch port only needs to reach the controller. A standalone AP bridges locally and does need a trunk.

## Slide 36
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 9. Edge-Host Connectivity: PoE, Voice, APs and IoT
2.2
• PoE classes: 15.4 W af, 30 W at, up to 90 W bt. The shared budget is what actually runs out, so read show power inline first.
• A voice VLAN plus a data VLAN on one access port lets a phone and a PC share a cable: the phone tags, the PC does not.
• Lightweight APs take an access port in the management VLAN; standalone APs take a trunk carrying every SSID’s VLAN. Getting this backwards breaks some SSIDs and not others.
• Printers and IoT devices belong in their own VLAN with port security. Virtualised hosts usually need a trunk.
• Use switchport trunk allowed vlan add, never bare allowed vlan, on a live trunk.

## Slide 37
Where we got to
• PoE classes: 15.4 W af, 30 W at, up to 90 W bt. The shared budget is what actually runs out, so read show power inline first.
• A voice VLAN plus a data VLAN on one access port lets a phone and a PC share a cable: the phone tags, the PC does not.
• Lightweight APs take an access port in the management VLAN; standalone APs take a trunk carrying every SSID’s VLAN. Getting this backwards breaks some SSIDs and not others.
• Printers and IoT devices belong in their own VLAN with port security. Virtualised hosts usually need a trunk.
NEXT
Chapter 10 — Trunking, 802.1Q and SVIs