## Slide 1
CCNA 200-301 V2.0
14
Troubleshooting Layer 2
Part II — Switching and Network Access
EXAM TOPICS
2.4
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 14: Troubleshooting Layer 2. Blueprint topics: 2.4.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• Apply a repeatable order of checks to a layer 2 fault instead of guessing.
• Select the right show command for a symptom, and read what it returns.
• Use show logging, ping, extended ping and capture output together to localise a fault.
• Diagnose the six faults that account for most switched-network problems.
Notes: Troubleshooting Layer 2 2.4

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
All of Part II. This chapter assembles Chapter 8 to Chapter 13 into a method.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
symptom
hypothesis
scope
errdisable
show logging
severity
divide and conquer
bottom-up
baseline
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
This chapter is the exam’s heaviest verb
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
This is what the blueprint actually asks for
Topic 2.4 — “troubleshoot basic Layer 2/Layer 3 connectivity and device operations using show commands (including show logs), ping, extended ping, trace route, and packet capture output” — is one of eight troubleshoot topics. Together with the eight configure topics they are 55% of the paper. The method below is worth more marks than any single technology in this book.

## Slide 7
Scope first, then layers
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 8
CONCEPT
Ask “how many?” before you ask “why?”
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
The single most useful question is how much is broken, because it tells you where to look before you have run a command.
• One device → that port, that cable, that host’s configuration.
• One VLAN, everywhere → the VLAN itself: does it exist, is it shut, is it allowed on the trunks, does its SVI have an address?
• Everything on one switch → that switch’s uplink, or spanning tree.
• Everything, everywhere → a loop, the root bridge, or a routing or gateway failure.
• Intermittent, under load → physical layer, duplex, or a saturated link. Almost never a VLAN.

## Slide 9
CONCEPT
Then work bottom-up
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Once you know the scope, walk the layers from the bottom. Each step is one command and rules out a whole class of cause.
• Is the port up? show interfaces status
• Is it clean? show interfaces — errors, duplex, speed
• Is it in the right VLAN? show interfaces switchport
• Does the switch see the device? show mac address-table
• Does the VLAN reach the next switch? show interfaces trunk
• Is spanning tree forwarding? show spanning-tree vlan

## Slide 10
CONCEPT
Then work bottom-up (continued)
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• Is there a gateway? show ip interface brief
Resist starting at step 7 because the user said “I cannot reach the internet”.

## Slide 11
The first three commands
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 12
VERIFY
show interfaces status
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
SW1#
Port Name Status Vlan Duplex Speed Type
Gi0/1 Uplink to SW2 connected trunk a-full a-1000 10/100/1000
Gi0/5 Desk 5 connected 10 a-full a-100 10/100/1000
Gi0/6 Desk 6 notconnect 10 auto auto 10/100/1000
Gi0/7 Desk 7 err-disabled 10 auto auto 10/100/1000
Gi0/8 Desk 8 connected 15 a-full a-1000 10/100/1000

## Slide 13
VERIFY
show logging | include LINK|LINEPROTO|ERR|SPANTREE
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
SW1#
%LINK-3-UPDOWN: Interface GigabitEthernet0/6, changed state to down
%SPANTREE-2-BLOCK_BPDUGUARD: Received BPDU on port Gi0/7 with BPDU Guard
enabled. Disabling port.
%PM-4-ERR_DISABLE: bpduguard error detected on Gi0/7, putting Gi0/7 in
err-disable state
%CDP-4-NATIVE_VLAN_MISMATCH: Native VLAN mismatch discovered on
GigabitEthernet0/1 (999), with SW2 GigabitEthernet0/1 (1).
Notes: One screen, four different faults visible. Gi0/6 notconnect — nothing plugged in, or a dead cable. Gi0/7 err-disabled — a protection feature fired; find out which. Gi0/8 is in VLAN 15, which may or may not be intended — compare against the design.

## Slide 14
WATCH OUT
Read the log before you read anything else
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
The log frequently contains the answer in plain English, timestamped. Above, it names the errdisable cause and a native VLAN mismatch nobody had reported — a fault that is silently bridging VLAN 999 and VLAN 1 between two switches.
Filter it. show logging | include with the keywords above turns hundreds of lines into the handful that matter.

## Slide 15
The six faults, and what each looks like
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 16
WORKED EXAMPLE
Working a fault end to end
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Symptom. “Nobody in accounts can reach the file server since this morning. Sales are fine.”
Scope. One VLAN, multiple users, more than one switch. That rules out a single cable and points at the VLAN or its path.
• show interfaces status on the access switch — accounts ports are connected in VLAN 30. Not a port problem.
• show mac address-table vlan 30 — addresses are being learned locally. The devices are alive and the switch sees them.

## Slide 17
WORKED EXAMPLE
Working a fault end to end (continued)
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• show interfaces trunk on the uplink — VLAN 30 appears in “allowed” but not in “forwarding and not pruned”.
• show spanning-tree vlan 30 — the uplink is Altn BLK.

## Slide 18
WORKED EXAMPLE
Working a fault end to end (continued)
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• show logging | include SPANTREE — a topology change overnight; a second switch was added and won the root election for VLAN 30.
Cause. Not a VLAN fault at all. The new switch became root for VLAN 30 only, which moved the tree and put the accounts uplink into blocking. Sales, in VLAN 20, still had the old root and were unaffected — which is exactly why only one VLAN broke.
Fix. Set the intended root explicitly for all VLANs, add root guard on the ports facing access switches, and confirm the uplink returns to Desg FWD.

## Slide 19
COMMON PITFALLS · The six faults, and what each looks like
Common pitfalls
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• Changing something before you have measured. If you reconfigure before capturing the current state you can no longer tell whether you fixed it or moved it.
• Changing more than one thing at once. Then you do not know which change worked, and you cannot write it up.
• Believing the reporter’s diagnosis. “The switch is broken” usually means “my thing does not work”. Take the symptom, discard the theory.
• Ignoring what still works. The working half of the network is evidence. Sales working and accounts failing localised the fault above faster than any command did.
• Skipping the log. It is timestamped and often explicit.

## Slide 20
BREAK & FIX · SYMPTOM
Chapter 14
Two symptoms, one cause, and a misleading first look.
Users report intermittent slowness. One user cannot connect at all. Both started after a contractor visited the comms room.
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 14
Two symptoms, one cause, and a misleading first look.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 22
BREAK & FIX · EVIDENCE
Chapter 14
show interfaces status | exclude connected
SW1#
Port Name Status Vlan Duplex Speed Type
Gi0/7 Desk 7 err-disabled 10 auto auto 10/100/1000
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 23
BREAK & FIX · EVIDENCE
Chapter 14
show logging | include ERR_DISABLE|MACFLAP
SW1#
%PM-4-ERR_DISABLE: bpduguard error detected on Gi0/7, putting Gi0/7 in
err-disable state
%SW_MATM-4-MACFLAP_NOTIF: Host 0011.2233.4455 in vlan 10 is flapping
between port Gi0/7 and port Gi0/12
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 24
BREAK & FIX · YOUR MOVE
Chapter 14
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Notes: The elimination matters as much as the answer.

## Slide 25
BREAK & FIX · DIAGNOSIS
Chapter 14
Why it is doing that
Diagnosis. Both symptoms are one event. The contractor plugged an unmanaged switch into Gi0/7 and, to “make sure it worked”, also patched it into Gi0/12. That created a loop: the MAC flap is the loop being seen from two ports, and the intermittent slowness is the resulting flooding. BPDU guard then errdisabled Gi0/7, which is the one port that is definitively dead — and which, by shutting, largely saved the network.
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 26
BREAK & FIX · THE FIX
Chapter 14
And the lesson
Fix. Remove the second patch lead. Confirm the flapping stops. Then recover the port with shutdown / no shutdown — after the cause is gone, not before, or it will simply errdisable again. Finally, note that BPDU guard did its job: without it this would have been a full broadcast storm rather than one dead port.
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4

## Slide 27
LAB · PACKET TRACER
Fix five faults against the clock
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Topology. Three switches, one router, six PCs across three VLANs — built, working, and then broken by a partner.
1. Build the network and confirm it works fully. Capture a baseline: show interfaces status, show interfaces trunk, show spanning-tree vlan and show ip interface brief from every device. You cannot troubleshoot without knowing what right looks like.
2. Hand the network to a partner, who introduces five faults from the table above without telling you which.
3. Find and fix them, writing down for each: the symptom, the scope, the command that proved it, and the fix. Give yourself twenty minutes.
4. Swap roles.

## Slide 28
LAB · PACKET TRACER
Fix five faults against the clock (continued)
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
5. Compare notes: which fault took longest, and would starting with scope rather than commands have found it faster?
6. Extension. Introduce a fault that produces no log message — a wrong access VLAN is a good one — and discuss why the log is a first stop rather than a complete answer.

## Slide 29
CHECKPOINT 1 of 3
Users on one VLAN across three switches lose connectivity; other VLANs are fine. What are the two most likely causes, and which command separates them?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Users on one VLAN across three switches lose connectivity; other VLANs are fine. What are the two most likely causes, and which command separates them?
Either the VLAN is missing from a trunk’s allowed list, or it has been deleted or shut down on one switch. show interfaces trunk separates them — read Vlans allowed and active, which reflects both the allowed list and whether the VLAN exists.

## Slide 31
CHECKPOINT 2 of 3
A port is errdisabled. You issue no shutdown and it errdisables again within seconds. What have you forgotten?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 32
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
A port is errdisabled. You issue no shutdown and it errdisables again within seconds. What have you forgotten?
To fix the cause. Err-disable is a symptom; whatever triggered it — a port security violation, a BPDU on a PortFast port — is still there and will trigger again the moment the port comes up.

## Slide 33
CHECKPOINT 3 of 3
Why does knowing what still works narrow a fault faster than knowing what is broken?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 34
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
Why does knowing what still works narrow a fault faster than knowing what is broken?
Because everything that still works is evidence you can trust, and it eliminates whole layers and paths at once. A user’s report tells you one thing is broken; knowing that four similar things are fine tells you where the fault cannot be, which is a much larger reduction in the search space.

## Slide 35
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 14. Troubleshooting Layer 2
2.4
• Establish scope first — one device, one VLAN, one switch, or everything. Scope points at the layer before you type anything.
• Then work bottom-up: port up, port clean, right VLAN, MAC learned, VLAN on the trunk, spanning tree forwarding, gateway present.
• Read show logging early. It is timestamped and often explicit.
• Six faults cover most cases: wrong VLAN, VLAN missing from a trunk, native VLAN mismatch, errdisable, spanning tree blocking, duplex mismatch.
• Capture a baseline while the network works. Change one thing at a time, and remove the cause before recovering an errdisabled port.

## Slide 36
Where we got to
• Establish scope first — one device, one VLAN, one switch, or everything. Scope points at the layer before you type anything.
• Then work bottom-up: port up, port clean, right VLAN, MAC learned, VLAN on the trunk, spanning tree forwarding, gateway present.
• Read show logging early. It is timestamped and often explicit.
• Six faults cover most cases: wrong VLAN, VLAN missing from a trunk, native VLAN mismatch, errdisable, spanning tree blocking, duplex mismatch.
NEXT
Chapter 15 — The Routing Table and How a Router Decides