## Slide 1
CCNA 200-301 V2.0
15
The Routing Table and How a Router Decides
Part III — IP Routing
EXAM TOPICS
3.1
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 15: The Routing Table and How a Router Decides. Blueprint topics: 3.1.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
• Read every column and code in show ip route.
• Apply the longest prefix match rule to determine which entry a given packet uses.
• Explain administrative distance and predict which source wins when two protocols offer the same prefix.
• Distinguish the three reasons a packet is dropped: no route, a route to null, and an unreachable next hop.
Notes: The Routing Table and How a Router Decides 3.1

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Chapter 4 for prefixes and masks — this chapter is unreadable without fluent subnetting. Chapter 10 for SVIs as gateways.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
routing table
prefix
next hop
exit interface
administrative distance
metric
longest prefix match
directly connected
local route
default route
gateway of last resort
null0
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
What a router is actually doing
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 7
DEFINITION
Routing table
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
The list of destinations a router knows how to reach, and for each one, the next hop — the neighbouring device to hand the packet to — and the interface to send it out of.
A router does not know the whole path. It knows one step. Every router along the way makes the same one-step decision independently, and the packet arrives because each of them was right about its own next hop. That is worth sitting with, because it explains why a fault three hops away looks like a working router with traffic disappearing into it.
Notes: A switch asks “which port is this MAC address on?”. A router asks a different and slightly harder question, once for every packet: Of everything I know how to reach, which entry best matches this destination, and where do I send the packet next?

## Slide 8
CONCEPT
One line, before twenty
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Every entry in the table has the same shape. Read this one slowly and the full dump below stops being a wall of text:
O 10.1.0.0/16 [110/20] via 10.255.0.2, 00:14:22, GigabitEthernet0/1
• O — how the router learned it. O is OSPF, S static, C connected, L local. The legend at the top of the output lists them all.
• 10.1.0.0/16 — what it reaches: the destination network and its prefix length.
• [110/20] — administrative distance and metric. 110 is how much the router trusts the source; 20 is how good this particular path is. Section sec:ad explains why those are two separate numbers.
• via 10.255.0.2 — the next hop.

## Slide 9
CONCEPT
One line, before twenty (continued)
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
• 00:14:22 — how long the route has been known.
• GigabitEthernet0/1 — the exit interface.
Connected and local routes have no distance, metric or next hop, because there is nothing between the router and them.

## Slide 10
Reading the table
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 11
VERIFY
show ip route
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
R1#
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP
O - OSPF, IA - OSPF inter area, N1 - OSPF NSSA external type 1
E1 - OSPF external type 1, E2 - OSPF external type 2
* - candidate default, U - per-user static route
Gateway of last resort is 203.0.113.1 to network 0.0.0.0
S* 0.0.0.0/0 [1/0] via 203.0.113.1
10.0.0.0/8 is variably subnetted, 4 subnets, 2 masks
O 10.1.0.0/16 [110/20] via 10.255.0.2, 00:14:22, GigabitEthernet0/1
C 10.255.0.0/30 is directly connected, GigabitEthernet0/1
L 10.255.0.1/32 is directly connected, GigabitEthernet0/1
S 10.9.9.0/24 [1/0] via 10.255.0.2
192.168.10.0/24 is directly connected, Vlan10
C 192.168.10.0/24 is directly connected, Vlan10
L 192.168.10.1/32 is directly connected, Vlan10

## Slide 12
CONCEPT
C and L are not the same thing
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
C is the subnet on a directly connected interface — the range the router can reach by ARP. L is a /32 host route for the router’s own address on that interface, so that traffic addressed to the router itself is delivered locally rather than forwarded.
You do not configure L routes; the router creates one for every address you give an interface. They appear in every table and are not a fault.

## Slide 13
Rule one: longest prefix match
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 14
CONCEPT
The most specific route wins, regardless of anything else
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
When several entries could carry a packet, the router uses the one with the longest prefix — the most 1 bits in the mask. Administrative distance and metric never override this; they only choose between entries with the same prefix length.

## Slide 15
WORKED EXAMPLE
Which entry carries the packet?
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Using the table above, a packet for 10.9.9.20:
• 0.0.0.0/0 — matches everything. Prefix length 0.
• 10.1.0.0/16 — does 10.9.9.20 fall inside? The /16 covers 10.1.0.0–10.1.255.255. No.
• 10.9.9.0/24 — covers 10.9.9.0–10.9.9.255. Yes. Prefix length 24.
Two entries match: the default and the /24. The /24 is longer, so the packet goes via 10.255.0.2. Note that the default route has a better administrative distance (1 versus 1 — equal here) and it still loses, because prefix length is decided first.
Now a packet for 172.20.5.1: only 0.0.0.0/0 matches, so it takes the gateway of last resort.

## Slide 16
Rule two: administrative distance
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 17
DEFINITION
Administrative distance
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Administrative distance ranks the trustworthiness of a route’s source. When two sources offer the same prefix at the same length, the lower distance is installed and the other is discarded — it does not even appear in the table.

## Slide 18
CONCEPT
Why a static route beats OSPF, and when that bites
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
A static route at distance 1 will always displace an OSPF route at 110 for the same prefix. That is usually what you want — until the static route’s path fails. OSPF would have re-routed; the static route sits there pointing at a dead path, because a static route has no way of knowing anything is wrong beyond the directly connected interface.
The deliberate use of this is the floating static route: a backup static configured with a distance higher than the dynamic protocol, so it stays out of the table until the dynamic route disappears. That is Chapter 16.

## Slide 19
Three ways a packet dies
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 20
WATCH OUT
A route in the table is not proof of reachability
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
The presence of an entry means the router knows where it would send the packet. It says nothing about whether the next hop is alive, whether the far end has a route back, or whether an access list drops it en route.
Confirm with an extended ping sourced from the relevant interface (Chapter 6) — that tests the return path too, which a route entry never does.

## Slide 21
VERIFY
show ip route 10.9.9.20
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
R1#
Routing entry for 10.9.9.0/24
Known via "static", distance 1, metric 0
Routing Descriptor Blocks:
* 10.255.0.2
Route metric is 0, traffic share count is 1

## Slide 22
COMMON PITFALLS · Three ways a packet dies
Common pitfalls
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
• Comparing metrics across protocols. An OSPF cost of 20 and a RIP hop count of 2 are not comparable. Administrative distance decides first, and only then does metric compare within one protocol.
• Thinking a better distance beats a longer prefix. It does not. Prefix length is decided first, always.
• Missing the gateway of last resort line. If it says not set, there is no default and anything unmatched is dropped.
• Reading L entries as duplicates. They are the router’s own addresses and belong there.
Notes: Querying a specific address rather than reading the whole table is faster and is what the exam expects when it asks which entry would be used.

## Slide 23
COMMON PITFALLS · Three ways a packet dies
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
• Assuming symmetry. Traffic reaching a destination does not mean the reply can return. Most one-way faults are a missing reverse route.

## Slide 24
BREAK & FIX · SYMPTOM
Chapter 15
The route is there and the ping still fails.
Users on 192.168.10.0/24 cannot reach 10.9.9.0/24. R1 has the route:
A ping from R1 to 10.9.9.20 succeeds. A ping from a user’s PC fails.
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 25
BREAK & FIX · YOUR MOVE
Chapter 15
The route is there and the ping still fails.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 26
BREAK & FIX · EVIDENCE
Chapter 15
show ip route 10.9.9.0
R1#
Routing entry for 10.9.9.0/24
Known via "static", distance 1, metric 0
Routing Descriptor Blocks:
* 10.255.0.2
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 27
BREAK & FIX · EVIDENCE
Chapter 15
ping 10.9.9.20 source Vlan10
R1#
Sending 5, 100-byte ICMP Echos to 10.9.9.20, timeout is 2 seconds:
Packet sent with a source address of 192.168.10.1
.....
Success rate is 0 percent (0/5)
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 28
BREAK & FIX · YOUR MOVE
Chapter 15
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Notes: The elimination matters as much as the answer.

## Slide 29
BREAK & FIX · DIAGNOSIS
Chapter 15
Why it is doing that
Diagnosis. The difference between the two pings is the source address. R1’s own ping is sourced from 10.255.0.1, which the far end knows about because it is the link between them. The PC’s traffic is sourced from 192.168.10.x, and the far router has no route back to that subnet. The forward path is fine; the return path does not exist.
Confirm it without leaving R1, using an extended ping that borrows the user’s source address:
Same destination, different source, opposite result — which is proof, not inference.
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 30
BREAK & FIX · THE FIX
Chapter 15
And the lesson
Fix. Add a route on the far router back to 192.168.10.0/24. Then re-run the same extended ping and expect five exclamation marks.
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1

## Slide 31
LAB · PACKET TRACER
Read the table, then predict the path
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Topology. Three routers in a line, a LAN on each end, and a second path between the outer two.
1. Address everything and confirm the connected routes appear. Identify every C and L entry and explain each L.
2. Add static routes so the two LANs can reach each other. Record the distance and metric shown.
3. Add a default route on one router. Note the S* and the gateway of last resort line.
4. Write down, before testing, which entry a packet to each of four addresses would use. Verify each with show ip route <address>.
5. Add a second, more specific route for one destination and confirm it wins over the less specific one, regardless of distance.

## Slide 32
LAB · PACKET TRACER
Read the table, then predict the path (continued)
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
6. Remove the reverse route on the far router and reproduce the one-way fault above using ping ... source.
7. Extension. Add a route pointing to Null0 for an unused prefix and observe how traffic to it fails compared with having no route at all.

## Slide 33
CHECKPOINT 1 of 3
A table contains 10.0.0.0/8 via OSPF and 10.5.0.0/16 via a static route. Which carries a packet to 10.5.1.1, and why?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 34
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
A table contains 10.0.0.0/8 via OSPF and 10.5.0.0/16 via a static route. Which carries a packet to 10.5.1.1, and why?
The static 10.5.0.0/16, because it is the longer prefix match. Administrative distance never enters into it — longest prefix match is applied first and decides between entries.

## Slide 35
CHECKPOINT 2 of 3
Both OSPF and a static route offer 192.168.50.0/24. Which is installed, and what happens to the other?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 36
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
Both OSPF and a static route offer 192.168.50.0/24. Which is installed, and what happens to the other?
The static route, distance 1 against OSPF’s 110. The OSPF route is not installed in the routing table but remains in the OSPF database, so it will appear if the static route is removed or its next hop becomes unreachable.

## Slide 37
CHECKPOINT 3 of 3
A route exists but pings fail. Name three causes and the single command that distinguishes the most common one.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 38
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
A route exists but pings fail. Name three causes and the single command that distinguishes the most common one.
A layer 2 problem on the path; an ACL blocking the traffic; or no return route at the far end. traceroute distinguishes the most common by showing where the packets stop, and whether they get there and cannot get back.

## Slide 39
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 15. The Routing Table and How a Router Decides
3.1
• One table, many sources. C connected, L the router’s own address, S static, O OSPF.
• [distance/metric]. Distance ranks the source; metric ranks paths within one protocol and is never compared across protocols.
• Longest prefix match decides first. Distance only breaks ties between equal-length prefixes.
• Connected 0, static 1, OSPF 110. A static route displaces OSPF and will not fail over unless you make it float.
• A route in the table proves intent, not reachability. Test the return path with an extended ping.

## Slide 40
Where we got to
• One table, many sources. C connected, L the router’s own address, S static, O OSPF.
• [distance/metric]. Distance ranks the source; metric ranks paths within one protocol and is never compared across protocols.
• Longest prefix match decides first. Distance only breaks ties between equal-length prefixes.
• Connected 0, static 1, OSPF 110. A static route displaces OSPF and will not fail over unless you make it float.
NEXT
Chapter 16 — Static Routing, IPv4 and IPv6