## Slide 1
CCNA 200-301 V2.0
17
OSPFv2, Single Area
Part III — IP Routing
EXAM TOPICS
3.3
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 17: OSPFv2, Single Area. Blueprint topics: 3.3.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
• Explain how OSPF forms adjacencies and why they sometimes do not.
• Configure single-area OSPFv2 with an explicit router ID, on both broadcast and point-to-point links.
• Predict and influence DR and BDR election.
• Troubleshoot the five mismatches that prevent an adjacency, using show ip ospf neighbor and show ip ospf interface.
Notes: OSPFv2, Single Area 3.3

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Chapter 15 for administrative distance and metrics; Chapter 16 for the contrast with a route you configure by hand.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
OSPF
link-state
adjacency
neighbour
hello
router ID
area 0
DR
BDR
DROTHER
cost
reference bandwidth
wildcard mask
passive interface
FULL state
2-WAY state
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
What the blueprint asks for, precisely
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
This is what the blueprint actually asks for
Topic 3.3 is “configure single area OSPFv2 for IPv4 and OSPFv3 for IPv6” with four sub-points: neighbour adjacencies excluding authentication, point-to-point, broadcast with DR/BDR selection, and router ID. Multi-area OSPF, authentication, virtual links and route summarisation are all out of scope. Learn these four properly rather than the whole protocol thinly.

## Slide 7
What OSPF does that a static route cannot
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 8
CONCEPT
Link state, in three sentences
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Every OSPF router floods a description of its own links to every other router in the area. Each router therefore ends up with an identical map of the whole area, which it stores in a link-state database. Each then runs the shortest-path algorithm against that map to work out its own best route to everywhere.
Because every router has the whole map, a failure anywhere is known everywhere within seconds, and every router recalculates independently and consistently. That is the property a static route can never have.

## Slide 9
What OSPF does that a static route cannot
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Link state in one picture. The database is shared and identical; the routing table each router builds from it is its own.

## Slide 10
DEFINITION
Router ID, and how it is chosen
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
The router ID is a 32-bit value written like an IP address that uniquely identifies the router in OSPF. It is selected in this order:
• The value configured with router-id — always use this.
• Otherwise, the highest IP address on any loopback interface.
• Otherwise, the highest IP address on any active physical interface.
Left to itself the ID can change when an interface goes down, which forces the adjacency to rebuild. Configure it explicitly and the problem disappears.
Notes: Two routers become neighbours by exchanging hello packets on a shared link. The hello carries several parameters, and if any of them disagree, no adjacency forms — silently. Two further conditions are worth adding because they cause the same symptom: the router IDs must be unique, and the interface must not be passive.

## Slide 11
Configuring single-area OSPFv2
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 12
CONFIGURE
OSPF on R1, area 0
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
IOS · configuration mode
! A loopback gives a stable ID and a pingable address that never
! goes down with a physical interface.
interface Loopback0
ip address 1.1.1.1 255.255.255.255
!
router ospf 10
! The process number is LOCAL. R2 may use a different one and
! the two will still peer -- unlike EIGRP or BGP.
router-id 1.1.1.1
!
! The network statement uses a WILDCARD mask -- the inverse of a
! subnet mask. It means "enable OSPF on any interface whose
! address falls in this range, and advertise that subnet".
network 10.255.0.0 0.0.0.3 area 0
network 192.168.10.0 0.0.0.255 area 0
!
! Do not send hellos out of a LAN with no other routers on it.
! It saves bandwidth and removes an attack surface, while the
! subnet is still advertised.
passive-interface Vlan10
!

## Slide 13
CONFIGURE
OSPF on R1, area 0 (continued)
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
IOS · configuration mode
! Make cost reflect modern link speeds -- see the note below.
auto-cost reference-bandwidth 10000

## Slide 14
CONCEPT
Wildcard masks, quickly
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
A wildcard mask is the subnet mask with every bit inverted: 0 means “this bit must match”, 255 means “do not care”.
• /24 → mask 255.255.255.0 → wildcard 0.0.0.255
• /30 → mask 255.255.255.252 → wildcard 0.0.0.3
• A single interface → wildcard 0.0.0.0
The arithmetic is 255 minus each octet of the subnet mask. Wildcards return in Chapter 24.

## Slide 15
WATCH OUT
Reference bandwidth: change it everywhere or nowhere
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
OSPF cost is textreference bandwidth div textinterface bandwidth, and the default reference is 100 Mbps. That means a 1 Gbps link and a 10 Gbps link both come out at cost 1 — OSPF cannot tell them apart, and will happily choose the slower one.
Raising the reference to 10000 (10 Gbps) restores the distinction. But cost is compared across the area, so every router must use the same reference bandwidth or the path calculations disagree and traffic takes strange routes. Change it on all of them, or on none.

## Slide 16
DR and BDR on broadcast links
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 17
CONCEPT
Why a designated router exists
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
On a broadcast segment with n routers, full adjacencies between every pair would be n(n-1)/2 relationships — ten routers would need forty-five. Instead one router is elected DR and one BDR, and everyone else becomes a DROTHER adjacent only to those two. Flooding goes through the DR.
The election: highest OSPF interface priority wins; if priorities tie, highest router ID wins. Default priority is 1. Priority 0 means “never be DR”.
Two things surprise people. The election is per segment, not per router — a router can be DR on one link and DROTHER on another. And it is non-preemptive: a new router with a better priority does not take over until the current DR fails. To force it, clear the process or bounce the interface.

## Slide 18
CONFIGURE
Influencing the election, and avoiding it
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
IOS · configuration mode
! Make this router the DR on the segment.
interface GigabitEthernet0/0
ip ospf priority 255
!
! Never allow this one to be DR or BDR.
interface GigabitEthernet0/1
ip ospf priority 0
!
! On a link with exactly two routers, skip the election entirely.
! Point-to-point forms an adjacency faster and elects nobody.
interface GigabitEthernet0/2
ip ospf network point-to-point

## Slide 19
Verifying
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 20
VERIFY
show ip ospf neighbor
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
R1#
Neighbor ID Pri State Dead Time Address Interface
2.2.2.2 1 FULL/DR 00:00:33 10.255.0.2 GigabitEthernet0/1
3.3.3.3 1 FULL/BDR 00:00:31 10.255.0.3 GigabitEthernet0/1
4.4.4.4 0 FULL/ - 00:00:38 10.255.1.2 GigabitEthernet0/2

## Slide 21
VERIFY
show ip ospf interface GigabitEthernet0/1
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
R1#
GigabitEthernet0/1 is up, line protocol is up
Internet Address 10.255.0.1/30, Area 0, Attached via Network Statement
Process ID 10, Router ID 1.1.1.1, Network Type BROADCAST, Cost: 10
Designated Router (ID) 2.2.2.2, Interface address 10.255.0.2
Backup Designated router (ID) 3.3.3.3, Interface address 10.255.0.3
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
Neighbor Count is 2, Adjacent neighbor count is 2

## Slide 22
COMMON PITFALLS · Verifying
Common pitfalls
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
• Assuming the process number must match. It is locally significant. router ospf 10 peers happily with router ospf 65.
• Using a subnet mask in the network statement. It takes a wildcard. network 10.255.0.0 255.255.255.252 does not do what you expect.
• Leaving the router ID to chance. It changes when interfaces change, and every adjacency rebuilds.
• Panicking at 2-WAY. Between two DROTHERs it is correct.
• Changing reference bandwidth on one router. See the warning above.
Notes: This one output carries four of the five things that must match: area, network type, hello and dead intervals, and the subnet. When an adjacency will not form, run it on both routers and compare line by line.

## Slide 23
COMMON PITFALLS · Verifying
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
• Forgetting passive-interface on user VLANs. Hellos on a LAN full of PCs are wasted and expose the protocol.

## Slide 24
BREAK & FIX · SYMPTOM
Chapter 17
Adjacency stuck in EXSTART.
Two routers see each other but never reach FULL:
Hellos are being exchanged — so area, timers, subnet and network type all match, or the neighbour would not be listed at all. The failure is later, during database exchange.
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 25
BREAK & FIX · YOUR MOVE
Chapter 17
Adjacency stuck in EXSTART.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 26
BREAK & FIX · EVIDENCE
Chapter 17
show ip ospf neighbor
R1#
Neighbor ID Pri State Dead Time Address Interface
2.2.2.2 1 EXSTART/DR 00:00:35 10.255.0.2 GigabitEthernet0/1
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 27
BREAK & FIX · EVIDENCE
Chapter 17
show ip ospf interface GigabitEthernet0/1 | include MTU|Internet
R1#
Internet Address 10.255.0.1/30, Area 0, Attached via Network Statement
MTU is 1500 bytes
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 28
BREAK & FIX · EVIDENCE
Chapter 17
show ip ospf interface GigabitEthernet0/1 | include MTU|Internet
R2#
Internet Address 10.255.0.2/30, Area 0, Attached via Network Statement
MTU is 1400 bytes
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 29
BREAK & FIX · YOUR MOVE
Chapter 17
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Notes: The elimination matters as much as the answer.

## Slide 30
BREAK & FIX · DIAGNOSIS
Chapter 17
Why it is doing that
Diagnosis. An MTU mismatch. OSPF checks MTU during database description exchange and refuses to proceed if the two ends disagree — which is exactly why the adjacency reaches EXSTART and stops there. Being stuck in EXSTART or EXCHANGE is close to diagnostic of this.
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 31
BREAK & FIX · THE FIX
Chapter 17
And the lesson
Fix. Make the MTUs match: ip mtu 1500 on R2’s interface, or 1400 on R1’s if the smaller value was deliberate. The adjacency will move to FULL within a dead interval. Do not use ip ospf mtu-ignore except as a temporary measure — it suppresses the symptom and leaves a real MTU mismatch to fragment traffic later.
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3

## Slide 32
LAB · PACKET TRACER
Three routers, one area
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Topology. R1, R2, R3 on a shared Ethernet segment; each with a LAN; R1 also point-to-point to R3.
1. Configure loopbacks and explicit router IDs 1.1.1.1, 2.2.2.2, 3.3.3.3. Enable OSPF area 0 on all links and LANs, with LANs passive.
2. Confirm every neighbour reaches FULL. Record which router became DR and which BDR, and explain the election from the router IDs.
3. Set ip ospf priority 255 on R3’s segment interface. Note that nothing changes, then bounce the interfaces and note that it does. Explain why.
4. On the R1–R3 link, set ip ospf network point-to-point at both ends. Confirm the state becomes FULL/ - with no DR.

## Slide 33
LAB · PACKET TRACER
Three routers, one area (continued)
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
5. Change the hello interval on R1 only. Watch the adjacency drop, and find the mismatch with show ip ospf interface.
6. Set ip mtu 1400 on one end and reproduce the EXSTART fault above.
7. Extension. Raise the reference bandwidth on one router only and observe the asymmetric routing that results.

## Slide 34
CHECKPOINT 1 of 3
Two routers on a broadcast segment show 2-WAY and never go FULL. Under what circumstance is this correct rather than a fault?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 35
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Two routers on a broadcast segment show 2-WAY and never go FULL. Under what circumstance is this correct rather than a fault?
When both routers are DROTHERs. Two non-designated routers on a broadcast segment deliberately stop at 2-WAY — they exchange databases with the DR and BDR, not with each other. It is a fault only if one of them should have been the DR or BDR.

## Slide 36
CHECKPOINT 2 of 3
Which wildcard mask enables OSPF on 172.16.8.0/22?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 37
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
Which wildcard mask enables OSPF on 172.16.8.0/22?
0.0.3.255. The mask for /22 is 255.255.252.0, and 255-252 = 3.

## Slide 38
CHECKPOINT 3 of 3
A router’s OSPF adjacencies all rebuild every time one interface flaps. What is the cause, and what is the one-line fix?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 39
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
A router’s OSPF adjacencies all rebuild every time one interface flaps. What is the cause, and what is the one-line fix?
The router ID was derived from that interface’s address, so when the interface flaps the router ID changes and every adjacency rebuilds. Fix it with an explicit router-id, or a loopback, which never flaps.

## Slide 40
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 17. OSPFv2, Single Area
3.3
• OSPF floods a description of every link, so all routers in the area share one map and converge consistently.
• Area, hello and dead timers, subnet and mask, and network type must all match, or no adjacency forms. Router IDs must be unique.
• Configure the router ID explicitly; otherwise it moves and adjacencies rebuild.
• Network statements take wildcard masks. The process number is local.
• DR and BDR are elected per segment by priority then router ID, and the election is non-preemptive. ip ospf network point-to-point avoids it entirely on two-router links.
• FULL is healthy; 2-WAY between DROTHERs is healthy; stuck in EXSTART means MTU.

## Slide 41
Where we got to
• OSPF floods a description of every link, so all routers in the area share one map and converge consistently.
• Area, hello and dead timers, subnet and mask, and network type must all match, or no adjacency forms. Router IDs must be unique.
• Configure the router ID explicitly; otherwise it moves and adjacencies rebuild.
• Network statements take wildcard masks. The process number is local.
NEXT
Chapter 18 — OSPFv3 for IPv6