## Slide 1
CCNA 200-301 V2.0
18
OSPFv3 for IPv6
Part III — IP Routing
EXAM TOPICS
3.3
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 18: OSPFv3 for IPv6. Blueprint topics: 3.3.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
• State what OSPFv3 keeps from OSPFv2 and what it changes.
• Configure single-area OSPFv3 on interfaces rather than with network statements.
• Explain why an IPv6-only router still needs an IPv4-format router ID, and configure one.
• Troubleshoot an OSPFv3 adjacency, including the failure unique to it: a missing router ID.
Notes: OSPFv3 for IPv6 3.3

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Chapter 17 — this chapter assumes it and covers only the differences. Chapter 5 for link-local addressing.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
OSPFv3
router ID
link-local next hop
per-interface configuration
address family
ff02::5
ff02::6
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
One topic, two protocols
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
This is what the blueprint actually asks for
Topic 3.3 covers OSPFv2 and OSPFv3 together, and OSPFv3 is new in v2.0 — it was not in the v1.1 blueprint at all. The exam will not ask you to re-learn OSPF; it will ask whether you can configure the v6 version, which means knowing the handful of things that differ.

## Slide 7
WATCH OUT
The failure unique to OSPFv3
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
The router ID is still a 32-bit value written like an IPv4 address, even in a network with no IPv4 at all. If the router has no IPv4 address on any interface and you have not configured router-id, the process will not start. IOS says so, but the message is easily missed in a long paste:
% OSPFv3-1-IPV6 Router process 10 could not pick a router-id, please configure manually
Always configure it explicitly. It costs one line and removes the whole class of problem.
Notes: Almost everything conceptual. The link-state mechanism, the database, the shortest-path calculation, areas, the DR and BDR election with its priority-then- router-ID tie-break, the FULL and 2-WAY states, cost as the metric, hello and dead intervals that must match, and the administrative distance of 110 are all identical to Chapter 17. So is the troubleshooting. If an OSPFv3 adjacency will not form, the causes are the same list: area, timers, network type, MTU, duplicate router ID.

## Slide 8
Configuring it
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 9
CONFIGURE
Single-area OSPFv3 on R1
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
IOS · configuration mode
ipv6 unicast-routing
!
! The process exists mainly to hold the router ID; interfaces do
! the rest of the work.
ipv6 router ospf 10
router-id 1.1.1.1
passive-interface Vlan10
!
! Enable per interface. Every IPv6 prefix on the interface is
! advertised -- there is no network statement and no wildcard mask.
interface GigabitEthernet0/1
description Link to R2
ipv6 address 2001:db8:acad:99::1/64
ipv6 ospf 10 area 0
!
interface Vlan10
ipv6 address 2001:db8:acad:10::1/64
ipv6 ospf 10 area 0
!

## Slide 10
CONFIGURE
Single-area OSPFv3 on R1 (continued)
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
IOS · configuration mode
! Point-to-point on a two-router link, exactly as in OSPFv2.
interface GigabitEthernet0/2
ipv6 ospf network point-to-point

## Slide 11
CONCEPT
No network statements is a simplification, not a trap
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
In OSPFv2 you had to compute a wildcard mask and remember that the statement both enables the interface and advertises the subnet. OSPFv3 drops all of that: enable the interface and every prefix on it is advertised, including additional addresses added later.
The practical consequence is that passive-interface becomes more important, not less — it is now the only way to advertise a LAN’s prefix without sending hellos into it.

## Slide 12
Verifying
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 13
VERIFY
show ipv6 ospf neighbor
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
R1#
OSPFv3 Router with ID (1.1.1.1) (Process ID 10)
Neighbor ID Pri State Dead Time Interface ID Interface
2.2.2.2 1 FULL/BDR 00:00:31 4 GigabitEthernet0/1
3.3.3.3 1 FULL/DR 00:00:35 4 GigabitEthernet0/1

## Slide 14
VERIFY
show ipv6 route ospf
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
R1#
IPv6 Routing Table - default - 9 entries
Codes: C - Connected, L - Local, S - Static, O - OSPF intra, OI - OSPF inter
O 2001:DB8:ACAD:20::/64 [110/2]
via FE80::2, GigabitEthernet0/1
O 2001:DB8:ACAD:30::/64 [110/3]
via FE80::3, GigabitEthernet0/1
Notes: The neighbour IDs are still IPv4-format. The column that replaces the IPv4 address is Interface ID — the neighbour’s own index for its interface, which matters only when reading the database.

## Slide 15
WATCH OUT
The next hop is a link-local address, and that is correct
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Every OSPFv3 route resolves to a fe80:: next hop plus an interface. This looks wrong to anyone used to IPv4 and is not: link-local addresses are guaranteed to exist on every IPv6 interface and cannot be renumbered, so they are the stable choice. This is also why the interface must always be named alongside them (Chapter 16).

## Slide 16
VERIFY
show ipv6 ospf interface brief
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
R1#
Interface PID Area Intf ID Cost State Nbrs F/C
Gi0/1 10 0 4 1 BDR 2/2
Gi0/2 10 0 5 1 P2P 1/1
Vl10 10 0 8 1 DR 0/0

## Slide 17
COMMON PITFALLS · Verifying
Common pitfalls
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
• No router ID on an IPv6-only router. The process will not start. This is the single most common OSPFv3 fault.
• Looking for network statements. There are none; enable the interface.
• Forgetting ipv6 unicast-routing. As ever. Interfaces come up, OSPFv3 forms adjacencies, and nothing is forwarded.
• Expecting a global next hop in the routing table. Link-local is correct.
• Assuming OSPFv2 and OSPFv3 share anything at runtime. They are separate processes with separate databases and separate neighbours. A working v2 adjacency tells you nothing about v3 on the same link.

## Slide 18
BREAK & FIX · SYMPTOM
Chapter 18
OSPFv3 configured on both routers; no neighbours at all.
R1 and R2 both have IPv6 addresses on the link, ping each other’s link-local addresses successfully, and have identical-looking OSPFv3 configuration. show ipv6 ospf neighbor is empty on both.
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 19
BREAK & FIX · YOUR MOVE
Chapter 18
OSPFv3 configured on both routers; no neighbours at all.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 20
BREAK & FIX · EVIDENCE
Chapter 18
show ipv6 ospf
R1#
%OSPFv3: Router process 10 is not running, please configure a router-id
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 18
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Notes: The elimination matters as much as the answer.

## Slide 22
BREAK & FIX · DIAGNOSIS
Chapter 18
Why it is doing that
Diagnosis. Neither router has any IPv4 address anywhere — this is an IPv6-only lab — so neither could derive a 32-bit router ID, and the process never started. The interface commands were accepted and are sitting in the configuration doing nothing, which is why the configuration looks right.
The tell is that both ends are empty. A mismatch of area, timers or MTU usually leaves at least one side reporting something.
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 23
BREAK & FIX · THE FIX
Chapter 18
Starting the process
IOS · configuration mode
ipv6 router ospf 10
router-id 1.1.1.1
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 24
BREAK & FIX · THE FIX
Chapter 18
And the lesson
Fix. Configure a router ID on each router explicitly:
The process starts immediately and adjacencies form within a hello interval. Configure a distinct ID on R2 — duplicate router IDs are the next fault along, and they produce a flapping adjacency rather than none.
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3

## Slide 25
LAB · PACKET TRACER
Dual-stack routing, both protocols side by side
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Topology. The three-router topology from Chapter 17, now addressed for IPv4 and IPv6 simultaneously.
1. Keep the working OSPFv2 configuration. Add IPv6 addresses to every link and LAN, and ipv6 unicast-routing everywhere.
2. Configure OSPFv3 with explicit router IDs matching the v2 ones. Enable it per interface, LANs passive.
3. Confirm show ipv6 ospf neighbor reaches FULL on every link, and that the DR and BDR are the same routers as for OSPFv2. Explain why they need not have been.
4. Compare show ip route ospf with show ipv6 route ospf. Note that v4 next hops are global and v6 next hops are link-local.

## Slide 26
LAB · PACKET TRACER
Dual-stack routing, both protocols side by side (continued)
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
5. Remove the router ID from one router and clear the process. Reproduce the “process not running” fault, then fix it.
6. Set one link to ipv6 ospf network point-to-point at one end only and observe the result.
7. Extension. Shut a link and time how long each protocol takes to reconverge. They should be comparable — the algorithm is the same.

## Slide 27
CHECKPOINT 1 of 3
Why does an IPv6-only router still need a router ID in IPv4 format, and what happens if it cannot get one?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 28
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Why does an IPv6-only router still need a router ID in IPv4 format, and what happens if it cannot get one?
Because the router ID is a 32-bit value written in IPv4 format regardless of the address family, and it is normally derived from an IPv4 address on the device. With no IPv4 anywhere, none can be derived, and the process will not start at all — the interface commands are accepted and do nothing.

## Slide 29
CHECKPOINT 2 of 3
OSPFv2 works on a link and OSPFv3 does not. What does the working v2 adjacency prove about the v3 problem?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
OSPFv2 works on a link and OSPFv3 does not. What does the working v2 adjacency prove about the v3 problem?
Nothing. They are separate processes with separate databases, neighbours and adjacencies. A working v2 adjacency proves the link and layer 2 are fine, which is useful, but says nothing about v3’s configuration.

## Slide 31
CHECKPOINT 3 of 3
Where is OSPFv3 enabled, and what is advertised as a result?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 32
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
Where is OSPFv3 enabled, and what is advertised as a result?
Per interface, with ipv6 ospf <pid> area <n>. Every IPv6 prefix on that interface is advertised — there are no network statements and no wildcard masks, which is why passive-interface matters more in OSPFv3 than in OSPFv2.

## Slide 33
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 18. OSPFv3 for IPv6
3.3
• OSPFv3 is OSPF. The database, the algorithm, the states, the DR election and the troubleshooting are unchanged.
• It is enabled per interface with ipv6 ospf <pid> area <n>, and every prefix on that interface is advertised. No network statements, no wildcards.
• Neighbours are reached by link-local address, so routes show a fe80:: next hop plus an interface. That is correct.
• The router ID is still 32-bit IPv4 format and must be configured on an IPv6-only router, or the process will not start.
• v2 and v3 are independent processes. One working says nothing about the other.

## Slide 34
Where we got to
• OSPFv3 is OSPF. The database, the algorithm, the states, the DR election and the troubleshooting are unchanged.
• It is enabled per interface with ipv6 ospf <pid> area <n>, and every prefix on that interface is advertised. No network statements, no wildcards.
• Neighbours are reached by link-local address, so routes show a fe80:: next hop plus an interface. That is correct.
• The router ID is still 32-bit IPv4 format and must be configured on an IPv6-only router, or the process will not start.
NEXT
Chapter 19 — First Hop Redundancy: HSRP and VRRP