## Slide 1
CCNA 200-301 V2.0
19
First Hop Redundancy: HSRP and VRRP
Part III — IP Routing
EXAM TOPICS
3.4
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 19: First Hop Redundancy: HSRP and VRRP. Blueprint topics: 3.4.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
• Explain the problem a first hop redundancy protocol solves, and why routing protocols do not solve it.
• Interpret the operational status of HSRP and VRRP — which the blueprint asks for by name.
• Configure basic HSRP and VRRP with priority and preemption.
• Diagnose the two classic faults: both routers active, and a gateway that fails over but does not fail back.
Notes: First Hop Redundancy: HSRP and VRRP 3.4

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Chapter 15 for gateways; Chapter 10 for SVIs, which is where these protocols usually live.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
first hop redundancy
virtual IP
virtual MAC
HSRP
VRRP
active
standby
master
backup
priority
preemption
group number
tracking
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
The verb is interpret, not configure
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
This is what the blueprint actually asks for
Topic 3.4 is “interpret the operational status of First Hop Redundancy Protocols (HSRP and VRRP)”. You are far more likely to be shown show standby brief and asked which router is forwarding, or why a failover did not happen, than to be asked to configure it from scratch. Configuration is here because you cannot interpret what you have never built — but read the verification sections hardest.

## Slide 7
The problem
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 8
CONCEPT
The solution: a gateway address that is not tied to a router
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Two routers share a virtual IP address and a virtual MAC address. Hosts are configured with the virtual IP as their gateway and never know that two routers exist. One router is elected to answer for it; the other waits.
When the active router fails, the standby takes over both the virtual IP and the virtual MAC. Because the MAC does not change, the hosts’ ARP caches stay valid and no host has to do anything at all. That is the whole trick, and it is why the virtual MAC matters as much as the virtual IP.
Notes: Every host is configured with one default gateway address. If the router holding that address fails, every host on the subnet is cut off — and no routing protocol helps, because the hosts are not running one. They have a single static address and no way to learn a new one quickly.

## Slide 9
The problem
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
The host is configured once and never reconfigured. Failover moves the virtual IP and the virtual MAC, which is why nothing on the LAN has to re-learn anything.

## Slide 10
WATCH OUT
The preemption default is the difference that catches people
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
HSRP does not preempt by default. Configure a router with priority 150, reload it, and when it comes back the other router — priority 100 — keeps the active role. Your carefully planned primary is now the standby, and everything still works, so nobody notices until the second failure.
VRRP preempts by default, so it behaves the way most people expect.
If you want a specific router to be primary, configure standby 10 preempt explicitly. This is the single most commonly missed HSRP command.

## Slide 11
Configuring HSRP
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 12
CONFIGURE
HSRP on two multilayer switches, VLAN 10
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
IOS · configuration mode
! ---------- CORE1: the intended primary ----------
interface Vlan10
ip address 192.168.10.2 255.255.255.0
! The virtual IP -- this is what hosts use as their gateway.
standby 10 ip 192.168.10.1
! Higher priority wins the election.
standby 10 priority 150
! Without this, CORE1 will NOT take the role back after a reload.
standby 10 preempt
! Give up the role if the uplink dies -- otherwise CORE1 stays
! active while having no path to anywhere.
standby 10 track GigabitEthernet0/24 60
standby 10 name VLAN10-GW
!
! ---------- CORE2: the standby ----------
interface Vlan10
ip address 192.168.10.3 255.255.255.0
standby 10 ip 192.168.10.1
standby 10 priority 100
standby 10 preempt

## Slide 13
CONCEPT
Tracking, and why it is not optional
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Without tracking, the active router keeps the role as long as its own VLAN interface is up. If its uplink fails, it is still active, still answering for the gateway, and has nowhere to send the traffic — a black hole that the standby router cannot detect, because from its point of view the active router is perfectly healthy.
standby 10 track Gi0/24 60 decrements the priority by 60 when that interface goes down: 150 becomes 90, which is below CORE2’s 100, so CORE2 preempts and takes over. The decrement must be large enough to cross the gap between the two priorities, or nothing happens.

## Slide 14
Interpreting the status
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 15
VERIFY
show standby brief
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
CORE1#
P indicates configured to preempt.
|
Interface Grp Pri P State Active Standby Virtual IP
Vl10 10 150 P Active local 192.168.10.3 192.168.10.1
Vl20 20 100 P Standby 192.168.10.3 local 192.168.20.1

## Slide 16
VERIFY
show standby Vlan10
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
CORE1#
Vlan10 - Group 10
State is Active
2 state changes, last state change 04:12:19
Virtual IP address is 192.168.10.1
Active virtual MAC address is 0000.0c07.ac0a
Local virtual MAC address is 0000.0c07.ac0a (v1 default)
Hello time 3 sec, hold time 10 sec
Preemption enabled
Active router is local
Standby router is 192.168.10.3, priority 100 (expires in 8.048 sec)
Priority 150 (configured 150)
Track interface GigabitEthernet0/24 state Up decrement 60
Notes: Read it column by column. Pri is this router’s priority. P means preemption is configured — its absence is the fault described above. State is the role. Active and Standby name who holds each role, where local means this router. Note that VLAN 10 and VLAN 20 have opposite roles here. That is deliberate load sharing: half the VLANs are active on each core switch, so both boxes carry traffic instead of one sitting idle.

## Slide 17
VERIFY
show vrrp brief
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
CORE1#
Interface Grp Pri Time Own Pre State Master addr Group addr
Vl30 30 110 3570 Y Y Master 192.168.30.2 192.168.30.1
Notes: Two lines to check first: Priority 150 (configured 150) — if the two numbers differ, a tracked interface is down and has decremented it — and Preemption enabled.

## Slide 18
COMMON PITFALLS · Interpreting the status
Common pitfalls
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
• Forgetting preempt on HSRP. The intended primary never takes the role back.
• Mismatched group numbers. Two routers with different group numbers on the same VLAN both become active, each for its own group. The symptom is intermittent connectivity as hosts ARP for a virtual IP that two devices answer.
• Mismatched virtual IPs. Same result.
• A track decrement too small to matter. 150 with a decrement of 10 still beats 100. Size the decrement against the gap.
• Configuring the virtual IP as a router’s real address in HSRP. Not allowed. VRRP permits it; HSRP does not.

## Slide 19
COMMON PITFALLS · Interpreting the status
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
• Assuming the gateway works because the routers are up. Test by pinging the virtual address from a host, then failing the active router and pinging again.

## Slide 20
BREAK & FIX · SYMPTOM
Chapter 19
Both routers say they are active.
Users on VLAN 10 report intermittent loss. Both core switches report the active role for group 10.
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 19
Both routers say they are active.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 22
BREAK & FIX · EVIDENCE
Chapter 19
show standby brief
CORE1#
Interface Grp Pri P State Active Standby Virtual IP
Vl10 10 150 P Active local unknown 192.168.10.1
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 23
BREAK & FIX · EVIDENCE
Chapter 19
show standby brief
CORE2#
Interface Grp Pri P State Active Standby Virtual IP
Vl10 11 100 P Active local unknown 192.168.10.1
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 24
BREAK & FIX · YOUR MOVE
Chapter 19
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Notes: The elimination matters as much as the answer.

## Slide 25
BREAK & FIX · DIAGNOSIS
Chapter 19
Why it is doing that
Diagnosis. Look at the Grp column: CORE1 is in group 10, CORE2 in group 11. They are not peers at all — they are two independent HSRP groups that happen to share a virtual IP address. Each sees no partner, so each elects itself active, and each answers ARP for 192.168.10.1 with a different virtual MAC (0000.0c07.ac0a against 0000.0c07.ac0b). Hosts get whichever reply arrives first, and traffic splits unpredictably between two routers.
The giveaway is Standby unknown on both sides. A healthy pair always names its partner.
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 26
BREAK & FIX · THE FIX
Chapter 19
And the lesson
Fix. Correct the group number on CORE2 to 10. Within a hello interval the two will see each other, the priorities decide, and one becomes standby. Confirm that each side names the other in the Standby column, and that only one virtual MAC is now in use.
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4

## Slide 27
LAB · PACKET TRACER
Fail a gateway and watch it survive
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Topology. Two multilayer switches as redundant gateways for VLANs 10 and 20; an access switch; two PCs.
1. Address both cores in VLAN 10 and configure HSRP group 10 with virtual IP 192.168.10.1, CORE1 at priority 150 with preempt.
2. Point the PCs at the virtual IP and confirm they can reach the rest of the network. Record the ARP entry a PC holds for its gateway — note the virtual MAC.
3. Run show standby brief on both. Identify active, standby and the preempt flag.
4. Start a continuous ping from a PC, then shut CORE1’s VLAN 10 interface. Count how many pings are lost and confirm the PC’s ARP entry has not changed.
5. Bring CORE1 back and confirm it resumes the active role. Then remove preempt, repeat, and observe that it does not.

## Slide 28
LAB · PACKET TRACER
Fail a gateway and watch it survive (continued)
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
6. Configure tracking on CORE1’s uplink with a decrement of 60. Shut the uplink and confirm failover; use a decrement of 10 instead and confirm it does not.
7. Configure VLAN 20 with CORE2 as primary, so the two share the load.
8. Extension. Repeat the first four steps with VRRP on a third VLAN and note the difference in default preemption behaviour.

## Slide 29
CHECKPOINT 1 of 3
Why does a host not need to update its ARP cache when the active router fails?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
Why does a host not need to update its ARP cache when the active router fails?
Because the virtual MAC address moves with the virtual IP. The host’s ARP cache still maps the gateway IP to the same MAC; the new active router simply starts answering to it. The host never learns anything happened, which is the entire point.

## Slide 31
CHECKPOINT 2 of 3
show standby brief shows Standby unknown on both routers. What does that indicate?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 32
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
show standby brief shows Standby unknown on both routers. What does that indicate?
That the two routers are not seeing each other’s hellos — so each believes it is alone. Causes: mismatched group numbers, different subnets, a VLAN or trunk fault between them, or an ACL blocking the multicast. Both then claim active, and two devices answer for the same IP.

## Slide 33
CHECKPOINT 3 of 3
A router is configured with priority 150 and a tracked interface with decrement 10. Its peer is at 100. The tracked interface fails. What happens, and is it what was intended?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 34
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
A router is configured with priority 150 and a tracked interface with decrement 10. Its peer is at 100. The tracked interface fails. What happens, and is it what was intended?
The priority drops to 140, which is still above the peer’s 100, so nothing happens — the router keeps the active role despite having lost the tracked interface. That is almost certainly not what was intended: the decrement must be large enough to take the priority below the peer’s, so 51 or more.

## Slide 35
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 19. First Hop Redundancy: HSRP and VRRP
3.4
• Hosts have one static gateway address, so redundancy has to be provided below them: two routers share a virtual IP and a virtual MAC.
• HSRP is Cisco, uses active and standby, and does not preempt by default. VRRP is standard, uses master and backup, and does.
• Priority decides; preemption decides whether the better router takes the role back.
• Track the uplink, with a decrement large enough to cross the priority gap, or the active router can become a black hole.
• Interpret show standby brief by columns: priority, the P flag, state, and who is named as partner. Standby unknown means the two are not peering.

## Slide 36
Where we got to
• Hosts have one static gateway address, so redundancy has to be provided below them: two routers share a virtual IP and a virtual MAC.
• HSRP is Cisco, uses active and standby, and does not preempt by default. VRRP is standard, uses master and backup, and does.
• Priority decides; preemption decides whether the better router takes the role back.
• Track the uplink, with a decrement large enough to cross the priority gap, or the active router can become a black hole.
NEXT
Chapter 20 — DHCP: Client, Server and Relay