## Slide 1
CCNA 200-301 V2.0
32
AI in Network Operations
Part V — Wireless, Virtualisation and Operations
EXAM TOPICS
5.1
5.2
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 32: AI in Network Operations. Blueprint topics: 5.1, 5.2.

## Slide 2
THE COURSE
Where this chapter sits
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Part I
Foundations
chapters 1–7
Part II
Switching and Network Access
chapters 8–14
Part III
IP Routing
chapters 15–19
Part IV
Network Services and Security
chapters 20–26
Part V
Wireless, Virtualisation and Operations
chapters 27–32
Part VI
Sitting the Exam
chapters 33–34
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Notes: Ten seconds. Students meeting a chapter in week ten cannot place it without being shown.

## Slide 3
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Distinguish generative AI from agentic AI, and describe what makes a system agentic.
• Describe where AI is genuinely used in network operations, and where it should not be trusted.
• Select an effective prompt, using the four components the blueprint names: data classification, output format, persona and instructions.
• Judge what data may safely be sent to an AI system, and sanitise what may not.
Notes: AI in Network Operations 5.15.2

## Slide 4
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Chapter 30 for the five management approaches — agentic systems sit on top of them, not instead of them. Chapter 31 for automation, which is what an agent actually uses to act. Chapter 23 for why credentials must not leave the organisation.

## Slide 5
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
generative AI
agentic AI
autonomy
tool use
human in the loop
prompt
persona
data classification
sanitisation
hallucination
blast radius
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 6
ON THE EXAM
Two topics, and the second one is unusual
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
This is what the blueprint actually asks for
5.1 is describe the role of agentic AI in network operations.
5.2 is select a prompt to send to a generative AI system to support network operations considering prompt components such as data classification, output format, persona, and instructions.
Read 5.2 carefully, because it tells you the question format. Select means you will be shown several candidate prompts and asked which is best — not asked to write one. And the four components are named, which means the marking scheme is those four. A prompt that has all four beats one that does not.
Note the order Cisco lists them in: data classification comes first. That is not accidental, and Section sec:dataclass explains why.

## Slide 7
Generative and agentic
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2

## Slide 8
DEFINITION
Generative AI
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
A system that produces content — text, code, configuration — in response to a prompt. It answers and stops. Every action taken as a result is taken by you.

## Slide 9
DEFINITION
Agentic AI
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
A system that pursues a goal rather than answering a question. It perceives the current state, plans, uses tools to act, observes the result, and iterates — choosing the intermediate steps itself.

## Slide 10
Generative and agentic
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
The difference is the loop and who closes it. A generative system hands you an answer; an agentic one acts and checks its own work.

## Slide 11
WATCH OUT
The one-sentence answer for the exam
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Generative AI produces content; agentic AI takes action toward a goal, using tools, and evaluates its own results. Autonomy and tool use are the two words that separate them.

## Slide 12
Where it is actually used
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2

## Slide 13
CONCEPT
Blast radius is the design question
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Before granting autonomy, ask what the worst outcome is if the system is confidently wrong. Clearing one err-disabled port has a blast radius of one port. Changing a route map on a core router has a blast radius of the organisation.
The same technology can sit at different rungs for different actions, and a well-designed deployment does exactly that. “Human in the loop” is not a blanket policy; it is a decision made per action, based on reversibility and reach.
Notes: The useful question about an agentic system is not “is it intelligent” but how much is it allowed to do without asking. Recommend. It tells you what it would do. You do it. No risk beyond a wasted suggestion. Approve then act. It prepares the change and waits for a human to approve. This is where most production deployments sit, and sensibly. Act then report. It makes the change and tells you afterwards. Appropriate for narrow, reversible, well-understood actions — clearing an err-disabled port, restarting a stuck process. Fully autonomous. It acts within a defined scope with no notification. Appropriate for very little in a production network.

## Slide 14
WATCH OUT
What these systems are bad at, and you must know
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Being confidently wrong. A fluent, plausible, incorrect answer is the characteristic failure. It does not signal uncertainty the way a colleague would.
• Your network specifically. Training data is the internet, not your topology. It does not know that VLAN 40 is the guest network here.
• Currency. It may recommend commands deprecated years ago, or miss ones added last year.
• Accountability. When a change breaks a site, a person is answerable. Change control, approval and rollback do not become optional because a machine proposed the change.

## Slide 15
Selecting a prompt
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2

## Slide 16
WORKED EXAMPLE
The same question, asked twice
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Weak:
Why is my DHCP not working? Here is my config: [entire running configuration pasted, including snmp-server community, username ... secret and the site’s public addressing]
No persona, no output format, no scope — and it has just sent credentials and the organisation’s real addressing to a third party. Even a good answer would not justify that.
Strong:
You are a senior network engineer working on Cisco IOS XE 17.12.
Clients in VLAN 30 receive APIPA addresses. VLANs 10 and 20 on the same distribution switch lease correctly. The DHCP server is central and reached across a routed core. Relevant configuration, with addresses substituted:
interface Vlan30 / ip address 10.30.0.1 255.255.255.0
List the three most likely causes, most likely first. For each give the single show command that would confirm or eliminate it. Reply as a table with columns Cause, Confirming command, Expected output if this is the fault. Do not propose configuration changes.
All four components are present, and each earns its place: the persona sets the platform, the classification decided that addresses would be substituted and credentials omitted, the instructions bound the scope, and the format makes the answer directly actionable.
Notes: This is topic 5.2, and it is a practical skill with four named parts.

## Slide 17
ON THE EXAM
How to answer a “select the best prompt” question
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
This is what the blueprint actually asks for
Score each candidate against the four components and pick the one with most. Then apply three tie-breakers:
• Eliminate anything containing credentials, keys or real public addressing immediately, however good the rest of it is. Data classification is listed first for a reason and a prompt that leaks is wrong regardless of its other qualities.
• Prefer specific over polite. “Please help me with my network” scores nothing. Length is not the measure — specificity is.
• Prefer a stated output format. It is the component most often missing from the distractors, so it frequently decides the answer.

## Slide 18
WATCH OUT
Assume anything you send leaves your control
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
A prompt sent to an external service has been disclosed to a third party. It may be logged, retained, reviewed by humans, or used for training, depending on the contract — and deleting it later does not undo the disclosure.
Never send: passwords, hashes, SNMP community strings, pre-shared keys, certificates, API tokens; personal data; real public IP addressing; anything your organisation classifies as confidential or above.
Sanitise first: substitute addresses consistently (documentation ranges 192.0.2.0/24, 198.51.100.0/24, 203.0.113.0/24 exist for exactly this), replace hostnames, strip credential lines entirely, and include only the configuration relevant to the question.
And check the policy. Many organisations permit an approved internal or contracted tool and prohibit public ones. Knowing which applies to you is part of the job now.

## Slide 19
COMMON PITFALLS · Data classification, properly
Common pitfalls
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Pasting a whole running configuration. Slower, worse answers, and a disclosure.
• Confusing generative with agentic. Tool use and autonomy are the difference.
• Omitting the output format. You get an essay where you needed three commands.
• No persona or platform. You get generic advice, or IOS syntax for a platform you are not running.
• Accepting a confident answer without verifying. Check the command exists on your platform before typing it.
• Granting autonomy without considering blast radius.

## Slide 20
COMMON PITFALLS · Data classification, properly
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Assuming it knows your network. It knows the internet.
• Treating an AI-proposed change as exempt from change control.

## Slide 21
BREAK & FIX · SYMPTOM
Chapter 32
The suggested command was accepted and took the site off the air.
An engineer asks an assistant why a trunk is not carrying VLAN 50 and is told to run switchport trunk allowed vlan 50 on the uplink. They apply it. Every VLAN except 50 immediately stops working across that link.
The prompt that was used: “VLAN 50 isn’t going over my trunk, what command fixes it?”
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2

## Slide 22
BREAK & FIX · YOUR MOVE
Chapter 32
The suggested command was accepted and took the site off the air.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 23
BREAK & FIX · DIAGNOSIS
Chapter 32
Why it is doing that
Diagnosis — of the answer. The command is real, correctly spelled and valid. It also replaces the allowed list rather than adding to it, so a trunk carrying 10, 20 and 30 now carries only 50. The correct command was switchport trunk allowed vlan add 50 (Chapter 10).
Diagnosis — of the prompt, which is the examinable part. Measure it against the four components:
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2

## Slide 24
LAB · ANY GENERATIVE AI ASSISTANT, PLUS A LAB DEVICE
Prompt engineering as an examinable skill
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Platform note. This lab needs no particular tool. Use whatever assistant your institution permits — and check that policy first, which is task 1 and is not a formality.
1. Find and read your institution’s or employer’s policy on sending data to AI services. Write down, in one sentence, what you are permitted to send.
2. Take a real configuration from one of your lab devices. Produce a sanitised version fit to include in a prompt: substitute addressing into documentation ranges, rename hosts, remove every credential. List everything you removed and why.
3. Write the weakest useful prompt you can for a real problem from Chapter 14. Record the answer.
4. Rewrite it with all four components. Record the answer. Compare the two for specificity, correctness and usability.

## Slide 25
LAB · ANY GENERATIVE AI ASSISTANT, PLUS A LAB DEVICE
Prompt engineering as an examinable skill (continued)
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
5. Verify both answers on the device. Note anything suggested that was wrong, deprecated, or not supported on your platform. This step is the one that matters.
6. Ask a question whose correct answer depends on context you deliberately withhold — as in this chapter’s Break & Fix. Confirm you can produce a confidently wrong answer, and identify which missing component caused it.
7. Write four candidate prompts for one task, one of which is clearly best, and swap with a colleague. Score each other’s against the four components. This is the exam question format.

## Slide 26
LAB · ANY GENERATIVE AI ASSISTANT, PLUS A LAB DEVICE
Prompt engineering as an examinable skill (continued)
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
8. Autonomy. For each of these, place it on the four-rung ladder and justify: clearing an err-disabled port; adding a VLAN to an access switch; changing an OSPF cost on a core link; opening a ticket.
9. Extension. Write the one-page guidance your team should follow for using AI assistants on network work — what may be sent, what must be verified, and which actions may ever be automatic.

## Slide 27
CHECKPOINT 1 of 6
State the difference between generative and agentic AI in one sentence.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 28
ANSWER
Checkpoint 1 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
State the difference between generative and agentic AI in one sentence.
Generative AI produces content in response to a prompt and stops; agentic AI pursues a goal, uses tools to act, and evaluates its own results.

## Slide 29
CHECKPOINT 2 of 6
Name the four prompt components the blueprint lists, and say which is listed first and why.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 2 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Name the four prompt components the blueprint lists, and say which is listed first and why.
Data classification, output format, persona and instructions. Data classification is listed first, because a prompt that discloses credentials or real addressing is wrong regardless of how good the rest of it is — and the disclosure cannot be undone.

## Slide 31
CHECKPOINT 3 of 6
Give three categories of data that must never be sent to an external AI service.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 32
ANSWER
Checkpoint 3 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Give three categories of data that must never be sent to an external AI service.
Credentials of any kind (passwords, hashes, community strings, pre-shared keys, tokens); personal data; and real public IP addressing or anything the organisation classifies as confidential.

## Slide 33
CHECKPOINT 4 of 6
What is blast radius, and how does it govern how much autonomy an agent should have?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 34
ANSWER
Checkpoint 4 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
What is blast radius, and how does it govern how much autonomy an agent should have?
How much breaks if the action is wrong. It governs autonomy because the question is not how capable the system is but how bad a confident mistake would be — clearing one err-disabled port is reversible and local, while changing a core route map reaches the whole organisation.

## Slide 35
CHECKPOINT 5 of 6
An assistant gives a fluent, confident, wrong answer. What is this called and what is the defence?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 36
ANSWER
Checkpoint 5 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
An assistant gives a fluent, confident, wrong answer. What is this called and what is the defence?
A hallucination. The defence is verification: check the command exists on your platform, check it against the exhibit or the device, and keep change control. Fluency is not evidence.

## Slide 37
CHECKPOINT 6 of 6
Name three genuine uses of AI in network operations.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 38
ANSWER
Checkpoint 6 of 6
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
Name three genuine uses of AI in network operations.
Any three of: anomaly detection, event correlation and noise reduction, root-cause suggestion, configuration drafting and review, documentation and summarisation, capacity forecasting, guided remediation.

## Slide 39
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Generative AI produces content in response to a prompt. Agentic AI pursues a goal, uses tools, acts, and evaluates its own results. Autonomy and tool use are the difference.
• Real roles: anomaly detection, event correlation, root-cause suggestion, configuration drafting, documentation, capacity forecasting, guided remediation.
• Autonomy is a ladder — recommend, approve then act, act then report, fully autonomous — chosen per action according to blast radius.
• The four prompt components: data classification, output format, persona, instructions. A prompt with all four beats one without.

## Slide 40
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 32. AI in Network Operations
5.1 5.2
• Data classification is listed first. Never send credentials, keys, personal data or real public addressing; sanitise into documentation ranges first; check your organisation’s policy.
• In a “select the prompt” question: eliminate anything that leaks, prefer specificity over politeness, and look for the stated output format.
• These systems are confidently wrong, do not know your network, and may be out of date. Verify before you apply, and keep change control.

## Slide 41
Where we got to
• Generative AI produces content in response to a prompt. Agentic AI pursues a goal, uses tools, acts, and evaluates its own results. Autonomy and tool use are the difference.
• Real roles: anomaly detection, event correlation, root-cause suggestion, configuration drafting, documentation, capacity forecasting, guided remediation.
• Autonomy is a ladder — recommend, approve then act, act then report, fully autonomous — chosen per action according to blast radius.
• The four prompt components: data classification, output format, persona, instructions. A prompt with all four beats one without.
NEXT
Chapter 33 — A Troubleshooting Method for the 28 Per Cent