## Slide 1
CCNA 200-301 V2.0
01
Networks, Models and This Exam
Part I — Foundations
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 1: Networks, Models and This Exam. Blueprint topics: none.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
• Describe what a network does, in terms of the four things every network must solve: naming, addressing, forwarding and error handling.
• Explain the layered model well enough to use it as a troubleshooting tool, which is the only reason this exam still cares about it.
• Identify the devices in a small enterprise network and say what each one decides.
• Navigate the CCNA v2.0 blueprint and this book against it.
Notes: Networks, Models and This Exam

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
Nothing. This is the first chapter, and the course assumes no prior networking.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
host
node
link
frame
packet
segment
encapsulation
layer
protocol
switch
router
access layer
distribution layer
broadcast domain
collision domain
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
CONCEPT
The four problems, and the four answers
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
Every network technology in this book is an answer to one of four questions.
• Who am I talking to? → addressing. MAC addresses locally (Chapter 3), IP addresses globally (Chapter 4).
• How do I find them? → forwarding. Switches learn (Chapter 3); routers decide (Chapter 15).
• How do we not talk over each other? → media access and loop prevention (Chapter 3, Chapter 12).
• What if it goes wrong? → error detection, acknowledgement and retransmission (Chapter 6).
When you meet a new protocol, ask which of the four it is answering. It will be one of them.
Notes: Two computers in the same room, joined by a cable, can exchange bytes. Everything else in networking exists because that arrangement does not scale. Add a third machine and you need a way to say which machine you mean. Add a building and you need a way to find a machine you cannot see. Add the internet and you need a way to reach a machine whose owner you have never met, over equipment owned by people you will never meet either.

## Slide 6
DEFINITION
Protocol
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
An agreed set of rules for a conversation: what may be said, in what order, in what format, and what to do when the expected reply does not arrive.
Two people who both know to say “hello”, wait, then speak, have a protocol. Two computers need theirs written down to the bit, because neither can improvise. Almost every capitalised acronym in this book — ARP, DHCP, OSPF, HSRP — is one such agreement, and each exists because somebody had one of the four problems above.

## Slide 7
CONCEPT
The model is a troubleshooting tool
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
When something does not work, the layered model tells you what to test next. If a cable is unplugged, checking DNS is a waste of a minute you do not have in the exam. Work up: is the link up? Does it have an address? Can it reach its gateway? Can it resolve a name? Every troubleshooting question in this exam — and there are eight topics’ worth — is answered by walking the layers in order.
The v2.0 blueprint no longer asks you to describe the OSI model, as v1.1 did. It assumes you use it.
Notes: A network stack is split into layers so that each layer can be changed without rewriting the others. Wi-Fi replaced the cable without anyone rewriting the web. That is the engineering argument, and it is real, but it is not why the layered model matters to you this year.

## Slide 8
DEFINITION
Encapsulation, and the names of things
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
As data moves down the stack each layer wraps it in a header. The wrapped unit gets a different name at each layer, and using the right one is how you show you know which layer you are discussing.
• Application data becomes a segment at layer 4 (TCP) or a datagram (UDP), when a port number is attached.
• That becomes a packet at layer 3, when IP addresses are attached.
• That becomes a frame at layer 2, when MAC addresses are attached.
• That becomes bits at layer 1.
Switches forward frames. Routers forward packets. That single sentence explains most of the difference between the two devices.
Notes: The bottom two rows are where this exam starts: topic 1.1 is entirely physical-layer diagnosis, and it is examined in Chapter 2.

## Slide 9
The devices, and what each one decides
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
A small enterprise network. Access switches connect end devices; a distribution switch aggregates them and routes between VLANs; the router reaches other networks; the firewall polices what leaves. Every chapter in Parts II to IV configures one piece of this picture.

## Slide 10
DEFINITION
Two domains worth keeping straight
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
A collision domain is the set of ports that could transmit at the same instant and interfere. Every switch port is its own collision domain, which is why modern switched networks do not collide — and why a collisions counter that is climbing means something is badly wrong, usually a duplex mismatch (Chapter 2).
A broadcast domain is the set of devices that receive each other’s broadcasts. One VLAN is one broadcast domain. Splitting broadcast domains is the entire purpose of Chapter 8, and joining them again is the purpose of Chapter 15.

## Slide 11
ON THE EXAM
How the blueprint is built, and how to read it
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
This is what the blueprint actually asks for
Cisco publishes twenty-nine numbered topics in five domains. The number is the whole contract: if a technique is not in a topic statement, it is not directly examinable, and if it is, the verb tells you the depth expected.
• Describe — you must be able to explain it. Six topics.
• Interpret, Validate, Select, Use, Manage — you must be able to read output or make a choice. Seven topics.
• Configure — you must produce the commands. Eight topics.
• Troubleshoot or Diagnose — you must find and fix a fault. Eight topics.
Sixteen of twenty-nine are configure-or-fix. That is the single most useful fact about this exam, and it should change how you study: time at a command line beats time with a highlighter, by a wide margin.

## Slide 12
COMMON PITFALLS · This exam, and this book
Common pitfalls
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
• Studying a v1.1 book. The exam number, 200-301, did not change when the blueprint did. A book that teaches QoS, NTP, REST APIs, JSON or Terraform in a CCNA context is written for the old blueprint. Check the version before you trust the contents.
• Learning the OSI layers as a list to recite. Nobody will ask you to name layer 6. They will show you a broken network and expect you to work upwards.
• Assuming “switch” means layer 2. Multilayer switches route. Most of the distribution layer in a real network is switches doing routing, and topic 2.1 explicitly includes switch virtual interfaces.
Notes: Every chapter of this book carries its topic numbers under the title. If you want to revise by blueprint rather than by chapter, Appendix app:coverage maps all twenty-nine topics to the chapters that cover them.

## Slide 13
BREAK & FIX · SYMPTOM
Chapter 1
Three reports, three different layers, and no commands yet.
You have not configured anything and cannot yet read a show command. That is deliberate: this first Break & Fix is about placing a fault, not fixing one, because deciding which layer to investigate is the decision that all the later chapters depend on.
Three reports arrive within an hour.
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam

## Slide 14
BREAK & FIX · YOUR MOVE
Chapter 1
Three reports, three different layers, and no commands yet.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 15
CHECKPOINT 1 of 3
A user reports that a web page will not load. Ping to the server’s IP address succeeds. Which layers have you just ruled out, and which is the first one you should now suspect?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 16
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
A user reports that a web page will not load. Ping to the server’s IP address succeeds. Which layers have you just ruled out, and which is the first one you should now suspect?
Layers 1 to 3 are ruled out: something reached the server and came back. Suspect layer 7 first — specifically name resolution or the web service itself. Test the name (Chapter 21) and the port (Chapter 6).

## Slide 17
CHECKPOINT 2 of 3
A switch port shows as up, but the collisions counter is increasing steadily. Which layer is at fault, and what is the most likely single cause?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 18
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
A switch port shows as up, but the collisions counter is increasing steadily. Which layer is at fault, and what is the most likely single cause?
Layer 1. Rising collisions on a link that reports full duplex means a duplex mismatch: one end is half duplex and is correctly reporting collisions the other end does not see.

## Slide 19
CHECKPOINT 3 of 3
Why does a router drop a packet for an unknown network when a switch floods a frame for an unknown MAC address?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 20
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
Why does a router drop a packet for an unknown network when a switch floods a frame for an unknown MAC address?
Because they are different jobs. A switch’s flooding is a recovery mechanism — the destination is probably on one of those ports and will answer, teaching the switch where it is. A router’s unknown network has no such prospect; flooding a packet to every interface would loop and multiply. So a router drops and reports.

## Slide 21
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 1. Networks, Models and This Exam
• Networks solve four problems: addressing, forwarding, media access and error handling. Every protocol you meet answers one of them.
• Layers matter because they tell you what to test next. Work upwards from the physical layer; do not start at DNS.
• Switches forward frames using MAC addresses and flood when they do not know. Routers forward packets using IP addresses and drop when they do not know.
• One VLAN is one broadcast domain. Every switch port is its own collision domain.
• CCNA v2.0 has twenty-nine topics. Sixteen of them ask you to configure or to fix. Study accordingly.

## Slide 22
Where we got to
• Networks solve four problems: addressing, forwarding, media access and error handling. Every protocol you meet answers one of them.
• Layers matter because they tell you what to test next. Work upwards from the physical layer; do not start at DNS.
• Switches forward frames using MAC addresses and flood when they do not know. Routers forward packets using IP addresses and drop when they do not know.
• One VLAN is one broadcast domain. Every switch port is its own collision domain.
NEXT
Chapter 2 — The Physical Layer and Cable Faults