## Slide 1
CCNA 200-301 V2.0
04
IPv4 Addressing and Subnetting
Part I — Foundations
EXAM TOPICS
1.3
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 4: IPv4 Addressing and Subnetting. Blueprint topics: 1.3.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Convert between dotted decimal, binary and prefix length fast enough to do it in an exam without a calculator.
• Compute the network address, broadcast address, usable range and host count of any subnet, in under thirty seconds.
• Subnet a given block to meet a stated requirement, and apply variable-length masks without overlapping.
• Diagnose the four addressing faults that account for almost every broken host: wrong mask, wrong gateway, address outside the subnet, and duplicate address.
Notes: IPv4 Addressing and Subnetting 1.3

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Chapter 1 and Chapter 3. You need to be comfortable that a switch works on MAC addresses and a router works on IP addresses.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
dotted decimal
prefix length
subnet mask
network address
broadcast address
usable range
block size
magic number
RFC 1918
private address
public address
VLSM
default gateway
APIPA
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
This topic is worth more time than any other in Part I
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
This is what the blueprint actually asks for
Topic 1.3 says troubleshoot IPv4 addressing, assignment and subnetting, “public and private”. You will be given a host that cannot reach something and expected to spot that its mask is wrong. Every second you spend computing a subnet boundary is a second not spent reasoning, so the arithmetic has to be automatic. Learn the method in §sec:magic until it is boring.

## Slide 6
DEFINITION
Bits, bytes and octets
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
A bit is a single 0 or 1. Eight bits make a byte, which in networking is almost always called an octet — the words mean the same thing here.
Each position in an octet is worth twice the one to its right:
Notes: Everything in this chapter is a consequence of one fact: an IPv4 address is 32 bits, and we write it as four decimal numbers only for our own convenience. The shortcut in Section sec:magic lets you subnet without ever writing a bit down — but it will be a magic trick you can forget rather than a method you can rebuild unless you look at the bits properly once. This is that once.

## Slide 7
CONCEPT
Both directions, in one line each
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Binary to decimal: add the position values wherever there is a 1. 64+8+4+1 = 77.
Decimal to binary: walk left to right, and at each position ask “does this fit in what is left?”. For 77: 128 no (0), 64 yes (1, leaving 13), 32 no (0), 16 no (0), 8 yes (1, leaving 5), 4 yes (1, leaving 1), 2 no (0), 1 yes (1, leaving 0). That gives 01001101.
Two facts fall straight out and are worth holding on to. 255 is all eight bits set — which is why it is the largest value an octet can hold, and why a mask octet of 255 means “all of this octet is network”. And 0 is all eight clear, meaning “none of it is”.
Notes: % Nine columns: the budget is about 12.8 cm, not the 15.78 of two.

## Slide 8
WORKED EXAMPLE
Where the block size comes from
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Take 192.168.10.77 with mask 255.255.255.192, and write only the last octet of each in bits:
{@{}ll@{}} address 77 & 01 001101 mask 192 & 11 000000
The mask has two 1 bits in this octet, so two bits of it are network and the remaining six are host. Set those six host bits to zero and you have the network address; set them all to one and you have the broadcast address:
{@{}lll@{}} network & 01 000000 & = 64 broadcast & 01 111111 & = 127
So the subnet is 192.168.10.64 to 192.168.10.127 — and it is 64 addresses wide, because six free host bits give 2⁶ = 64 combinations.
Now notice: 256 - 192 = 64 as well. That is not a coincidence and it is not a trick. Subtracting the mask value from 256 is simply a fast way of asking “how many combinations do the remaining host bits have?” That is the magic number, and Section sec:magic does the whole job with it.

## Slide 9
CONCEPT
Powers of two, which you should know on sight
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Host bits decide subnet size, so these eleven numbers cover almost every question you will be asked.
{@{}lllllllllll@{}} 2¹ & 2² & 2³ & 2⁴ & 2⁵ & 2⁶ & 2⁷ & 2⁸ & 2⁹ & 2¹⁰ & 2¹¹ 2 & 4 & 8 & 16 & 32 & 64 & 128 & 256 & 512 & 1024 & 2048
Usable hosts is always two fewer than the total, because the all-zeros address names the network itself and the all-ones address is the broadcast. Neither can be given to a host. So six host bits give 64 addresses and 62 usable ones.

## Slide 10
DEFINITION
Network part and host part
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
The subnet mask marks, with 1 bits, which leading bits of the address identify the network. The remaining 0 bits identify the host within it. Written as a count of 1 bits, the mask is a prefix length: 255.255.255.0 and /24 are the same statement.
Two addresses are on the same subnet if and only if their network parts are identical. That single sentence is the source of most addressing faults: a host with the wrong mask computes a different network part, decides its neighbour is remote, and sends the traffic to a gateway that may not want it.
Notes: An IPv4 address is 32 bits, written as four decimal bytes. It carries two pieces of information at once, and the mask is what separates them.

## Slide 11
DEFINITION
Default gateway
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
The address a host sends traffic to when the destination is not on its own subnet. Almost always a router or a layer 3 switch interface on that subnet.
Every host makes exactly one decision for every packet it sends, and it makes it with the mask:
Three consequences that account for a great many faults, and that Chapter 28 will make you test for directly:
• Same network part as mine? Then the destination is local. ARP for it directly and send the frame straight there. The gateway is not involved at all.
• Different? Then it is remote. ARP for the gateway, and hand the frame to it — with the destination’s IP address still inside, but the gateway’s MAC address on the outside.
• A host with no gateway can reach its own subnet and nothing else. Everything local works, so the user reports “the internet is down” rather than “my machine is misconfigured”.
• The gateway must be inside the host’s own subnet. A host will not ARP for something it believes is remote, so a gateway outside the subnet is unreachable by definition — which is the fault in this chapter’s Break & Fix.

## Slide 12
DEFINITION
Default gateway (continued)
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Get the mask wrong and the host makes the local-or-remote decision wrongly, for some destinations and not others. That is why a wrong mask presents as “some things work”, which is far harder to read than “nothing works”.

## Slide 13
DEFINITION
Private addresses — RFC 1918
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Three ranges are reserved for internal use and are never routed on the internet. The exam expects you to recognise them instantly.
• 10.0.0.0/8 — one very large block
• 172.16.0.0/12 — that is 172.16.0.0 to 172.31.255.255, and the upper bound catches people out
• 192.168.0.0/16
Also worth knowing: 169.254.0.0/16 is APIPA, which a host assigns itself when DHCP fails. A host with a 169.254 address has not been given one — see Chapter 20.
Notes: Usable is block size minus two, because the first address in a block is the network address and the last is the broadcast address. The exception is /31, where both are usable because a point-to-point link has no need for a broadcast.

## Slide 14
CONCEPT
Four steps, every time
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Find the interesting octet — the one where the mask is neither 255 nor 0.
• Block size = 256 - (the mask value in that octet). This is the magic number.
• Count in blocks from zero in that octet until you pass the address. The multiple you last passed is the network address.
• Broadcast = next network address -1. Usable range is everything between the two, exclusive.
Notes: You have now seen where this comes from, so it is a shortcut rather than a spell. In the exam you will not have time to write out binary — and after this section you will not need to.

## Slide 15
WORKED EXAMPLE
Where does 172.16.83.190/26 live?
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Mask for /26 is 255.255.255.192. The interesting octet is the fourth.
• Block size = 256 - 192 = 64.
• Count in 64s in the fourth octet: 0, 64, 128, 192. Our host is 190, which sits after 128 and before 192. Network address is 172.16.83.128.
• Next network is 172.16.83.192, so broadcast is 172.16.83.191. Usable range is 172.16.83.129 to 172.16.83.190.
So .190 is the last usable address in its subnet — a perfectly valid host address, and a favourite exam distractor because it looks like a broadcast.

## Slide 16
WORKED EXAMPLE
The same method in the third octet: 10.44.150.7/21
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• /21 is 255.255.248.0. Interesting octet is the third.
• Block size = 256 - 248 = 8.
• Count in 8s in the third octet: 0, 8, …, 144, 152. Our 150 sits after 144. Network is 10.44.144.0.
• Next network is 10.44.152.0, so broadcast is 10.44.151.255. Usable is 10.44.144.1 to 10.44.151.254 — 2046 hosts.
Note that the fourth octet plays no part in finding the boundary. Only the interesting octet does.

## Slide 17
WORKED EXAMPLE
Split 192.168.20.0/24 for four sites of 50, 25, 10 and 2 hosts
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Work largest first, or you will strand addresses.
• 50 hosts needs 62 usable → /26, block 64. 192.168.20.0/26 — usable .1–.62.
• 25 hosts needs 30 usable → /27, block 32. Next free address is .64: 192.168.20.64/27 — usable .65–.94.
• 10 hosts needs 14 usable → /28, block 16. Next free is .96: 192.168.20.96/28 — usable .97–.110.
• 2 hosts (a router link) → /30, block 4. Next free is .112: 192.168.20.112/30 — usable .113–.114.
Everything from .116 upwards is still free. This is VLSM: different masks inside one block, sized to the requirement.

## Slide 18
WATCH OUT
The two rules VLSM must obey
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• A subnet must start on a multiple of its own block size. A /27 can start at .64 or .96, never at .70.
• Subnets must not overlap. If you allocate smallest-first you will eventually place a large subnet where it does not fit, and have to start again. Largest first avoids this.

## Slide 19
CONFIGURE
An interface address and a default gateway
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
IOS · configuration mode
! On a router interface -- the mask is written in full.
interface GigabitEthernet0/0
description User VLAN 10 gateway
ip address 192.168.20.1 255.255.255.192
no shutdown
!
! On a layer 2 switch, the management address lives on an SVI,
! and the switch needs a default gateway because it does not route.
interface Vlan10
ip address 192.168.20.2 255.255.255.192
no shutdown
!
ip default-gateway 192.168.20.1

## Slide 20
VERIFY
show ip interface brief
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
R1#
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 192.168.20.1 YES manual up up
GigabitEthernet0/1 unassigned YES unset administratively down down
Vlan1 unassigned YES unset down down

## Slide 21
CONCEPT
Reading the two status columns
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
The pair of columns is the single most useful diagnostic on a router, and the combinations mean different things.
• up / up — working.
• up / down — the cable and electrical link are fine, but the protocol is not. Usually an encapsulation or keepalive mismatch, or the far end is not configured.
• down / down — a physical problem. Cable, transceiver, or the other end is shut. Go back to Chapter 2.
• administratively down / down — somebody typed shutdown. The fix is no shutdown.

## Slide 22
COMMON PITFALLS · Configuring and verifying an address
Common pitfalls
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Forgetting no shutdown. Router interfaces are shut by default. Switch ports are not. This asymmetry catches everyone once.
• Assuming 172.16.0.0/12 stops at 172.16. It runs to 172.31.255.255. 172.32.0.0 is public.
• Giving the gateway an address outside the subnet. A host will accept the configuration and then fail silently for everything off-net.
• Using the network or broadcast address on a host. .0 and .255 are only network and broadcast in a /24. In a /26 the boundaries move, and 192.168.20.64 is a network address even though it does not end in zero.

## Slide 23
BREAK & FIX · SYMPTOM
Chapter 4
“I can reach my own floor but nothing else”.
A host is configured 192.168.20.100 mask 255.255.255.192, gateway 192.168.20.1. It can ping 192.168.20.90 but not its gateway and nothing beyond.
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3

## Slide 24
BREAK & FIX · YOUR MOVE
Chapter 4
“I can reach my own floor but nothing else”.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 25
BREAK & FIX · DIAGNOSIS
Chapter 4
Why it is doing that
Diagnosis. Work the mask. /26 gives block size 64, so the boundaries are .0, .64, .128, .192. The host at .100 is in the 192.168.20.64/26 subnet, usable .65–.126. Its gateway at .1 is in the first subnet, 192.168.20.0/26. The host and its gateway are on different subnets, so the host cannot ARP for it and has no way off its own segment. It can still reach .90 because that address is in the same /26.
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3

## Slide 26
BREAK & FIX · THE FIX
Chapter 4
And the lesson
Fix. Either move the host into the subnet its gateway serves, or — far more likely what was intended — correct the gateway to 192.168.20.65, the first usable address of the subnet the host is actually in. Then confirm with a ping to the gateway before testing anything remote.
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3

## Slide 27
LAB · PACKET TRACER
Subnet, configure, then break it
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
Topology. One router, two switches, four PCs — two per VLAN.
1. Subnet 172.16.5.0/24 into two subnets of at least 100 hosts each. Write down, before touching a device: network address, first and last usable address, and broadcast address for both.
2. Configure the router with a gateway address in each subnet and the PCs with addresses from your plan. Verify with show ip interface brief and a ping within each subnet.
3. Prove routing works between the two subnets by pinging across.
4. Now change one PC’s mask from your planned value to 255.255.255.0. Predict what will break before you test, then test it. Explain the result in terms of the network part.

## Slide 28
LAB · PACKET TRACER
Subnet, configure, then break it (continued)
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
1. Change it back, then set one PC’s gateway to an address in the other subnet. Predict and test again.
2. Extension. Re-plan the same /24 using VLSM for four segments of 100, 50, 20 and 2 hosts, and configure it without overlaps.

## Slide 29
CHECKPOINT 1 of 3
For 10.19.200.37/27: give the network address, broadcast address, and first and last usable address.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
For 10.19.200.37/27: give the network address, broadcast address, and first and last usable address.
/27 gives a block size of 32 in the fourth octet. The address ends in 37, which falls in the block starting at 32. Network 10.19.200.32, broadcast 10.19.200.63, first usable 10.19.200.33, last usable 10.19.200.62.

## Slide 31
CHECKPOINT 2 of 3
A host is 192.168.1.130/25 and its gateway is 192.168.1.126. Will it work? Show your reasoning.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 32
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
A host is 192.168.1.130/25 and its gateway is 192.168.1.126. Will it work? Show your reasoning.
No. /25 has a block size of 128, so the host is in 192.168.1.128/25, whose range is .129 to .254. The gateway 192.168.1.126 is in the other half, 192.168.1.0/25. The host will ARP for a gateway that is not on its segment and reach nothing beyond its own subnet.

## Slide 33
CHECKPOINT 3 of 3
How many usable addresses does a /30 provide, and why is a /31 sometimes used instead on a router-to-router link?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 34
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
How many usable addresses does a /30 provide, and why is a /31 sometimes used instead on a router-to-router link?
Two. A /31 is used on a router-to-router link because there are only ever two devices and neither needs a broadcast address, so it provides both addresses usefully and halves the address consumption of every point-to-point link on a network.

## Slide 35
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Address plus mask equals two facts: which network, and which host. Devices are on the same subnet only if their network parts match.
• Block size =256- mask octet. Count in blocks. That method answers every subnetting question you will be asked.
• Usable = block -2, except /31 and /32.
• Private ranges are 10/8, 172.16/12 (to 172.31) and 192.168/16. A 169.254 address means DHCP failed.
• Plan VLSM largest first, and start every subnet on a multiple of its own block size.

## Slide 36
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 4. IPv4 Addressing and Subnetting
1.3
• Four faults cover most cases: wrong mask, wrong gateway, address outside the subnet, duplicate address.

## Slide 37
Where we got to
• Address plus mask equals two facts: which network, and which host. Devices are on the same subnet only if their network parts match.
• Block size =256- mask octet. Count in blocks. That method answers every subnetting question you will be asked.
• Usable = block -2, except /31 and /32.
• Private ranges are 10/8, 172.16/12 (to 172.31) and 192.168/16. A 169.254 address means DHCP failed.
NEXT
Chapter 5 — IPv6 Addressing