## Slide 1
CCNA 200-301 V2.0
05
IPv6 Addressing
Part I — Foundations
EXAM TOPICS
1.4
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 5: IPv6 Addressing. Blueprint topics: 1.4.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Abbreviate and expand an IPv6 address correctly, applying both compression rules without ambiguity.
• Identify the address types the exam names: global unicast, link local, unique local, multicast, and the solicited-node address.
• Construct an interface identifier by modified EUI-64, which the blueprint calls out explicitly.
• Size a prefix, and diagnose the assignment faults that stop an IPv6 host communicating.
Notes: IPv6 Addressing 1.4

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Chapter 4 — the ideas of network part, host part and prefix length carry over unchanged. Chapter 3 for MAC addresses, which EUI-64 is built from.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
global unicast
link local
unique local
multicast
solicited-node
anycast
modified EUI-64
SLAAC
router advertisement
neighbour discovery
dual stack
prefix
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
What v2.0 asks, and what it dropped
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
This is what the blueprint actually asks for
Topic 1.4 says troubleshoot IPv6 address configuration, assignment and prefix sizing, and narrows the scope to “unicast and modified EUI 64”. The previous blueprint asked you to compare every address type in detail; this one does not. Concentrate on getting an address onto an interface, understanding where the link-local one came from, and spotting a wrong prefix.

## Slide 6
CONCEPT
The two compression rules
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Drop leading zeros in any group. 0db8 becomes db8; 0000 becomes 0. Trailing zeros are never dropped.
• Replace one run of all-zero groups with ::. You may do this once only, because a second :: would make the address ambiguous — there would be no way to know how many zeros each stood for.
Notes: An IPv6 address is 128 bits, written as eight groups of four hex digits separated by colons. If hexadecimal is not yet automatic, the two-minute primer in Chapter 3 is the one thing to re-read before going on — this whole chapter is written in it, and modified EUI-64 below cannot be followed without being able to expand one hex digit into four bits. Two rules compress it.

## Slide 7
WORKED EXAMPLE
Compressing an address
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Start with the full form:
2001:0db8:0000:0000:0000:ff00:0042:8329
• Drop leading zeros in each group: 2001:db8:0:0:0:ff00:42:8329
• Replace the longest run of zero groups with ::: 2001:db8::ff00:42:8329
Expanding is the same in reverse. Given 2001:db8::1, count the groups present — two before the :: and one after, so three — and the :: must therefore stand for five zero groups: 2001:0db8:0000:0000:0000:0000:0000:0001.

## Slide 8
WATCH OUT
There is no broadcast in IPv6
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
IPv6 has no broadcast address at all. Where IPv4 would broadcast, IPv6 uses a multicast group — usually ff02::1, all nodes. This is why ARP does not exist in IPv6: its job is done by neighbour discovery using the solicited-node multicast address, which reaches only the handful of hosts whose addresses end the same way rather than every device on the segment.

## Slide 9
CONCEPT
Turning a 48-bit MAC into a 64-bit interface ID
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Split the MAC in half.
• Insert fffe in the middle.
• Flip the seventh bit of the first byte — the universal/local bit. In hex this means adding or subtracting 2 from the second hex digit.
Notes: The blueprint names this explicitly, so it is examinable arithmetic.

## Slide 10
WORKED EXAMPLE
EUI-64 from 00d0.58a1.0201
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Split: 00d0.58 and a1.0201.
• Insert fffe: 00d0:58ff:fea1:0201.
• Flip the seventh bit of 00. In binary 00 is 0000 0000; flipping the seventh bit gives 0000 0010, which is 02.
• Interface ID is 02d0:58ff:fea1:0201. With a prefix of 2001:db8:acad:10::/64 the full address is 2001:db8:acad:10:2d0:58ff:fea1:201.
The quick check: an address containing ff:fe in the middle of its host portion was almost certainly built by EUI-64.

## Slide 11
CONFIGURE
IPv6 on a router interface, three ways
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
IOS · configuration mode
! Routing must be enabled globally first -- this is the step most often
! forgotten, and without it the router will not forward or advertise.
ipv6 unicast-routing
!
interface GigabitEthernet0/0
description User VLAN 10 gateway
! 1. A fully specified address.
ipv6 address 2001:db8:acad:10::1/64
! 2. Or let the device build the host part by EUI-64.
ipv6 address 2001:db8:acad:20::/64 eui-64
! 3. A link-local address is created automatically, but you can pin it
! to something memorable -- worth doing, because routing protocols
! show it as the next hop.
ipv6 address fe80::1 link-local
no shutdown

## Slide 12
VERIFY
show ipv6 interface brief
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
R1#
GigabitEthernet0/0 [up/up]
FE80::1
2001:DB8:ACAD:10::1
2001:DB8:ACAD:20:2D0:58FF:FEA1:201
GigabitEthernet0/1 [administratively down/down]
unassigned

## Slide 13
CONCEPT
How a host gets an address: SLAAC versus DHCPv6
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
A host sends a router solicitation to ff02::2; a router replies with a router advertisement carrying the prefix. Then either:
• SLAAC — the host builds its own address from the advertised prefix plus an interface ID it generates. No server involved.
• DHCPv6 — the advertisement tells the host to ask a server, which supplies the address and other options.
A host with only a fe80:: address and no global one has heard no router advertisement. That is the IPv6 equivalent of an APIPA address, and it points at the router, not the host.
Notes: Note that one interface holds several addresses at once, and that this is normal rather than a fault. An IPv6 interface essentially always has a link-local address plus whatever global addresses it has been given.

## Slide 14
COMMON PITFALLS · Configuring IPv6
Common pitfalls
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Omitting ipv6 unicast-routing. Interfaces come up and addresses look right, but the router neither forwards nor advertises.
• Using :: twice. It is not merely discouraged, it is invalid, because the address can no longer be expanded uniquely.
• Dropping trailing zeros. 2001:db8:1000:: cannot be shortened to 2001:db8:1::. Only leading zeros go.
• Assuming a prefix other than /64 for a LAN. SLAAC requires a 64-bit interface ID, so a LAN prefix longer than /64 breaks autoconfiguration. Point-to-point links are the usual exception.

## Slide 15
BREAK & FIX · SYMPTOM
Chapter 5
Dual-stack host reaches IPv4 destinations only.
A workstation has a working IPv4 address and, for IPv6, only fe80::2d0:58ff:fea1:201. It cannot reach any IPv6 destination, on or off the segment.
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4

## Slide 16
BREAK & FIX · YOUR MOVE
Chapter 5
Dual-stack host reaches IPv4 destinations only.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 17
BREAK & FIX · DIAGNOSIS
Chapter 5
Why it is doing that
Diagnosis. A link-local address is generated by the host itself and proves nothing except that the interface is up. The absence of a global address means no router advertisement is being received. Either no router is configured for IPv6 on that VLAN, or ipv6 unicast-routing is missing, or the router interface has no global prefix to advertise.
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4

## Slide 18
BREAK & FIX · THE FIX
Chapter 5
And the lesson
Fix. On the gateway, confirm ipv6 unicast-routing is present in the running configuration, then check show ipv6 interface GigabitEthernet0/0 shows a global address and that router advertisements are not suppressed. Bring the prefix back and the host will build its own address within seconds — no change is needed on the host at all.
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4

## Slide 19
LAB · PACKET TRACER
Dual-stack a small network
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Topology. One router, one switch, two PCs, addressed for both protocols.
1. Enable ipv6 unicast-routing and give Gi0/0 the address 2001:db8:acad:10::1/64 and link-local fe80::1.
2. Set both PCs to obtain IPv6 automatically. Record the addresses they build and confirm they contain ff:fe.
3. Compute by hand what each PC’s EUI-64 address should be from its MAC, and check your answer against the device.
4. Ping between the PCs using IPv6, then ping the router’s link-local address from a PC. Note that the link-local ping needs no global addressing at all.

## Slide 20
LAB · PACKET TRACER
Dual-stack a small network (continued)
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
1. Remove ipv6 unicast-routing and observe what happens to the PCs after their addresses expire.
2. Extension. Configure a second VLAN with prefix 2001:db8:acad:20::/64 and route between the two.

## Slide 21
CHECKPOINT 1 of 3
Compress 2001:0db8:0000:0012:0000:0000:0000:00ab fully.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 22
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Compress 2001:0db8:0000:0012:0000:0000:0000:00ab fully.
2001:db8:0:12::ab. Leading zeros drop in every group; the single run of three all-zero groups becomes ::. Note the fourth group is 0, not part of the :: — only one run may be compressed, and the longer one wins.

## Slide 23
CHECKPOINT 2 of 3
A host shows only an fe80:: address. What is missing, and on which device would you look?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 24
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
A host shows only an fe80:: address. What is missing, and on which device would you look?
A global unicast address, which means no router advertisement is being received. Look at the router or layer 3 switch for the segment: is ipv6 unicast-routing enabled, and does the interface have a global address to advertise a prefix from?

## Slide 25
CHECKPOINT 3 of 3
Build the modified EUI-64 interface identifier for MAC aabb.cc00.0100.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 26
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
Build the modified EUI-64 interface identifier for MAC aabb.cc00.0100.
Split the MAC, insert fffe, and flip the seventh bit: aa becomes a8. The result is a8bb:ccff:fe00:0100.

## Slide 27
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 5. IPv6 Addressing
1.4
• Drop leading zeros; use :: once, for the longest zero run.
• 2000::/3 global, fe80::/10 link local, fd00::/8 unique local, ff00::/8 multicast. There is no broadcast.
• EUI-64: split the MAC, insert fffe, flip the seventh bit.
• ipv6 unicast-routing is a separate, easily forgotten step.
• LANs are /64 because SLAAC needs a 64-bit interface ID.
• Only a link-local address means no router advertisement was heard — investigate the router, not the host.

## Slide 28
Where we got to
• Drop leading zeros; use :: once, for the longest zero run.
• 2000::/3 global, fe80::/10 link local, fd00::/8 unique local, ff00::/8 multicast. There is no broadcast.
• EUI-64: split the MAC, insert fffe, flip the seventh bit.
• ipv6 unicast-routing is a separate, easily forgotten step.
NEXT
Chapter 6 — TCP, UDP and the Diagnostic Toolkit