## Slide 1
CCNA 200-301 V2.0
07
The IOS Command Line
Part I — Foundations
EXAM TOPICS
2.4
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 7: The IOS Command Line. Blueprint topics: 2.4.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
• Move between IOS command modes without hesitating, and recognise which mode a prompt indicates.
• Distinguish the running configuration from the startup configuration, and save deliberately rather than by habit.
• Perform a first-time device setup: hostname, addressing, passwords, SSH and a banner.
• Filter show output, which is what makes long output usable under exam time pressure.
Notes: The IOS Command Line 2.4

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Chapter 4 for addressing and Chapter 6 for the diagnostic commands you will now be typing for real.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
user EXEC
privileged EXEC
global configuration
interface configuration
line configuration
running-config
startup-config
NVRAM
context-sensitive help
pipe
banner
SSH
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
CONCEPT
Getting out, and the two ways to do it
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
exit steps back one level. end, or Ctrl-Z, jumps straight to privileged EXEC from anywhere. When an exam question shows you a prompt, the prompt is telling you which commands are currently legal — a global command typed in interface mode is rejected, and that is a favourite trap.
One shortcut worth knowing: do runs a privileged EXEC command without leaving configuration mode, so do show ip interface brief works from SW1(config-if)#.

## Slide 6
DEFINITION
running-config and startup-config
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
The running configuration is in RAM. It is what the device is doing right now, and every command you type takes effect there immediately.
The startup configuration is in NVRAM. It is what the device will load when it next boots. Nothing you type reaches it until you copy it there.
• copy running-config startup-config — save. Abbreviated wr or write memory on most platforms.
• show running-config — what is in force.
• show startup-config — what will be in force after a reload.

## Slide 7
WATCH OUT
Not saving is a technique, not only a mistake
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Because configuration takes effect immediately and is lost on reload, a deliberately unsaved change is a safety net. If you are about to modify the access list or the interface you are connected through, and you get it wrong, a power cycle restores the last saved configuration and your access with it.
The professional habit is: make the risky change, verify you still have access, then save. Reversing that order is how people lock themselves out of devices in another building.

## Slide 8
CONCEPT
Filtering output is a survival skill
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
A full show running-config on a production switch runs to hundreds of lines. The pipe cuts it to what you need, and in an exam it is the difference between answering and scrolling.
• | include vlan — only lines containing “vlan”
• | exclude ! — drop the ! comment lines
• | begin interface — start output at the first match
• | section interface Gi0/1 — that interface’s whole block

## Slide 9
VERIFY
show running-config | section interface GigabitEthernet0/1
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
SW1#
interface GigabitEthernet0/1
description Uplink to SW2
switchport trunk encapsulation dot1q
switchport mode trunk
switchport trunk allowed vlan 10,20,30

## Slide 10
CONFIGURE
A switch from the box to remotely manageable
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
IOS · configuration mode
enable
configure terminal
!
! 1. Identify the device. The hostname appears in every prompt and log.
hostname SW1
!
! 2. Protect privileged mode. "secret" is hashed; "password" is not --
! never use "enable password".
enable secret Str0ng-Enable-Secret
!
! 3. A local user for SSH, with full privilege.
username netadmin privilege 15 secret Str0ng-User-Secret
!
! 4. A management address. A layer 2 switch has no routed ports, so
! this lives on an SVI, and it needs a gateway to be reachable
! from another subnet.
interface Vlan1
ip address 10.0.0.11 255.255.255.0
no shutdown
exit
ip default-gateway 10.0.0.1

## Slide 11
CONFIGURE
A switch from the box to remotely manageable (continued)
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
IOS · configuration mode
!
! 5. SSH needs a domain name and a key. 2048-bit minimum; version 2 only.
ip domain-name example.local
crypto key generate rsa modulus 2048
ip ssh version 2
!
! 6. Console: require login, and stop output interrupting your typing.
line console 0
login local
logging synchronous
exec-timeout 10 0
exit
!
! 7. Remote access: SSH only, authenticated against local users.
line vty 0 15
login local
transport input ssh
exec-timeout 10 0
exit
!

## Slide 12
CONFIGURE
A switch from the box to remotely manageable (continued)
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
IOS · configuration mode
! 8. A legal banner. Never write "welcome" -- it has been argued in court.
banner motd # Authorised access only. Activity is logged. #
!
end
copy running-config startup-config

## Slide 13
VERIFY
show ip ssh
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
SW1#
SSH Enabled - version 2.0
Authentication timeout: 120 secs; Authentication retries: 3

## Slide 14
COMMON PITFALLS · A first-time setup, end to end
Common pitfalls
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
• Using enable password. It is stored in clear text. enable secret is hashed, and where both exist the secret wins.
• Forgetting transport input ssh. Leave it at the default and Telnet stays available, which undoes the point of configuring SSH.
• Generating a key without a hostname and domain name. The key is named after them, and the command fails or produces a useless key if they are still at defaults.
• Saving before verifying. See the warning above. Verify access, then save.
• Omitting logging synchronous. Without it a log message arrives in the middle of the line you are typing, and you cannot tell what you have actually entered.

## Slide 15
BREAK & FIX · SYMPTOM
Chapter 7
The change worked yesterday and the device came back without it.
A colleague configured a new VLAN and confirmed it working. After a power cut overnight, the VLAN is gone and the configuration looks like it did last week.
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4

## Slide 16
BREAK & FIX · YOUR MOVE
Chapter 7
The change worked yesterday and the device came back without it.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 17
BREAK & FIX · EVIDENCE
Chapter 7
show archive config differences nvram:startup-config system:running-config
SW1#
!Contextual Config Diffs:
+vlan 30
+ name Guest
+interface GigabitEthernet0/9
+ switchport access vlan 30
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 18
BREAK & FIX · YOUR MOVE
Chapter 7
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Notes: The elimination matters as much as the answer.

## Slide 19
BREAK & FIX · DIAGNOSIS
Chapter 7
Why it is doing that
Diagnosis. The change was made in the running configuration and never copied to the startup configuration. The reload loaded NVRAM, which did not have it. Nothing is broken — the device did exactly what it was told.
Confirm it by comparing the two before doing anything else:
Any output at all means the two differ and a reload will lose the difference.
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4

## Slide 20
BREAK & FIX · THE FIX
Chapter 7
And the lesson
Fix. Re-apply the change, verify, then copy running-config startup-config. As a habit, run that comparison before you leave any device.
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4

## Slide 21
LAB · PACKET TRACER
Bring up a switch you can reach from your desk
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Topology. One switch, one PC on the same VLAN, connected by console cable and by an Ethernet cable.
1. Connect by console. Move through all five modes in turn and write down the prompt at each. Use end to jump back from the deepest.
2. Set hostname, enable secret and a local user.
3. Give Vlan1 an address in the PC’s subnet and a default gateway. Ping the switch from the PC to prove it.
4. Enable SSH properly: domain name, 2048-bit key, version 2, and transport input ssh on the VTY lines.
5. SSH from the PC. Then try Telnet and confirm it is refused.

## Slide 22
LAB · PACKET TRACER
Bring up a switch you can reach from your desk (continued)
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
1. Make a small change, do not save, reload, and observe the change vanish. Repeat with a save.
2. Extension. Practise | include, | section and | begin on show running-config until you can extract a single interface block in one command without thinking.

## Slide 23
CHECKPOINT 1 of 3
You are at SW1(config-if)# and need to check the routing table without losing your place. What do you type?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 24
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
You are at SW1(config-if)# and need to check the routing table without losing your place. What do you type?
do show ip route. The do prefix runs a privileged EXEC command from any configuration mode without leaving it.

## Slide 25
CHECKPOINT 2 of 3
Which configuration does a device load on boot, and which one are you editing when you type a command?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 26
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Which configuration does a device load on boot, and which one are you editing when you type a command?
It boots from startup-config in NVRAM. You are editing running-config in RAM. Anything not saved is lost at the next reload — see Chapter 31 for how this catches out automation too.

## Slide 27
CHECKPOINT 3 of 3
Why must a hostname and domain name be set before generating an RSA key?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 28
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
Why must a hostname and domain name be set before generating an RSA key?
Because the RSA key pair is named after the fully qualified domain name, hostname.domain. Without both, the device has no name to label the key with and refuses to generate it.

## Slide 29
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 7. The IOS Command Line
2.4
• The prompt tells you the mode, and the mode decides which commands are legal. end returns to privileged EXEC from anywhere; do runs one EXEC command without leaving.
• Commands take effect in the running configuration immediately and are lost on reload until copied to the startup configuration.
• Verify access first, save second. An unsaved risky change is a safety net.
• enable secret, not enable password. SSH version 2 with a 2048-bit key, and transport input ssh to shut off Telnet.
• Filtering with | include, | section and | begin is what makes device output usable at speed.

## Slide 30
Where we got to
• The prompt tells you the mode, and the mode decides which commands are legal. end returns to privileged EXEC from anywhere; do runs one EXEC command without leaving.
• Commands take effect in the running configuration immediately and are lost on reload until copied to the startup configuration.
• Verify access first, save second. An unsaved risky change is a safety net.
• enable secret, not enable password. SSH version 2 with a 2048-bit key, and transport input ssh to shut off Telnet.
NEXT
Chapter 8 — VLANs and Access Ports