## Slide 1
CCNA 200-301 V2.0
08
VLANs and Access Ports
Part II — Switching and Network Access
EXAM TOPICS
2.2
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 8: VLANs and Access Ports. Blueprint topics: 2.2.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
• Explain what a VLAN changes about a switch, in terms of the learning-and-flooding algorithm from Chapter 3.
• Create VLANs and assign access ports to them.
• Verify VLAN membership from three different angles, and know which one to trust when they disagree.
• Diagnose the classic VLAN faults: a port in the wrong VLAN, a VLAN that does not exist, and a VLAN that is shut down.
Notes: VLANs and Access Ports 2.2

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Chapter 3 for the MAC table and flooding; Chapter 7 for moving around the command line.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
VLAN
broadcast domain
access port
VLAN database
default VLAN
native VLAN
management VLAN
SVI
VLAN 1
shutdown VLAN
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
DEFINITION
VLAN
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
A VLAN is a broadcast domain implemented in software on a switch. Ports in VLAN 10 behave as though they were on a physically separate switch from ports in VLAN 20: a broadcast from one never reaches the other, and a frame cannot cross between them without passing through something that routes.

## Slide 6
CONCEPT
One line changes in the switching algorithm
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Recall the algorithm from Chapter 3: learn the source, then forward, flood, or filter. VLANs change exactly one thing — every step is now scoped to a VLAN.
• Learning is per VLAN. The same MAC address may legitimately appear in two VLANs on the same switch.
• Flooding is per VLAN. An unknown unicast in VLAN 10 goes out every VLAN 10 port and no others.
• A frame never leaves the VLAN it arrived in. Not once, not for broadcast, not for anything.
That is the whole mechanism. Everything else about VLANs — trunking, inter-VLAN routing, voice VLANs — is machinery for coping with the consequences of that one rule.

## Slide 7
What a VLAN actually does
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
The whole idea, in one picture. Four ports on one switch become two broadcast domains that cannot reach each other — and nothing physical changed.

## Slide 8
WATCH OUT
The consequence people forget
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
If two devices are in different VLANs they cannot communicate, even if they are in the same IP subnet, plugged into adjacent ports on the same switch. The switch will not carry the frame. Conversely two devices in the same VLAN but different subnets cannot communicate either, because IP will not deliver it.
VLAN and subnet are separate ideas that must be kept aligned by design. The convention that saves everyone trouble is one VLAN, one subnet, and a number that matches: VLAN 10 is 192.168.10.0/24, VLAN 20 is 192.168.20.0/24.

## Slide 9
CONFIGURE
Three VLANs and the access ports that use them
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
IOS · configuration mode
! Create the VLANs and name them. A name is documentation that
! survives on the device -- use it.
vlan 10
name Staff
vlan 20
name Guest
vlan 30
name Voice
exit
!
! Assign a single access port.
interface GigabitEthernet0/5
description Staff desk 5
switchport mode access
switchport access vlan 10
no shutdown
!

## Slide 10
CONFIGURE
Three VLANs and the access ports that use them (continued)
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
IOS · configuration mode
! Assign a block of ports in one go.
interface range GigabitEthernet0/6 - 12
description Staff desks 6-12
switchport mode access
switchport access vlan 10
!
interface range GigabitEthernet0/13 - 18
description Guest desks
switchport mode access
switchport access vlan 20

## Slide 11
CONCEPT
Why switchport mode access matters
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Without it the port is left in dynamic auto mode, which means it will negotiate and may become a trunk if the device on the other end asks for one. On an access port that is both a fault waiting to happen and a security hole — an attacker who can negotiate a trunk can reach every VLAN.
Set it explicitly. It is one line, and it is the difference between a port that does what you configured and a port that does what the far end suggests.

## Slide 12
VERIFY
show vlan brief
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
SW1#
VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Gi0/1, Gi0/2, Gi0/3, Gi0/4
10 Staff active Gi0/5, Gi0/6, Gi0/7, Gi0/8
Gi0/9, Gi0/10, Gi0/11, Gi0/12
20 Guest active Gi0/13, Gi0/14, Gi0/15
30 Voice active
1002 fddi-default act/unsup

## Slide 13
VERIFY
show interfaces GigabitEthernet0/5 switchport
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
SW1#
Name: Gi0/5
Switchport: Enabled
Administrative Mode: static access
Operational Mode: static access
Administrative Trunking Encapsulation: dot1q
Access Mode VLAN: 10 (Staff)
Trunking Native Mode VLAN: 1 (default)
Voice VLAN: none
Notes: This is the view by VLAN. Note that VLAN 30 exists but has no ports — it was created and never used, which is a common and harmless state, and also a common symptom of a half-finished change.

## Slide 14
VERIFY
show mac address-table vlan 10
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
SW1#
Mac Address Table
-------------------------------------------
Vlan Mac Address Type Ports
---- ----------- -------- -----
10 000a.f36e.7712 DYNAMIC Gi0/5
10 0060.5c2b.19a4 DYNAMIC Gi0/7
Notes: This is the view by port, and it is the one to trust when something is odd. Administrative mode is what you configured; operational mode is what the port has actually become. When those two differ, you have found your fault.

## Slide 15
COMMON PITFALLS · Verifying, three ways
Common pitfalls
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
• Assigning a port to a VLAN that does not exist. On many platforms the switch creates it silently; on others the port simply stops forwarding. Either way show vlan brief tells you within seconds.
• Leaving everything in VLAN 1. VLAN 1 cannot be deleted and carries control traffic. Do not put users on it, and do not use it as the management VLAN.
• Forgetting that a VLAN can be shut down. shutdown inside vlan 10 stops the whole VLAN forwarding on that switch while every port still shows as correctly assigned. It is an unusual fault and therefore a nasty one.
Notes: This is the view by evidence: which devices are actually present in the VLAN. If a port is in VLAN 10 and no MAC address ever appears against it, nothing is plugged in or the device is silent — and that distinction is the start of most access-layer troubleshooting.

## Slide 16
COMMON PITFALLS · Verifying, three ways
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
• Deleting a VLAN and leaving ports assigned to it. Those ports become inactive. show vlan brief will not list them at all, which is confusing until you know to look for their absence.

## Slide 17
BREAK & FIX · SYMPTOM
Chapter 8
A new desk cannot reach anything, and the port looks fine.
A user on Gi0/9 has no connectivity. The port is up, the cable is good, and the configuration reads exactly like the working port next to it.
Gi0/9 is not listed against VLAN 10 — nor against any other VLAN.
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2

## Slide 18
BREAK & FIX · YOUR MOVE
Chapter 8
A new desk cannot reach anything, and the port looks fine.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 19
BREAK & FIX · EVIDENCE
Chapter 8
show vlan brief | include Staff|Gi0/9
SW1#
10 Staff active Gi0/5, Gi0/6, Gi0/7, Gi0/8
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 20
BREAK & FIX · EVIDENCE
Chapter 8
show interfaces GigabitEthernet0/9 switchport
SW1#
Name: Gi0/9
Switchport: Enabled
Administrative Mode: static access
Operational Mode: static access
Access Mode VLAN: 15 (Inactive)
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 8
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Notes: The elimination matters as much as the answer.

## Slide 22
BREAK & FIX · DIAGNOSIS
Chapter 8
Why it is doing that
Diagnosis. The port was assigned to VLAN 15, which does not exist on this switch — most likely a typing slip for 10, or a VLAN that was deleted after the port was configured. The word (Inactive) is the whole diagnosis: the port is administratively correct and operationally orphaned.
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2

## Slide 23
BREAK & FIX · THE FIX
Chapter 8
And the lesson
Fix. Either create VLAN 15 if it was meant to exist, or reassign the port: switchport access vlan 10. Confirm with show vlan brief that Gi0/9 now appears in the Staff list, then confirm a MAC address learns against it.
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2

## Slide 24
LAB · PACKET TRACER
Divide one switch into three networks
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Topology. One switch, six PCs — two per VLAN — all in the same IP subnet to begin with.
1. With every port in VLAN 1, confirm all six PCs can ping each other. Record the MAC address table.
2. Create VLANs 10, 20 and 30 with names, and move two PCs into each.
3. Re-test. Which pings now succeed and which fail? Explain each result in terms of broadcast domains, not IP.
4. Run all three verification commands from this chapter and reconcile them.
5. Assign Gi0/11 to VLAN 99, which you have not created. Record what show vlan brief and show interfaces switchport each say.

## Slide 25
LAB · PACKET TRACER
Divide one switch into three networks (continued)
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
1. Enter vlan 20 and type shutdown. Confirm the ports still look correctly assigned while nothing passes. Undo it.
2. Extension. Re-address the PCs so each VLAN is its own subnet. Note that inter-VLAN pings still fail — and that fixing it needs Chapter 10.

## Slide 26
CHECKPOINT 1 of 3
Two PCs are in the same IP subnet, plugged into the same switch, in VLANs 10 and 20. Can they ping each other? Justify your answer at layer 2.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 27
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Two PCs are in the same IP subnet, plugged into the same switch, in VLANs 10 and 20. Can they ping each other? Justify your answer at layer 2.
No. VLANs are separate broadcast domains, so the ARP request never reaches the other host. Sharing an IP subnet is irrelevant at layer 2 — and because both believe the destination is local, neither will send the traffic to a router either. This configuration cannot be fixed by routing; the VLANs must be corrected.

## Slide 28
CHECKPOINT 2 of 3
Which command distinguishes what you configured on a port from what the port has actually become?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 29
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
Which command distinguishes what you configured on a port from what the port has actually become?
show interfaces <int> switchport, which reports both Administrative Mode (what you configured) and Operational Mode (what it actually became).

## Slide 30
CHECKPOINT 3 of 3
A port shows Access Mode VLAN: 15 (Inactive). State the two possible causes.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 31
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
A port shows Access Mode VLAN: 15 (Inactive). State the two possible causes.
Either the VLAN does not exist in the VLAN database, or it exists and is shut down. show vlan brief distinguishes them.

## Slide 32
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 8. VLANs and Access Ports
2.2
• A VLAN is a broadcast domain in software. Learning, flooding and forwarding all become per-VLAN operations.
• A frame never leaves its VLAN without being routed.
• Keep VLAN and subnet aligned one-to-one; mismatches produce faults that look like everything and nothing.
• Always set switchport mode access explicitly, or the port may negotiate a trunk.
• Verify three ways: show vlan brief by VLAN, show interfaces switchport by port, and the MAC table by evidence. Administrative versus operational mode is where faults show.

## Slide 33
Where we got to
• A VLAN is a broadcast domain in software. Learning, flooding and forwarding all become per-VLAN operations.
• A frame never leaves its VLAN without being routed.
• Keep VLAN and subnet aligned one-to-one; mismatches produce faults that look like everything and nothing.
• Always set switchport mode access explicitly, or the port may negotiate a trunk.
NEXT
Chapter 9 — Edge-Host Connectivity: PoE, Voice, APs and IoT