## Slide 1
CCNA 200-301 V2.0
11
EtherChannel and LACP
Part II — Switching and Network Access
EXAM TOPICS
2.1
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 11: EtherChannel and LACP. Blueprint topics: 2.1.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
• Explain why bundling links needs a protocol rather than just more cables, in terms of what spanning tree would otherwise do.
• Configure a layer 2 EtherChannel with LACP, and a layer 3 EtherChannel between routed ports.
• Verify a bundle and read the flags in show etherchannel summary.
• Diagnose the parameter mismatches that stop a bundle forming — the single most common EtherChannel fault.
Notes: EtherChannel and LACP 2.1

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Chapter 10 for trunks and allowed VLAN lists; Chapter 8 for access ports.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
EtherChannel
port channel
LACP
PAgP
active
passive
on
load balancing
bundle
suspended port
layer 3 EtherChannel
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
DEFINITION
EtherChannel
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
An EtherChannel bundles two to eight physical links into one logical interface, the port channel. Spanning tree sees a single link and does not block any member, so all of the bandwidth is usable, and if one member fails the others carry on without a topology change.
Notes: Run two cables between a pair of switches and you do not get twice the bandwidth. You get a loop, and spanning tree (Chapter 12) blocks one of them — so you have paid for two links and can use one.

## Slide 6
Why bundling needs a protocol
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Bundling is not about speed for one conversation — it is about spanning tree seeing one link instead of four, and therefore blocking none of them.

## Slide 7
CONCEPT
Load balancing is per conversation, not per packet
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Frames are distributed across members by hashing fields from the frame — source MAC, destination MAC, source and destination IP, or a combination. Every frame in one conversation hashes the same way, so a conversation always takes one member link.
The consequence catches people out: a single large file transfer between two hosts gets one member’s worth of bandwidth, not the whole bundle. Four 1 Gbps links do not give one server a 4 Gbps transfer. They give you 4 Gbps of aggregate capacity across many conversations, which is a different thing. When somebody complains that a new EtherChannel “did not make the backup faster”, this is why.

## Slide 8
WATCH OUT
Never mix on with a negotiating mode
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
on at one end and active at the other does not form a bundle, and worse, the on end starts forwarding on every member immediately while the far end still treats them as individual links. That is a loop, built by hand. Either both ends negotiate, or both ends are on. LACP active at both ends is the right default.

## Slide 9
CONCEPT
The rule that governs everything: members must match
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Every member port in a bundle, at both ends, must agree on:
• speed and duplex;
• switch mode — all access, or all trunk;
• if trunking: the same native VLAN and the same allowed VLAN list;
• if access: the same access VLAN.
One port that disagrees is suspended and stays out of the bundle. Configure the port channel interface and let the settings inherit downward, rather than configuring each member separately — that is how you avoid the mismatch in the first place.

## Slide 10
CONFIGURE
A two-member LACP trunk bundle, both ends
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
IOS · configuration mode
! Put the physical members into the channel group first. Creating
! the group creates the Port-channel interface automatically.
interface range GigabitEthernet0/1 - 2
description Member of Po1 - uplink to SW2
shutdown
channel-group 1 mode active
no shutdown
exit
!
! Now configure the logical interface. Settings applied here
! propagate to every member, which is what keeps them matching.
interface Port-channel1
description Uplink bundle to SW2
switchport trunk encapsulation dot1q
switchport mode trunk
switchport trunk native vlan 999
switchport trunk allowed vlan 10,20,30
!
! Hash on both source and destination IP for a better spread than
! the default source-MAC-only on many platforms.
port-channel load-balance src-dst-ip

## Slide 11
VERIFY
show etherchannel summary
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
SW1#
Flags: D - down P - bundled in port-channel
I - stand-alone s - suspended
H - Hot-standby (LACP only)
R - Layer3 S - Layer2
U - in use f - failed to allocate aggregator
M - not in use, minimum links not met
u - unsuitable for bundling
w - waiting to be aggregated
d - default port
Number of channel-groups in use: 1
Number of aggregators: 1
Group Port-channel Protocol Ports
------+-------------+-----------+-----------------------------------------------
1 Po1(SU) LACP Gi0/1(P) Gi0/2(P)

## Slide 12
CONFIGURE
A routed bundle
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
IOS · configuration mode
interface Port-channel2
description Routed bundle to Core2
! no switchport makes this a routed interface -- do it BEFORE
! adding an address, or the address command is rejected.
no switchport
ip address 10.255.0.1 255.255.255.252
!
interface range GigabitEthernet0/23 - 24
no switchport
channel-group 2 mode active
no shutdown
Notes: Read the flags. Po1(SU) means layer Switched and Used — healthy. Each member showing (P) is bundled. The ones to worry about are (I) stand-alone, (s) suspended and (D) down. Between two multilayer switches you may want the bundle routed rather than switched.

## Slide 13
COMMON PITFALLS · A layer 3 EtherChannel
Common pitfalls
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
• Passive–passive or auto–auto. Neither end initiates and no bundle forms. The ports stay up as individual links, which spanning tree then blocks — so you get a working network and half the bandwidth you paid for.
• Mismatched allowed VLAN lists. A favourite: the bundle forms, one VLAN is missing from one end, and only that VLAN breaks.
• Configuring members individually. Configure interface Port-channel1; let it inherit.
• Adding no switchport after the IP address. On a layer 3 bundle the order matters.
• Expecting one flow to use the whole bundle. It never will.

## Slide 14
BREAK & FIX · SYMPTOM
Chapter 11
The bundle formed with one member instead of four.
A new four-link bundle shows only Gi0/1 bundled; the other three are suspended.
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1

## Slide 15
BREAK & FIX · YOUR MOVE
Chapter 11
The bundle formed with one member instead of four.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 16
BREAK & FIX · EVIDENCE
Chapter 11
show etherchannel summary | begin Group
SW1#
Group Port-channel Protocol Ports
------+-------------+-----------+-----------------------------------------------
1 Po1(SU) LACP Gi0/1(P) Gi0/2(s) Gi0/3(s) Gi0/4(s)
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 17
BREAK & FIX · EVIDENCE
Chapter 11
show interfaces GigabitEthernet0/2 switchport | include Access|Trunking|Mode
SW1#
Administrative Mode: static access
Operational Mode: static access
Access Mode VLAN: 1 (default)
Trunking Native Mode VLAN: 1 (default)
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 18
BREAK & FIX · YOUR MOVE
Chapter 11
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Notes: The elimination matters as much as the answer.

## Slide 19
BREAK & FIX · DIAGNOSIS
Chapter 11
Why it is doing that
Diagnosis. Gi0/1 was configured as a trunk before being added to the group, and the others were left as access ports in VLAN 1. Members must agree on switch mode, so the three that disagree with the first are suspended. The (s) flag is the whole diagnosis; the second command identifies which parameter differs.
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1

## Slide 20
BREAK & FIX · THE FIX
Chapter 11
And the lesson
Fix. Do not fix the members one by one — that invites the same fault again. Apply the trunk configuration to interface Port-channel1 and let it propagate, then confirm all four show (P). If a member still refuses, compare speed and duplex next.
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1

## Slide 21
LAB · PACKET TRACER
Bundle four links and break them
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Topology. Two switches joined by four Ethernet links; one PC on each.
1. Cable all four links with no EtherChannel configured. Run show spanning-tree and record how many are forwarding and how many are blocking. Explain the result.
2. Configure Po1 with LACP active at both ends, trunked, native VLAN 999, allowed 10 and 20. Verify with show etherchannel summary.
3. Re-run show spanning-tree. How many logical links does it now see?
4. Shut one member. Confirm traffic continues and that spanning tree does not reconverge.
5. Set one member’s access VLAN to 20 by configuring the physical port directly. Record the flag it earns and explain it.
6. Change one end to passive while the other is also passive. Record what the bundle does.

## Slide 22
LAB · PACKET TRACER
Bundle four links and break them (continued)
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
1. Extension. Build a layer 3 EtherChannel between two multilayer switches with a /30 and prove you can ping across it.

## Slide 23
CHECKPOINT 1 of 3
Two switches are configured channel-group 1 mode passive at both ends. What happens, and what does spanning tree do about it?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 24
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Two switches are configured channel-group 1 mode passive at both ends. What happens, and what does spanning tree do about it?
No channel forms — both ends wait to be asked. The individual links stay up, so spanning tree sees parallel paths and blocks all but one. The result is a working but single-link connection, which is why the symptom is “it works, but it is not four gigabits”.

## Slide 25
CHECKPOINT 2 of 3
A member port shows (s). Name three parameters you would compare and the command that shows them.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 26
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
A member port shows (s). Name three parameters you would compare and the command that shows them.
(s) is suspended: a parameter mismatch. Compare speed, duplex, and the allowed VLAN list and native VLAN on each member. show interfaces <int> switchport and show interfaces status show them.

## Slide 27
CHECKPOINT 3 of 3
Why does adding a second member to a bundle not double the speed of a single file copy?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 28
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
Why does adding a second member to a bundle not double the speed of a single file copy?
Because load balancing is per-flow, not per-packet. A hash of addresses and ports selects one member for a conversation, and one file copy is one conversation. Bundling raises aggregate capacity across many flows, not the speed of any single one.

## Slide 29
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 11. EtherChannel and LACP
2.1
• An EtherChannel makes several links look like one, so spanning tree blocks none of them.
• LACP active at both ends is the sensible default. Passive–passive and auto–auto form nothing; on mixed with a negotiating mode builds a loop.
• Members must match on speed, duplex, switch mode, native VLAN and allowed list. Configure the port channel interface and let it inherit.
• Read show etherchannel summary by its flags: (P) bundled, (s) suspended for a mismatch, (I) stand-alone, (D) down.
• Load balancing is per conversation. One flow uses one member.

## Slide 30
Where we got to
• An EtherChannel makes several links look like one, so spanning tree blocks none of them.
• LACP active at both ends is the sensible default. Passive–passive and auto–auto form nothing; on mixed with a negotiating mode builds a loop.
• Members must match on speed, duplex, switch mode, native VLAN and allowed list. Configure the port channel interface and let it inherit.
• Read show etherchannel summary by its flags: (P) bundled, (s) suspended for a mismatch, (I) stand-alone, (D) down.
NEXT
Chapter 12 — Rapid PVST+ and the Protection Features