## Slide 1
CCNA 200-301 V2.0
13
CDP, LLDP and Documenting a Network
Part II — Switching and Network Access
EXAM TOPICS
2.3
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 13: CDP, LLDP and Documenting a Network. Blueprint topics: 2.3.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
• Explain what discovery protocols advertise and what they cannot tell you.
• Configure CDP and LLDP, including disabling them where they should not run.
• Validate a network diagram against the devices themselves, which is precisely what topic 2.3 asks.
• Use discovery output to find a mismatch — native VLAN, duplex or an undocumented device.
Notes: CDP, LLDP and Documenting a Network 2.3

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Chapter 10 for native VLANs, Chapter 2 for duplex, Chapter 7 for filtering output.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
CDP
LLDP
LLDP-MED
neighbour
holdtime
advertisement
capability code
platform
local interface
port ID
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
The verb here is validate
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
This is what the blueprint actually asks for
Topic 2.3 is “validate the accuracy of network documentation using CDP and LLDP”. It is not asking you to describe the protocols. It is asking you to take a diagram that claims SW1 Gi0/1 connects to R1 Gi0/0, and prove from the devices whether that is true. Expect to be shown a diagram and some show cdp neighbors output that contradicts it.

## Slide 6
DEFINITION
What a neighbour advertisement carries
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Device identifier, the local and remote interface, the platform and capabilities, and depending on the protocol and platform: IP address, IOS version, native VLAN, duplex and power requirements.
Crucially, a neighbour is directly connected at layer 2. A device two switches away never appears. That is exactly what makes the output usable as evidence of physical cabling.
Notes: Run both in a mixed estate: CDP for the Cisco gear, LLDP for everything else.

## Slide 7
VERIFY
show cdp neighbors
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
SW1#
Capability Codes: R - Router, T - Trans Bridge, B - Source Route Bridge
S - Switch, H - Host, I - IGMP, r - Repeater, P - Phone
Device ID Local Intrfce Holdtme Capability Platform Port ID
R1 Gig 0/1 142 R S I C1111 Gig 0/0/0
SW2 Gig 0/2 167 S I WS-C2960 Gig 0/1
SW3 Gig 0/3 121 S I WS-C2960 Gig 0/24
AP-EAST Gig 0/10 155 H AIR-AP2802 Gig 0

## Slide 8
VERIFY
show cdp neighbors detail
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
SW1#
-------------------------
Device ID: R1
Entry address(es):
IP address: 10.0.0.1
Platform: Cisco C1111-4P, Capabilities: Router Switch IGMP
Interface: GigabitEthernet0/1, Port ID (outgoing port): GigabitEthernet0/0/0
Holdtime : 142 sec
Version :
Cisco IOS XE Software, Version 17.09.04a
Duplex: full
Native VLAN: 999
Notes: Read it as four columns that matter: Device ID (who), Local Intrfce (my port), Port ID (their port), Capability (what kind of device). Those four are the cabling diagram, taken from the devices rather than from a drawing somebody updated in 2019.

## Slide 9
CONFIGURE
Running both protocols, and switching them off where they do not belong
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
IOS · configuration mode
! CDP is on by default; LLDP is not.
lldp run
!
! Turn CDP off on a port facing anything you do not control.
! Advertising your platform and IOS version to a guest network,
! an ISP handoff or an untrusted uplink is free reconnaissance.
interface GigabitEthernet0/24
description ISP handoff - no discovery
no cdp enable
no lldp transmit
no lldp receive
!
! Globally, if policy demands it:
! no cdp run
Notes: detail adds the IP address, the software version, the duplex and the native VLAN — which is how a native VLAN mismatch gets caught before it causes a security incident.

## Slide 10
WATCH OUT
Do not disable it everywhere on principle
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
There is a reflex to switch CDP off across the estate “for security”. Weigh it properly: internally, CDP and LLDP are how you validate cabling, how phones learn their voice VLAN (Chapter 9), and how native VLAN and duplex mismatches are detected. Disable them on untrusted edges — ISP links, guest ports, DMZ segments — and leave them running inside.

## Slide 11
WORKED EXAMPLE
The diagram says one thing, the switch says another
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
The documentation claims:
• SW1 Gi0/2 → SW2 Gi0/1
• SW1 Gi0/3 → SW3 Gi0/1
The output above shows Gi0/2 to SW2 Gi0/1 — correct — but Gi0/3 to SW3 Gig 0/24, not Gi0/1.
What that means in practice. Somebody re-patched SW3 and did not update the diagram. It may be harmless. It may not: if SW3 Gi0/24 is configured as an access port while Gi0/1 was the trunk, the uplink is carrying one VLAN instead of all of them, and the fault will surface later as “the new VLAN does not work on the third floor”.
What to do. Correct the diagram, then check that the port actually in use carries the configuration the design intended. Discovery output tells you what is plugged in; it does not tell you whether the port is configured correctly. That is a second check.

## Slide 12
COMMON PITFALLS · Validating a diagram
Common pitfalls
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
• Expecting to see non-adjacent devices. Neighbours are one hop. A device that does not appear may simply be further away.
• Concluding a device is absent when CDP is off. A non-Cisco switch, or one with CDP disabled, is invisible to CDP and may still be there. Cross-check with LLDP and the MAC address table.
• Trusting stale entries. Holdtime counts down from 180 s. An entry can persist for three minutes after a device is unplugged.
• Forgetting lldp run. Without it, show lldp neighbors is empty and you may wrongly conclude nothing is connected.

## Slide 13
COMMON PITFALLS · Validating a diagram
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
• Reading the port columns backwards. Local Intrfce is yours; Port ID is theirs.

## Slide 14
BREAK & FIX · SYMPTOM
Chapter 13
An undocumented switch appears in the discovery table.
An audit of SW1 shows a neighbour that is not on any diagram:
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3

## Slide 15
BREAK & FIX · YOUR MOVE
Chapter 13
An undocumented switch appears in the discovery table.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 16
BREAK & FIX · EVIDENCE
Chapter 13
show cdp neighbors GigabitEthernet0/14 detail
SW1#
-------------------------
Device ID: Switch
Entry address(es):
Platform: cisco WS-C2960-8TC-L, Capabilities: Switch IGMP
Interface: GigabitEthernet0/14, Port ID (outgoing port): FastEthernet0/1
Holdtime : 131 sec
Version :
Cisco IOS Software, C2960 Software, Version 12.2(55)SE
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 17
BREAK & FIX · YOUR MOVE
Chapter 13
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Notes: The elimination matters as much as the answer.

## Slide 18
BREAK & FIX · DIAGNOSIS
Chapter 13
Why it is doing that
Diagnosis. An eight-port switch with the default hostname Switch, no management address, and a decade-old IOS version, connected to an access port — somebody has plugged a desk switch into a wall socket to get more ports. It is unmanaged, it participates in spanning tree, and it can influence the root election (Chapter 12).
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3

## Slide 19
BREAK & FIX · THE FIX
Chapter 13
And the lesson
Fix. Short term: confirm what is downstream of it before unplugging anything, because there are probably users behind it. Long term, this is exactly what spanning-tree bpduguard on access ports is for — with it configured, the port would have errdisabled the moment the switch was connected and the problem would have announced itself instead of being found in an audit months later.
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3

## Slide 20
LAB · PACKET TRACER
Draw the network from the devices
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Topology. Four switches and a router, cabled by your instructor or a partner without telling you how, plus a deliberately wrong diagram.
1. Using only show cdp neighbors from each device, draw the physical topology. Do not look at the cables.
2. Compare your drawing with the supplied diagram and list every discrepancy.
3. Run show cdp neighbors detail on one link and record the IOS version, duplex and native VLAN of the neighbour.
4. Create a native VLAN mismatch on one trunk and find the resulting log message.
5. Enable lldp run everywhere and compare show lldp neighbors with the CDP view. Account for any difference.
6. Disable CDP on one port and confirm the neighbour disappears — noting how long it takes.

## Slide 21
LAB · PACKET TRACER
Draw the network from the devices (continued)
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
1. Extension. Write a short procedure a junior technician could follow to validate a patching change using discovery output alone.

## Slide 22
CHECKPOINT 1 of 3
show cdp neighbors lists a device you know is three switches away. What must be true?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 23
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
show cdp neighbors lists a device you know is three switches away. What must be true?
There is no switch between you and it that processes CDP — so the intervening devices are hubs, media converters, or unmanaged switches that pass the frames through. Neighbour discovery only shows directly connected devices, so a distant one appearing means the path is not what the diagram says.

## Slide 24
CHECKPOINT 2 of 3
You unplug a device and it still appears in the table. Why, and for how long?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 25
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
You unplug a device and it still appears in the table. Why, and for how long?
Because entries persist for the advertised holdtime, 180 seconds by default for CDP. Until it expires, the table describes a neighbour that is no longer there.

## Slide 26
CHECKPOINT 3 of 3
Which single command would tell you a neighbour’s IOS version and native VLAN?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 27
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
Which single command would tell you a neighbour’s IOS version and native VLAN?
show cdp neighbors detail. The summary form gives neither.

## Slide 28
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
• CDP is Cisco and on by default; LLDP is open and off by default. Run both in a mixed estate.
• Neighbours are directly connected only — which is what makes the output evidence of cabling.
• Local Intrfce is your port, Port ID is theirs. Those two columns plus the device name are the diagram.
• detail adds IP, version, duplex and native VLAN, and catches mismatches before they cause incidents.

## Slide 29
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 13. CDP, LLDP and Documenting a Network
2.3
• Disable discovery on untrusted edges, not everywhere. Holdtime means entries persist for minutes after a device is removed.

## Slide 30
Where we got to
• CDP is Cisco and on by default; LLDP is open and off by default. Run both in a mixed estate.
• Neighbours are directly connected only — which is what makes the output evidence of cabling.
• Local Intrfce is your port, Port ID is theirs. Those two columns plus the device name are the diagram.
• detail adds IP, version, duplex and native VLAN, and catches mismatches before they cause incidents.
NEXT
Chapter 14 — Troubleshooting Layer 2