## Slide 1
CCNA 200-301 V2.0
16
Static Routing, IPv4 and IPv6
Part III — IP Routing
EXAM TOPICS
3.2
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 16: Static Routing, IPv4 and IPv6. Blueprint topics: 3.2.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
• Configure the four kinds of static route the blueprint names: default, network, host and floating.
• Choose correctly between a next-hop address, an exit interface, and both — a choice that matters more than it looks.
• Configure static routing for IPv6 alongside IPv4.
• Troubleshoot a static route that is absent from the table, or present and not working.
Notes: Static Routing, IPv4 and IPv6 3.2

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Chapter 15 — longest prefix match and administrative distance are assumed throughout. Chapter 5 for the v6 half.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
static route
default route
network route
host route
floating static
next hop
exit interface
fully specified route
recursive lookup
gateway of last resort
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
The verb is troubleshoot, and the sub-topics are a checklist
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
This is what the blueprint actually asks for
Topic 3.2 is “troubleshoot IPv4 and IPv6 static routing” and then lists exactly four kinds: default route, network route, host route, floating static. Expect to be shown a table and a symptom rather than asked to recite syntax — but you cannot diagnose what you cannot write, so learn the syntax first.

## Slide 6
CONFIGURE
All four, on IPv4
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
IOS · configuration mode
! Network route -- reach 10.9.9.0/24 through the neighbour at 10.255.0.2.
ip route 10.9.9.0 255.255.255.0 10.255.0.2
!
! Default route -- the gateway of last resort.
ip route 0.0.0.0 0.0.0.0 203.0.113.1
!
! Host route -- this one server goes a different way.
ip route 10.9.9.50 255.255.255.255 10.255.1.2
!
! Floating static -- distance 200 keeps it out of the table while
! OSPF (distance 110) has a route. It appears only if OSPF loses one.
ip route 10.1.0.0 255.255.0.0 10.255.2.2 200

## Slide 7
CONCEPT
Why the host route wins
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
All four routes above can match 10.9.9.50. The /32 host route is the longest prefix, so it is used — ahead of the /24, ahead of the default. Longest prefix match decides before distance is even considered (Chapter 15).

## Slide 8
WATCH OUT
Exit-interface-only routes on Ethernet are a trap
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Ethernet is multi-access: many devices share the segment. A route that names only an exit interface tells the router “send it out here” without saying to whom, so the router must ARP for every destination address it forwards, hoping something answers. On a link where proxy ARP is enabled it appears to work; where it is not, it silently fails; and either way the ARP table fills with entries that should not exist.
On a serial point-to-point link there is only one possible recipient, so the form is harmless. On Ethernet, always give the next hop — alone or fully specified.
Notes: This is the choice that produces the most subtle static-routing faults.

## Slide 9
VERIFY
show ip route static
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
R1#
10.0.0.0/8 is variably subnetted, 5 subnets, 3 masks
S 10.1.0.0/16 [200/0] via 10.255.2.2
S 10.9.9.0/24 [1/0] via 10.255.0.2
S 10.9.9.50/32 [1/0] via 10.255.1.2
S* 0.0.0.0/0 [1/0] via 203.0.113.1

## Slide 10
CONFIGURE
IPv6 static routes
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
IOS · configuration mode
ipv6 unicast-routing
!
! Network route via a global next-hop address.
ipv6 route 2001:db8:acad:20::/64 2001:db8:acad:99::2
!
! Default route.
ipv6 route ::/0 2001:db8:acad:99::2
!
! Host route.
ipv6 route 2001:db8:acad:20::50/128 2001:db8:acad:99::2
!
! Floating static.
ipv6 route 2001:db8:acad:30::/64 2001:db8:acad:98::2 200
!
! Via a LINK-LOCAL next hop -- the exit interface is mandatory,
! because fe80:: addresses are only unique per link and the router
! has no way to know which interface you mean.
ipv6 route 2001:db8:acad:40::/64 GigabitEthernet0/1 fe80::2
Notes: Note the floating static at [200/0] is shown here — meaning OSPF currently has no route for 10.1.0.0/16, so the backup has taken over. When OSPF is healthy that line is absent from the table entirely. The syntax mirrors IPv4, with one wrinkle worth learning.

## Slide 11
CONCEPT
Why link-local next hops need the interface
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
A link-local address is valid on one link only, and the same fe80::2 may legitimately exist on three different interfaces of the same router. Naming the interface removes the ambiguity. IOS rejects a link-local next hop without one.
This matters because routing protocols, including OSPFv3, use link-local addresses as their next hop — so link-local next hops are the normal case in IPv6, not an oddity.

## Slide 12
VERIFY
show ipv6 route static
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
R1#
IPv6 Routing Table - default - 7 entries
Codes: C - Connected, L - Local, S - Static, U - Per-user Static route
S ::/0 [1/0]
via 2001:DB8:ACAD:99::2
S 2001:DB8:ACAD:20::/64 [1/0]
via 2001:DB8:ACAD:99::2
S 2001:DB8:ACAD:40::/64 [1/0]
via FE80::2, GigabitEthernet0/1

## Slide 13
WORKED EXAMPLE
A backup path that only activates on failure
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
R1 reaches 10.1.0.0/16 through OSPF over its primary link, and has a slow secondary link to the same destination.
• OSPF’s route has distance 110.
• Configure the backup with a distance above 110: ip route 10.1.0.0 255.255.0.0 10.255.2.2 200.
• While OSPF is up, only the OSPF route is installed. show ip route shows O 10.1.0.0/16 [110/20] and no static entry at all.
• The primary link fails. OSPF withdraws its route. The static route, now the only candidate, is installed as S 10.1.0.0/16 [200/0].

## Slide 14
WORKED EXAMPLE
A backup path that only activates on failure (continued)
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
• The primary returns. OSPF’s route at 110 beats 200 and displaces the static again.
The number 200 is not magic — it just has to exceed the distance of whatever it is backing up. Back up a static route (distance 1) and any value from 2 upwards will do.

## Slide 15
COMMON PITFALLS · Floating statics, properly
Common pitfalls
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
• A floating static with too low a distance. Set it below the dynamic protocol’s and it takes over permanently, which is the opposite of a backup.
• Exit-interface-only routes on Ethernet. See the warning above.
• Forgetting the reverse route. A static route is one-directional. Both ends need one, and forgetting this is the commonest static-routing fault of all.
• A next hop that is not directly reachable. The route will not be installed at all; the router silently discards it. show ip route simply has no entry, which looks like you never typed it.
• Omitting the interface on an IPv6 link-local next hop. Rejected outright.

## Slide 16
BREAK & FIX · SYMPTOM
Chapter 16
The static route was typed and it is not in the table.
An engineer configures ip route 10.9.9.0 255.255.255.0 10.255.0.2 and show ip route static shows nothing. No error was displayed when the command was entered.
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2

## Slide 17
BREAK & FIX · YOUR MOVE
Chapter 16
The static route was typed and it is not in the table.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 18
BREAK & FIX · EVIDENCE
Chapter 16
show ip route 10.255.0.2
R1#
% Network not in table
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 19
BREAK & FIX · EVIDENCE
Chapter 16
show ip interface brief | include Gigabit
R1#
GigabitEthernet0/1 10.255.0.1 YES manual administratively down down
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 20
BREAK & FIX · YOUR MOVE
Chapter 16
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Notes: The elimination matters as much as the answer.

## Slide 21
BREAK & FIX · DIAGNOSIS
Chapter 16
Why it is doing that
Diagnosis. A static route is only installed if the router can resolve its next hop. 10.255.0.2 is not reachable — there is no connected subnet covering it — so the route is accepted into the configuration and never enters the routing table. This is why the command produced no error: the syntax was perfect and the topology was not.
Check the interface that should reach it:
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2

## Slide 22
BREAK & FIX · THE FIX
Chapter 16
And the lesson
Fix. The interface is shut. no shutdown on Gi0/1, and the connected route for 10.255.0.0/30 appears, the next hop resolves, and the static route installs itself immediately. Confirm with show ip route static — and remember the general rule: a static route missing from the table is nearly always an unreachable next hop, not a typing error.
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2

## Slide 23
LAB · PACKET TRACER
Four routes, one failure
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Topology. Three routers — R1, R2, R3 — with R1 connected to R2 by a fast link and to R3 by a slow one, and R2 and R3 both connected to a LAN at the far side. A LAN on R1.
1. Address everything. Confirm connected routes on all three and that neighbours ping.
2. On R1, add a network route to the far LAN via R2. Test from the R1 LAN — it will fail. Diagnose why, then add the reverse route and re-test.
3. Add a default route on R2 and R3 pointing back at R1. Note the S* and the gateway of last resort line.
4. Add a host route on R1 for one server in the far LAN, via R3. Prove with show ip route <address> that it is preferred over the network route.
5. Add a floating static via R3 for the far LAN with distance 5. Confirm it is not in the table.

## Slide 24
LAB · PACKET TRACER
Four routes, one failure (continued)
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
1. Shut R1’s link to R2. Confirm the floating static appears and traffic still flows. Restore the link and watch it withdraw.
2. Extension. Repeat steps 2 and 5 for IPv6, including one route via a link-local next hop.

## Slide 25
CHECKPOINT 1 of 3
You configure a static route and it never appears in the table, with no error message. What is the most likely cause and which command confirms it?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 26
ANSWER
Checkpoint 1 of 3
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
You configure a static route and it never appears in the table, with no error message. What is the most likely cause and which command confirms it?
The next hop is not reachable. A router will not install a static route whose next-hop address it cannot resolve to an interface. Confirm with show ip route <next-hop> — if that returns nothing, the static route has nowhere to point.

## Slide 27
CHECKPOINT 2 of 3
A floating static backing up an OSPF route is configured with distance 100. What will happen, and why is it wrong?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 28
ANSWER
Checkpoint 2 of 3
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
A floating static backing up an OSPF route is configured with distance 100. What will happen, and why is it wrong?
Nothing will happen: 100 is lower than OSPF’s 110, so the “backup” route wins permanently and the OSPF route is never installed. A floating static must have a distance higher than the protocol it backs up.

## Slide 29
CHECKPOINT 3 of 3
Why must an IPv6 static route using a link-local next hop also name an exit interface?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 30
ANSWER
Checkpoint 3 of 3
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
Why must an IPv6 static route using a link-local next hop also name an exit interface?
Because a link-local address is only unique within a link, and a router with several interfaces has no way to tell which one fe80::2 refers to. Naming the exit interface removes the ambiguity.

## Slide 31
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 16. Static Routing, IPv4 and IPv6
3.2
• Four kinds: network, default (0.0.0.0/0), host (/32) and floating. The host route wins on longest prefix match.
• Give a next hop on Ethernet — alone or fully specified. Exit-interface only belongs on point-to-point links.
• IPv6 mirrors IPv4, but a link-local next hop must name the exit interface.
• A floating static needs a distance above whatever it backs up: over 110 for OSPF, over 1 for another static.
• A static route absent from the table almost always means an unresolvable next hop. Routes are one-way; configure both ends.

## Slide 32
Where we got to
• Four kinds: network, default (0.0.0.0/0), host (/32) and floating. The host route wins on longest prefix match.
• Give a next hop on Ethernet — alone or fully specified. Exit-interface only belongs on point-to-point links.
• IPv6 mirrors IPv4, but a link-local next hop must name the exit interface.
• A floating static needs a distance above whatever it backs up: over 110 for OSPF, over 1 for another static.
NEXT
Chapter 17 — OSPFv2, Single Area