## Slide 1
CCNA 200-301 V2.0
23
Device Access, AAA and Secure File Transfer
Part IV — Network Services and Security
EXAM TOPICS
4.1
4.2
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 23: Device Access, AAA and Secure File Transfer. Blueprint topics: 4.1, 4.2.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• Configure local usernames, enable secrets and SSH-only access to the console and VTY lines.
• Configure a router or switch as an AAA client against TACACS+ and against RADIUS, with a local fallback that cannot lock you out.
• Compare TACACS+ and RADIUS and choose correctly between them.
• Manage configuration and image files over SCP and SFTP, and say why v2.0 replaced TFTP with them.
Notes: Device Access, AAA and Secure File Transfer 4.14.2

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Chapter 7 for line configuration and privilege levels. Chapter 21 for ip domain name, which SSH key generation requires. Chapter 6 for the difference between TCP and UDP, which is one of the real distinctions between TACACS+ and RADIUS.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
AAA
authentication
authorization
accounting
TACACS+
RADIUS
method list
fallback
enable secret
SCP
SFTP
privilege level
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
Two topics, one chapter, and a v2.0 change worth noticing
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
This is what the blueprint actually asks for
Topic 4.1 is configure network devices with local usernames and as an AAA client (TACACS+ and RADIUS) for management. Topic 4.2 is manage device configuration and software files using secure file transfer operations with SFTP/SCP.
They sit together because they are the same job: getting onto a device safely, and moving files onto it safely. And 4.2 is a genuine v2.0 change — v1.1 examined TFTP. TFTP is UDP, has no authentication of any kind, and sends everything in clear text. It has been removed from the blueprint and replaced by two protocols that fix all three problems. If a practice question offers TFTP as the secure answer, the question predates your exam.

## Slide 6
CONFIGURE
Baseline secure access
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
hostname CAMPUS-SW1
!
! A domain name is required before RSA keys can be generated: the key
! is named host.domain.
ip domain name campus.example.edu
!
! scrypt is type 9. Use it where the platform offers it. Never use
! "username ... password", which stores type 0 or type 7.
username netadmin privilege 15 algorithm-type scrypt secret S0me-Long-Passphrase
username helpdesk privilege 1 algorithm-type scrypt secret An0ther-Passphrase
!
enable algorithm-type scrypt secret Enable-Passphrase-Here
!
! 2048 is the practical minimum; below 768 the device will refuse to
! run SSH version 2 at all.
crypto key generate rsa modulus 2048
ip ssh version 2
ip ssh time-out 60
ip ssh authentication-retries 3
Notes: Before any server is involved, get the device itself right. Everything in this section should be on every device you build, including the ones that later use AAA — because AAA servers fail, and this is what you fall back to.

## Slide 7
CONFIGURE
Baseline secure access (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
!
line console 0
login local
exec-timeout 10 0
logging synchronous
!
line vty 0 15
login local
transport input ssh
exec-timeout 10 0

## Slide 8
WATCH OUT
transport input ssh is the line that matters
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Generating keys and enabling SSH does not disable Telnet. Until you say transport input ssh, the device still accepts plain-text logins on port 23, and an auditor will find it. The default on many platforms is transport input all.
The reverse mistake is worse: typing transport input ssh before the keys exist locks you out of a remote device completely. Generate keys first, prove SSH works from a second window, then restrict the transport.

## Slide 9
CONCEPT
Password types, and why service password-encryption is not enough
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• Type 0 — plain text. Visible in the configuration.
• Type 7 — Cisco’s reversible obfuscation, applied by service password-encryption. It is trivially reversed by tools that have existed for decades. It stops shoulder-surfing and nothing else.

## Slide 10
CONCEPT
Password types, and why service password-encryption is not enough (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• Type 5 — salted MD5. A real hash, but MD5 is old.
• Type 8 (PBKDF2) and type 9 (scrypt) — current. Use algorithm-type sha256 or algorithm-type scrypt.
So service password-encryption is still worth enabling — it covers things that can only be type 7, such as line passwords and TACACS+ keys — but it is not a substitute for storing user passwords as type 8 or 9.
enable secret is hashed; enable password is not. If both exist, the secret wins and the password is dead configuration that leaks a credential. Delete it.

## Slide 11
DEFINITION
AAA
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Authentication — who are you? Authorization — what are you allowed to do? Accounting — what did you actually do? Three distinct questions, answered by method lists that a device consults in order.

## Slide 12
WATCH OUT
The distinction that saves you and the one that locks you out
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
If the TACACS+ server answers “no, wrong password”, that is an answer. The device stops there and rejects you — it does not fall through to the local database. Fallback happens only when the server does not respond at all.
This is correct behaviour and it surprises people. A fallback method is protection against a dead server, not against a forgotten password.
Notes: A method list is an ordered list of ways to answer one of those questions. The device tries them left to right and moves on only when a method is unreachable, not when it returns a refusal.

## Slide 13
CONFIGURE
AAA against TACACS+, with a local fallback
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
aaa new-model
!
! The server. This is the IOS 15 / IOS XE syntax; older configurations
! used a single "tacacs-server host" line.
tacacs server TAC1
address ipv4 10.0.0.20
key SharedSecretHere
!
tacacs server TAC2
address ipv4 10.0.0.21
key SharedSecretHere
!
aaa group server tacacs+ TACGROUP
server name TAC1
server name TAC2
!
! Authentication: try the group, then the local database if no server
! answers. The trailing "local" is not optional in any network you
! intend to keep working.
aaa authentication login default group TACGROUP local
aaa authentication enable default group TACGROUP enable

## Slide 14
CONFIGURE
AAA against TACACS+, with a local fallback (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
!
! Authorization: what privilege level does this user get on login?
aaa authorization exec default group TACGROUP local if-authenticated
!
! Accounting: a record of every session and every command at level 15.
aaa accounting exec default start-stop group TACGROUP
aaa accounting commands 15 default start-stop group TACGROUP
!
! Source the packets from a stable address so the server's client
! entry always matches, whichever interface the traffic leaves by.
ip tacacs source-interface Loopback0

## Slide 15
CONFIGURE
The same device as a RADIUS client
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
radius server RAD1
address ipv4 10.0.0.30 auth-port 1812 acct-port 1813
key AnotherSharedSecret
!
aaa group server radius RADGROUP
server name RAD1
!
aaa authentication login default group RADGROUP local
aaa authorization exec default group RADGROUP local
ip radius source-interface Loopback0

## Slide 16
VERIFY
show aaa servers | include host|state
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
CAMPUS-SW1#
RADIUS: id 1, priority 1, host 10.0.0.30, auth-port 1812, acct-port 1813
State: current UP, duration 43112s, previous duration 0s

## Slide 17
ON THE EXAM
The one-sentence version
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
This is what the blueprint actually asks for
TACACS+ manages administrators; RADIUS manages users. If a question is about who may configure a switch, the answer is TACACS+. If it is about a laptop authenticating onto a wireless network, the answer is RADIUS.
Two supporting facts worth memorising because they are asked directly: TACACS+ is TCP 49 and encrypts the whole payload; RADIUS is UDP and encrypts only the password.
Notes: Both are AAA protocols and they are not interchangeable. This table is examinable more or less as it stands.

## Slide 18
CONFIGURE
Enabling the SCP server
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
! SCP will not start without all three of these. The authorization
! line in particular is easy to miss, and its absence produces a
! connection that authenticates and then refuses every transfer.
aaa new-model
aaa authentication login default local
aaa authorization exec default local
!
ip scp server enable
Notes: TFTP has no user authentication, no encryption, and runs over UDP with no integrity protection beyond a checksum. Anyone who can reach the server can read any file whose name they can guess, and a configuration file in flight is readable by anyone on the path — including the shared secrets in it. That is the case for its removal from the blueprint. SCP runs over SSH, so it inherits SSH’s authentication and encryption. The device can act as an SCP server, letting you pull and push files from a workstation.

## Slide 19
VERIFY
scp netadmin@10.0.0.1:running-config ./sw1-backup.cfg
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Linux or macOS
netadmin@10.0.0.1's password:
running-config 100% 8241 1.2MB/s 00:00
Notes: With that in place, from a workstation:

## Slide 20
VERIFY
copy sftp: flash:
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
CAMPUS-SW1#
Address or name of remote host []? 10.0.0.40
Source username [netadmin]? images
Source filename []? cat9k_iosxe.17.12.04.SPA.bin
Destination filename [cat9k_iosxe.17.12.04.SPA.bin]?
Accessing sftp://images@10.0.0.40/cat9k_iosxe.17.12.04.SPA.bin...
Loading file ! [OK - 1103237120 bytes]
1103237120 bytes copied in 412.338 secs (2675281 bytes/sec)
Notes: IOS is an SFTP client but not an SFTP server. So the direction of travel is the device fetching from, or sending to, a server you run.

## Slide 21
CONFIGURE
Backing the configuration up on a schedule
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
IOS · configuration mode
! One-off, non-interactive form. The password appears on the command
! line, so prefer key-based SCP where the platform supports it.
! do copy running-config scp://netadmin@10.0.0.40/CAMPUS-SW1.cfg
!
! Automatic archive: a copy every time someone saves, kept off-box.
archive
path scp://netadmin@10.0.0.40/archive/$h-
write-memory
maximum 14

## Slide 22
CONCEPT
Verify the image before you reload onto it
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
A transfer that reports [OK] has moved the bytes it was given. It has not told you the file is the image Cisco shipped. Before reloading:
• verify /md5 flash:cat9k_iosxe.17.12.04.SPA.bin and compare against the hash published with the download.
• show flash: to confirm the size matches.
• Confirm free space before the copy, not after — a partial copy that filled flash can leave a device unable to boot.

## Slide 23
COMMON PITFALLS · SFTP — the device as a client
Common pitfalls
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• aaa authentication login default group TACGROUP with no local. When the server is unreachable, nobody can log in — not even at the console. This is the classic lock-out.
• Testing AAA by closing your session. Always open a second session and prove it works before closing the first.
• Mismatched shared key. Authentication fails with no useful message on the client. Check the server’s logs, not the switch’s.
• No ip tacacs source-interface. Packets leave by whichever interface routing picks, the server does not recognise the source, and the failure is intermittent by design.
• transport input ssh before the keys exist. Instant remote lock-out.

## Slide 24
COMMON PITFALLS · SFTP — the device as a client
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• Enabling SCP without aaa authorization exec. Logs in, transfers nothing.
• Believing service password-encryption protects anything. Type 7 is reversible.
• Reaching for TFTP out of habit. It is off the blueprint and it was off the good-practice list long before that.

## Slide 25
BREAK & FIX · SYMPTOM
Chapter 23
Nobody can log in to any switch. The AAA server is up and other services work.
A campus of forty switches, all authenticating to TACACS+. Overnight, logins begin failing everywhere. The TACACS+ server is running, responds to ping from a workstation, and is authenticating VPN users normally. Console access fails as well as SSH.
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2

## Slide 26
BREAK & FIX · YOUR MOVE
Chapter 23
Nobody can log in to any switch. The AAA server is up and other services work.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 27
BREAK & FIX · EVIDENCE
Chapter 23
show run | include aaa authentication
CAMPUS-SW1#
aaa authentication login default group TACGROUP local
aaa authentication enable default group TACGROUP enable
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 28
BREAK & FIX · EVIDENCE
Chapter 23
show aaa servers | include host|state
CAMPUS-SW1#
TACACS+: id 1, priority 1, host 10.0.0.20, auth-port 49
State: current UP, duration 61204s
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 29
BREAK & FIX · YOUR MOVE
Chapter 23
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Notes: The elimination matters as much as the answer.

## Slide 30
BREAK & FIX · DIAGNOSIS
Chapter 23
Why it is doing that
Diagnosis. The configuration has a correct fallback and the server is reachable and marked UP. That combination rules out both of the usual suspects at once — and it is the clue.
Because the server is reachable, the device sends the request and gets an answer. The answer is a rejection. Fallback to local never fires, because fallback happens on silence, not on refusal. The fault is therefore on the server: overnight, the group that grants network-device administration was changed, and the server is now correctly refusing everyone.
The tell is that console access fails too. A network-side or transport-side fault would leave the console working, because the console does not depend on the network. A fault that follows you to the console is in the authentication decision itself.
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2

## Slide 31
BREAK & FIX · THE FIX
Chapter 23
And the lesson
Immediate recovery. You need an account the switch can validate without the server. If a local account exists, use it — but the method list consults TACACS+ first and TACACS+ is answering, so it will not be reached. Break the server’s reachability from the switch deliberately, or use the password-recovery procedure on one switch, restore local access, and work from there.
The lasting fix is on the server, not the switches. Restore the administration group.
And the lesson to write down. A local fallback protects you from an unreachable server. It does not protect you from a reachable server that says no. Sites that care about this keep a break-glass local account and test it on a schedule — and keep at least one device out of AAA entirely, reachable out-of-band, as the way back in.
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2

## Slide 32
LAB · CML OR GNS3, WITH A TACACS+ OR RADIUS SERVER
Secure access, AAA, and a backup you can restore
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Platform note. Packet Tracer models a simplified AAA server and will carry tasks 1–4. Tasks 5–8 need a real server (tac_plus or FreeRADIUS) and a real SSH stack, so use CML or GNS3.
Topology. Two switches and a router, a management VLAN, a Linux host running the AAA server and an SFTP server, and your own workstation.
1. Build baseline access on all three devices: hostname, domain name, two local users at different privilege levels, enable secret, RSA keys, SSH version 2, transport input ssh. Verify by SSH and confirm Telnet is refused.
2. Prove the password types. Run show run | include username and identify the type number on each. Add one user with password instead of secret and compare, then remove it.
3. Configure AAA against the server with a local fallback. Open a second SSH session before you test, and keep it open throughout.
4. Verify with show aaa servers and by logging in as a server-defined user. Confirm the privilege level you land in.

## Slide 33
LAB · CML OR GNS3, WITH A TACACS+ OR RADIUS SERVER
Secure access, AAA, and a backup you can restore (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
1. Break 1. Stop the AAA server. Log in again and confirm the local fallback works. Record how long the device waits before falling back.
2. Break 2. Restart the server and disable your test account on it. Attempt to log in. Explain why the local fallback does not rescue you, and relate this to the Break & Fix above.
3. Break 3. Remove local from the method list, stop the server, and log out of every session. Recover the device. Write down how long it took and what you would have done differently.
4. Enable the SCP server and copy the running configuration to your workstation. Then omit aaa authorization exec and observe the different failure.

## Slide 34
LAB · CML OR GNS3, WITH A TACACS+ OR RADIUS SERVER
Secure access, AAA, and a backup you can restore (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
1. Configure archive to write to SFTP on every write memory. Make a change, save, and confirm the archived file appears.
2. Extension. Copy an image by SFTP, verify its MD5 against the published hash, and deliberately truncate a copy to see what verify reports.

## Slide 35
CHECKPOINT 1 of 5
In aaa authentication login default group TACGROUP local, when is local used and when is it not?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 36
ANSWER
Checkpoint 1 of 5
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
In aaa authentication login default group TACGROUP local, when is local used and when is it not?
local is used only when the TACACS+ group does not respond at all. If a server answers and rejects the credentials, that is an answer, the list ends, and the local database is never consulted. Fallback protects against a dead server, not a forgotten password.

## Slide 37
CHECKPOINT 2 of 5
Give the transport, port and encryption scope of TACACS+ and of RADIUS, and say which you would choose for controlling switch administrators.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 38
ANSWER
Checkpoint 2 of 5
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Give the transport, port and encryption scope of TACACS+ and of RADIUS, and say which you would choose for controlling switch administrators.
TACACS+ is TCP 49 and encrypts the entire packet body; RADIUS is UDP 1812/1813 and encrypts only the password field. Choose TACACS+ for switch administrators — it separates authorization fully and supports per-command control.

## Slide 39
CHECKPOINT 3 of 5
Why must ip domain name be set before generating RSA keys?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 40
ANSWER
Checkpoint 3 of 5
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Why must ip domain name be set before generating RSA keys?
Because the RSA key pair is named hostname.domain. Without a domain name the device has no full name to label the key with and refuses.

## Slide 41
CHECKPOINT 4 of 5
What three commands does the IOS SCP server require, and what is the symptom when the authorization line is missing?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 42
ANSWER
Checkpoint 4 of 5
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
What three commands does the IOS SCP server require, and what is the symptom when the authorization line is missing?
aaa new-model, an aaa authentication login method, and aaa authorization exec — plus ip scp server enable itself. Without the authorization line, users authenticate successfully and every transfer is then refused.

## Slide 43
CHECKPOINT 5 of 5
Why did v2.0 replace TFTP with SFTP and SCP? Give three reasons.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 44
ANSWER
Checkpoint 5 of 5
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
Why did v2.0 replace TFTP with SFTP and SCP? Give three reasons.
TFTP has no user authentication, sends everything in clear text, and runs over UDP with no integrity protection. A configuration file in flight — including its shared secrets — is readable by anyone on the path, and anyone who can reach the server can fetch any file whose name they guess.

## Slide 45
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• Baseline first: hostname, domain name, local users with algorithm-type scrypt secret, enable secret, RSA keys, ip ssh version 2, login local, transport input ssh.
• Type 7 is obfuscation, not encryption. Type 8 and 9 are the current choices. enable password should not exist.
• AAA answers three separate questions through ordered method lists. A method is skipped only when it does not respond — a rejection ends the list.
• Always end an authentication method list with local, and always test from a second session.

## Slide 46
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 23. Device Access, AAA and Secure File Transfer
4.1 4.2
• TACACS+: TCP 49, whole packet encrypted, full AAA separation, per-command authorization, device administration. RADIUS: UDP 1812/1813, password only encrypted, combined authentication and authorization, network access.
• SCP puts file transfer inside SSH; IOS can be an SCP server and an SFTP client. Both replace TFTP, which authenticates nobody and encrypts nothing.
• Verify an image’s hash before reloading onto it.

## Slide 47
Where we got to
• Baseline first: hostname, domain name, local users with algorithm-type scrypt secret, enable secret, RSA keys, ip ssh version 2, login local, transport input ssh.
• Type 7 is obfuscation, not encryption. Type 8 and 9 are the current choices. enable password should not exist.
• AAA answers three separate questions through ordered method lists. A method is skipped only when it does not respond — a rejection ends the list.
• Always end an authentication method list with local, and always test from a second session.
NEXT
Chapter 24 — Access Control Lists