## Slide 1
CCNA 200-301 V2.0
27
Wireless Principles
Part V — Wireless, Virtualisation and Operations
EXAM TOPICS
1.5
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 27: Wireless Principles. Blueprint topics: 1.5.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• Select a band and a channel plan, and explain why 2.4 GHz has only three usable channels.
• Describe the RF characteristics that decide whether a link works: signal strength, noise, SNR, and what happens to radio waves on the way.
• Compare WEP, WPA, WPA2 and WPA3, and distinguish personal from enterprise authentication.
• Identify causes of interference, and tell co-channel interference apart from adjacent-channel interference.
Notes: Wireless Principles 1.5

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Chapter 3 — wireless is a shared medium with collision avoidance rather than detection, and the contrast is the quickest way in. Chapter 9 for how access points attach to the wired network. Chapter 23 for RADIUS, which is what “enterprise” wireless authenticates against.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
band
channel
non-overlapping
channel bonding
dBm
RSSI
SNR
noise floor
attenuation
SSID
BSSID
WPA2
WPA3
SAE
802.1X
co-channel interference
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
Four named sub-topics, and the verb is describe
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
This is what the blueprint actually asks for
Topic 1.5 is describe wireless principles, with four sub-topics named explicitly: 1.5.a band and channel selection, 1.5.b RF characteristics, 1.5.c security protocols, 1.5.d cause of interference.
There is no wireless configuration on this blueprint. v1.1 asked you to build a WLAN in a controller GUI; v2.0 does not. Do not spend time learning WLC menus for this exam — spend it on the four lists in this chapter, because that is exactly what is examined.
Access points do appear elsewhere: 2.2 covers connecting them to a switch port, which is Chapter 9’s material, and 1.6 covers the client end, which is Chapter 28’s.

## Slide 6
DEFINITION
Four names that get confused
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• SSID — the network’s name, as a human sees it. Several APs normally share one.
• BSSID — the MAC address of one radio on one AP. This is what a client is actually associated to.
• BSS — one AP’s coverage area. ESS — several APs sharing an SSID so a client can roam between them.
• Roaming — a client deciding, on its own, to move from one BSSID to another within the same ESS. The client decides, not the network. This matters in Chapter 28.
Notes: A switch port is a private, full-duplex conversation between two devices. A radio channel is a room everybody shouts across. Three consequences shape everything else in this chapter. It is half duplex and shared. Only one device on a channel may transmit at a time. Ten clients on one access point share the airtime between them — the advertised data rate is not per-client bandwidth. Collisions cannot be detected, only avoided. A radio cannot listen while it transmits, so Ethernet’s CSMA/CD is impossible. Wireless uses CSMA/CA: listen, wait a random interval, transmit, and expect an acknowledgement for every frame. The medium is unlicensed and shared with strangers. Your neighbour’s network, a microwave oven and a Bluetooth headset all have the same right to the spectrum that you do.

## Slide 7
WATCH OUT
Why 2.4 GHz has only three channels
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
The band is divided into channels numbered 1 to 11 in North America (1 to 13 in much of the rest of the world), spaced 5 MHz apart. But each channel is 20 MHz wide. A 20 MHz signal spaced 5 MHz from its neighbour overlaps it heavily.
To avoid overlap you need five channel numbers of separation — which in a band of eleven gives you exactly three: 1, 6 and 11. Any other plan puts two networks partly on top of each other, which is worse than putting them fully on top of each other. That last point is the one the exam tests, and it is explained below.

## Slide 8
Bands and channels
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
The 2.4 GHz band. Channels 1, 6 and 11 are the only trio that does not overlap; anything between them interferes with two networks instead of sharing one.

## Slide 9
WATCH OUT
The trade-off, which is examinable
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Every doubling of channel width roughly doubles throughput — and halves the number of non-overlapping channels available, and raises the noise floor by about 3 dB because the receiver is listening to twice as much spectrum.
So: bonding is sensible at 5 and 6 GHz where there is room, and in a low-density deployment. It is never sensible at 2.4 GHz, where a 40 MHz channel consumes most of the band and leaves no clean plan for anyone, including you.
Notes: Wider channels carry more data. 802.11n and later can bond adjacent 20 MHz channels into 40, 80 or 160 MHz.

## Slide 10
CONCEPT
DFS channels
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Part of the 5 GHz band is shared with weather and military radar. Access points using those channels must run dynamic frequency selection: listen before transmitting, and vacate the channel within seconds if radar appears.
The practical consequence is a real fault you will meet: a DFS event moves an AP to a different channel and every client on it is briefly disconnected. If a site reports unexplained drops on 5 GHz at irregular intervals — particularly near an airport or a coast — DFS is the first thing to check.

## Slide 11
WORKED EXAMPLE
The two rules that replace a calculator
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
The 3 dB rule: +3 dB doubles power, -3 dB halves it. The 10 dB rule: +10 dB multiplies by ten, -10 dB divides by ten.
So 20 dBm is 10 × 10 × 1,textmW = 100,mW. And 23 dBm is double that again — 200 mW.
Going the other way: a client receiving -70 dBm is receiving one ten-millionth of a milliwatt. Radio receivers are extraordinarily sensitive, which is why small amounts of noise matter so much.
Notes: Radio power spans an enormous range, so it is measured logarithmically. dBm — power relative to 1 milliwatt. 0 dBm is 1 mW. Absolute. dB — a ratio, with no unit of its own. A gain or a loss. dBi — antenna gain relative to a theoretical isotropic radiator.

## Slide 12
WATCH OUT
Signal strength alone tells you almost nothing
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
A client at -65 dBm sounds healthy. If the noise floor on that channel is -70 dBm, the SNR is 5 dB and the link is unusable.
A client at -75 dBm sounds marginal. With a noise floor of -95 dBm the SNR is 20 dB and it works perfectly well.
SNR is the number that decides whether a link works. Users and helpdesk tools report bars and RSSI; you should ask for the noise floor before drawing any conclusion. This is the single most useful idea in the chapter and it comes up again in Chapter 28.

## Slide 13
CONCEPT
Antennas do not amplify
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
An antenna with 9 dBi of gain does not create energy. It shapes the same energy into a narrower pattern — more in the direction you want, less everywhere else.
• Omnidirectional — radiates in a doughnut around the antenna. Ceiling APs in offices. Low gain, wide coverage.
• Directional (patch, Yagi, parabolic) — radiates into a cone. Point-to-point links, long corridors, lecture theatres, warehouse aisles. High gain, narrow coverage.
A common failure at scale: replacing omnidirectional antennas with high-gain ones to “fix” coverage, and discovering the new pattern misses the floor directly below the AP entirely.

## Slide 14
ON THE EXAM
The two distinctions to get right
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
This is what the blueprint actually asks for
Personal against Enterprise is about who authenticates.
• Personal (PSK) — one shared passphrase for everyone. Simple. Nobody is individually identified, and changing it means changing it on every device.
• Enterprise (802.1X/EAP) — each user authenticates individually against a RADIUS server (Chapter 23). Revoke one account without touching anyone else. This is what a campus should run.
WPA2 against WPA3 is about how the key is agreed. WPA2-Personal’s 4-way handshake can be captured and attacked offline, so a weak passphrase falls. WPA3 replaces it with SAE, where an attacker must guess against the live network each time — so offline attack is not possible, and each session has its own key even if the passphrase is later disclosed.

## Slide 15
CONCEPT
Open networks and OWE
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
An open network with no passphrase sends everything in clear. Opportunistic Wireless Encryption, part of the WPA3 family and marketed as “Enhanced Open”, encrypts the traffic anyway using an unauthenticated key agreement.
It stops passive eavesdropping on a guest network. It does not authenticate the AP, so it does not stop somebody standing up a fake one. Worth deploying on guest SSIDs; not worth mistaking for security.

## Slide 16
WATCH OUT
Counter-intuitive, and a favourite question
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Co-channel interference is better than adjacent-channel interference.
Two APs on channel 6 can hear one another, so CSMA/CA works: they defer to each other and share the channel. Throughput halves; nothing is corrupted.
Two APs on channels 6 and 8 cannot decode one another — each sees the other only as raised noise. Neither defers, both transmit, and frames are destroyed and retransmitted. Throughput collapses.
So a bad channel plan is worse than no channel plan. If you take one thing from this section: overlap, do not straddle.

## Slide 17
CONCEPT
Non-Wi-Fi interference needs a spectrum analyser
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
A Wi-Fi analyser on a laptop shows you Wi-Fi. A microwave oven does not appear in it, because it transmits no frames — it just raises the noise floor.
So a channel that looks empty in a Wi-Fi scan and performs terribly is the signature of a non-Wi-Fi source. Finding it needs a spectrum analyser, which looks at raw RF energy rather than at decoded frames. Knowing that the distinction exists is the examinable part.
Notes: Microwave ovens — 2.4 GHz, high power, intermittent. Classic symptom: wireless fails in the staff room at 12:30 every day. Bluetooth and wireless headsets — 2.4 GHz frequency hopping, low power, constant. Cordless phones, video senders, wireless cameras, baby monitors — often 2.4 GHz, often continuous, often invisible to Wi-Fi tools because they are not Wi-Fi. Radar — 5 GHz, and triggers DFS events rather than plain interference. Too much of your own network — APs at full transmit power in a dense deployment interfere with each other. Reducing power often improves a busy site. Physical obstruction — not interference strictly, but it presents identically to a user. Lift shafts, fire doors, foil-backed insulation, and fish tanks.

## Slide 18
COMMON PITFALLS · Everything else
Common pitfalls
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• Using any 2.4 GHz channel other than 1, 6 or 11. Creates ACI for two networks instead of sharing with one.
• Bonding channels at 2.4 GHz. Consumes the band.
• Reading RSSI without the noise floor. SNR is the number that matters.
• Turning transmit power up to fix coverage. In a dense deployment this usually makes things worse, and it does nothing for the client’s weaker transmitter on the return path.
• Confusing SSID with BSSID. A client roams between BSSIDs while the SSID never changes.
• Assuming the AP controls roaming. The client decides.

## Slide 19
COMMON PITFALLS · Everything else
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• Treating WPA2-Personal as adequate for a campus. Use Enterprise; a shared passphrase cannot be revoked for one person.
• Expecting a Wi-Fi scanner to reveal a microwave oven.

## Slide 20
BREAK & FIX · SYMPTOM
Chapter 27
One lecture theatre is unusable when full and perfect when empty.
A 200-seat theatre has four access points and tests clean every morning. During lectures, clients associate but throughput collapses and voice calls fail. The wired network behind the APs shows no errors and no congestion. A survey taken at 08:00 shows every seat at -58 dBm or better.
% A listing nested inside a breakable box cannot itself be split, so % without this tcolorbox forces it onto the page and reports an overfull % vbox. Break the outer box early instead.
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5

## Slide 21
BREAK & FIX · YOUR MOVE
Chapter 27
One lecture theatre is unusable when full and perfect when empty.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 22
BREAK & FIX · EVIDENCE
Chapter 27
wifi scan — summary
Survey, taken during a full lecture#
BSSID SSID Chan Width RSSI Noise SNR
00:11:22:aa:bb:01 CAMPUS 6 20 -61 -73 12
00:11:22:aa:bb:02 CAMPUS 6 20 -64 -73 9
00:11:22:aa:bb:03 CAMPUS 8 20 -59 -73 14
00:11:22:aa:bb:04 CAMPUS 11 20 -66 -73 7
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 23
BREAK & FIX · YOUR MOVE
Chapter 27
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Notes: The elimination matters as much as the answer.

## Slide 24
BREAK & FIX · DIAGNOSIS
Chapter 27
Why it is doing that
Diagnosis. Three faults are visible in that one table, and they compound.
First, the noise floor is -73 dBm. A clean environment is around -92. Something is raising it by nearly 20 dB, and the strong signal readings are therefore worthless — every SNR here is below the 20 dB minimum for reliable data.
Second, the channel plan is wrong. Four APs in one room are using channels 6, 6, 8 and 11. The pair on channel 6 is co-channel interference, which is merely wasteful. But channel 8 overlaps both 6 and 11 — it is adjacent-channel interference against three other radios simultaneously, and that is corruption rather than sharing.
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5

## Slide 25
BREAK & FIX · DIAGNOSIS
Chapter 27
Why it is doing that
Third, the room is full of people. Bodies are largely water, which absorbs 2.4 GHz strongly. This is why it works when empty: the morning survey measured a room with no attenuation in it and no clients contending.
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5

## Slide 26
BREAK & FIX · THE FIX
Chapter 27
And the lesson
Fix, in order of value.
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5

## Slide 27
LAB · ANY LAPTOP OR PHONE WITH A WI-FI ANALYSER
A survey of somewhere you actually use
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Platform note. This topic has no configuration on the blueprint, so this lab is measurement rather than building. Use any Wi-Fi analyser — built-in tools work: netsh wlan show interfaces on Windows, the option-click Wi-Fi menu on macOS, iw dev wlan0 scan on Linux.
Location. A room you can visit twice, ideally once empty and once busy.
1. Record every visible SSID, its BSSIDs, band, channel and channel width. Draw the channel occupancy of 2.4 GHz as a diagram like the one in this chapter.
2. Identify every case of adjacent-channel interference in what you found. For each, name the channel that should have been used instead.
3. Record RSSI and noise for your own connection at five points: beside the AP, across the room, behind a wall, around a corner, and at the far edge of coverage. Calculate SNR at each.
4. Plot RSSI against distance. Confirm the roughly 6 dB loss per doubling of distance, and identify where your measurements depart from it and why.

## Slide 28
LAB · ANY LAPTOP OR PHONE WITH A WI-FI ANALYSER
A survey of somewhere you actually use (continued)
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
1. Find one place where signal is strong and SNR is poor. Explain what that tells you.
2. Identify the security protocol in use on each SSID you can see. Note any still offering WPA or WEP.
3. Move between two APs on the same SSID while watching the BSSID. Record the RSSI at which your client chose to roam — and note that you did not choose it and the network did not either.
4. If you can: repeat the RSSI and noise measurements with the room occupied. Compare, and quantify the absorption.

## Slide 29
LAB · ANY LAPTOP OR PHONE WITH A WI-FI ANALYSER
A survey of somewhere you actually use (continued)
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
1. Extension. Write the one-page recommendation you would give the building’s network team, with the evidence for each point.

## Slide 30
CHECKPOINT 1 of 6
Why does the 2.4 GHz band have only three non-overlapping channels, and which are they?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 31
ANSWER
Checkpoint 1 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Why does the 2.4 GHz band have only three non-overlapping channels, and which are they?
Because channels are numbered 5 MHz apart but each is 20 MHz wide, so five channel numbers of separation are needed to avoid overlap. In a band of eleven usable channels that gives exactly three: 1, 6 and 11.

## Slide 32
CHECKPOINT 2 of 6
Which is worse, co-channel or adjacent-channel interference, and why?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 33
ANSWER
Checkpoint 2 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Which is worse, co-channel or adjacent-channel interference, and why?
Adjacent-channel is worse. Two APs on the same channel can hear each other, so CSMA/CA works and they share the airtime — throughput halves but nothing is corrupted. On partly overlapping channels neither can decode the other, so neither defers, both transmit, and frames are destroyed and retransmitted.

## Slide 34
CHECKPOINT 3 of 6
A client reports -62 dBm and cannot hold a call. What is the next number you ask for, and what would make this normal?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 35
ANSWER
Checkpoint 3 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
A client reports -62 dBm and cannot hold a call. What is the next number you ask for, and what would make this normal?
The noise floor, so you can calculate SNR. A signal of -62 is strong; if the noise floor is around -70 the SNR is only 8 dB, well below the 25 dB voice needs. That would make the report entirely normal.

## Slide 36
CHECKPOINT 4 of 6
State the difference between WPA2-Personal and WPA2-Enterprise, and between WPA2 and WPA3.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 37
ANSWER
Checkpoint 4 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
State the difference between WPA2-Personal and WPA2-Enterprise, and between WPA2 and WPA3.
Personal shares one passphrase among everyone and identifies nobody; Enterprise authenticates each user individually via 802.1X against a RADIUS server, so one account can be revoked without touching anyone else. WPA2 uses AES-CCMP with a 4-way handshake that can be captured and attacked offline; WPA3 replaces it with SAE, which resists offline attack and adds forward secrecy.

## Slide 38
CHECKPOINT 5 of 6
Give two reasons a room might work when empty and fail when full.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 39
ANSWER
Checkpoint 5 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
Give two reasons a room might work when empty and fail when full.
Bodies are largely water, which absorbs 2.4 GHz strongly — so a full room attenuates far more than an empty one. And a full room means many clients contending for the same airtime on a half-duplex shared medium.

## Slide 40
CHECKPOINT 6 of 6
What kind of interference is invisible to a Wi-Fi analyser, and what tool finds it?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 41
ANSWER
Checkpoint 6 of 6
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
What kind of interference is invisible to a Wi-Fi analyser, and what tool finds it?
Non-Wi-Fi interference — a microwave oven, a video sender, a cordless phone. It transmits no frames, so it never appears in a Wi-Fi scan; it simply raises the noise floor. Finding it needs a spectrum analyser, which looks at raw RF energy rather than decoded frames.

## Slide 42
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• Wireless is half duplex, shared, and uses collision avoidance. The advertised rate is shared between everyone on the channel.
• SSID is the name, BSSID is the radio’s MAC. The client decides when to roam.
• 2.4 GHz: three non-overlapping channels, 1, 6 and 11. 5 GHz: around 25, some DFS. 6 GHz: 59, newest clients only.
• Channel bonding doubles throughput, halves the channel count and raises the noise floor. Never at 2.4 GHz.
• +3 dB doubles power, +10 dB multiplies by ten. 0 dBm is 1 mW.

## Slide 43
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 27. Wireless Principles
1.5
• SNR decides whether a link works, not RSSI. Aim for 25 dB for voice, 20 dB minimum for data.
• Radio waves are absorbed, reflected, refracted, diffracted and scattered; free-space loss costs about 6 dB per doubling of distance.
• WEP is broken, WPA deprecated, WPA2 uses AES-CCMP with a 4-way handshake, WPA3 uses SAE and resists offline attack. Personal shares a passphrase; Enterprise authenticates each user via RADIUS.
• Co-channel interference shares politely; adjacent-channel interference corrupts. A bad plan is worse than no plan.

## Slide 44
Where we got to
• Wireless is half duplex, shared, and uses collision avoidance. The advertised rate is shared between everyone on the channel.
• SSID is the name, BSSID is the radio’s MAC. The client decides when to roam.
• 2.4 GHz: three non-overlapping channels, 1, 6 and 11. 5 GHz: around 25, some DFS. 6 GHz: 59, newest clients only.
• Channel bonding doubles throughput, halves the channel count and raises the noise floor. Never at 2.4 GHz.
NEXT
Chapter 28 — Troubleshooting Client Connectivity