## Slide 1
CCNA 200-301 V2.0
31
Ansible and Configuration Management
Part V — Wireless, Virtualisation and Operations
EXAM TOPICS
5.5
LECTURER
Dr. Mustafa Hameed
THE ISLAMIA UNIVERSITY OF BAHAWALPUR
Department of Information Technology
Notes: Chapter 31: Ansible and Configuration Management. Blueprint topics: 5.5.

## Slide 2
LEARNING OUTCOMES
What you will be able to do
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
• Explain what agentless means and why it matters for network devices.
• Read an inventory file and a playbook, and say what each line does.
• Use Ansible to run show commands across many devices and to push a configuration change.
• Recognise the three failures that account for most broken playbooks: YAML indentation, the wrong module, and a change that was never saved.
Notes: Ansible and Configuration Management 5.5

## Slide 3
ASSUMED KNOWLEDGE
Before we start
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Chapter 23 for SSH and credentials — Ansible logs in exactly as you do. Chapter 30 for the five management approaches; this chapter is the automation-based one made concrete. Chapter 7 for the commands being pushed.

## Slide 4
KEY TERMS
Vocabulary for this chapter
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
agentless
idempotent
control node
managed node
inventory
play
task
module
playbook
facts
YAML
dry run
vault
Each is defined where it first matters — not here.
Notes: Do not define these now - they are defined as they arrive. This slide is for the students' notes.

## Slide 5
ON THE EXAM
The verb is use
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
This is what the blueprint actually asks for
Topic 5.5 is use configuration management mechanisms such as Ansible to execute commands. It is the only topic in domain 5 that is not describe, select or interpret — so you are expected to be able to read a playbook and say what it will do to which devices.
“Such as Ansible” leaves the door open to Puppet, Chef and SaltStack, but every published Cisco example uses Ansible, and Ansible is the one whose agentless model actually suits network hardware. Learn Ansible; know the other names and the one-line difference.

## Slide 6
DEFINITION
Configuration management
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Describing the state a set of machines should be in, and using a tool to make them match that description — repeatably, and with a record of what was done.
Notes: Forty access switches need one new VLAN and one new ACL line. Done by hand that is forty SSH sessions, forty opportunities to typo, and no record of which device got which version. Done a second time next month, it is forty more.

## Slide 7
WATCH OUT
This is the whole reason Ansible dominates network automation
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
A server can run an agent. A Catalyst switch cannot — it is an appliance, and you may not install arbitrary software on it. Any tool that requires an agent is therefore unavailable for the devices this exam is about.
Ansible needs nothing on the device except the SSH access you already configured in Chapter 23. That is the answer to “why Ansible for networks”, and it is a fair exam question.

## Slide 8
DEFINITION
Idempotent
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
An operation that produces the same result whether it is applied once or twenty times. Ansible tasks are written to describe a desired state, so a task that has already been satisfied reports ok and changes nothing.
This is what makes it safe to run the same playbook every day. A script that blindly types commands is not idempotent; a playbook that says “this line should be present” is.

## Slide 9
The pieces
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Everything lives on the control node. The devices need only the SSH access they already have.

## Slide 10
CONFIGURE
Inventory.yml
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Ansible · YAML
all:
children:
access_switches:
hosts:
SW1: { ansible_host: 10.0.0.11 }
SW2: { ansible_host: 10.0.0.12 }
SW3: { ansible_host: 10.0.0.13 }
routers:
hosts:
R1: { ansible_host: 10.0.0.1 }
vars:
# network_cli is essential. Without it Ansible assumes the far end
# is a Linux host with a Python interpreter, and every task fails
# with an error that does not mention the real problem.
ansible_connection: ansible.netcommon.network_cli
ansible_network_os: cisco.ios.ios
ansible_user: netadmin
Notes: Playbooks are YAML, and almost every first failure is a YAML failure. Three rules carry you: Indentation is structure, and it must be spaces. A tab character is a syntax error. Two spaces per level is the convention. A leading - makes a list item. Items at the same indentation belong to the same list. key: value makes a mapping. The space after the colon is required.

## Slide 11
WATCH OUT
Never put the password in the inventory
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Use ansible-vault to encrypt a variables file, and supply the key at run time:
Then run with –ask-vault-pass, or use SSH keys and no password at all. A plain-text credential in a file that is about to be committed to version control is how credentials leak, and “it is only the lab” is how the habit forms.

## Slide 12
VERIFY
ansible access_switches -i inventory.yml -m cisco.ios.ios_command -a "commands=’show version’"
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Linux or macOS
SW1 | SUCCESS => {
"changed": false,
"stdout_lines": [["Cisco IOS XE Software, Version 17.12.04", "..."]]
}
SW2 | SUCCESS => {
"changed": false,
"stdout_lines": [["Cisco IOS XE Software, Version 17.09.05", "..."]]
}

## Slide 13
CONFIGURE
Audit.yml — collect and report
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Ansible · YAML
---
- name: Audit access switches
hosts: access_switches
gather_facts: false
tasks:
- name: Collect version and inventory facts
cisco.ios.ios_facts:
gather_subset:
- hardware
register: device_facts
- name: Show what we found
debug:
msg: "{{ inventory_hostname }} runs {{ ansible_net_version }}"
- name: Run a show command and keep the output
cisco.ios.ios_command:
commands:
- show interfaces status
register: intf
Notes: Note "changed": false. A show command reads and does not alter, so nothing changed — and Ansible says so explicitly. That field is the one to watch on every run.

## Slide 14
CONFIGURE
Audit.yml — collect and report (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Ansible · YAML
- name: Write it to a file on the control node
copy:
content: "{{ intf.stdout[0] }}"
dest: "./reports/{{ inventory_hostname }}-interfaces.txt"
delegate_to: localhost

## Slide 15
CONFIGURE
Vlan.yml — make a change on every switch
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Ansible · YAML
---
- name: Add the guest VLAN everywhere
hosts: access_switches
gather_facts: false
tasks:
- name: Create VLAN 40
cisco.ios.ios_config:
lines:
- name GUEST
parents: vlan 40
- name: Allow it on the uplink trunk
cisco.ios.ios_config:
lines:
- switchport trunk allowed vlan add 40
parents: interface GigabitEthernet1/0/48
# Without this the change lives in the running configuration only
# and is lost at the next reload. "modified" saves only when this
# run actually changed something.

## Slide 16
CONFIGURE
Vlan.yml — make a change on every switch (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Ansible · YAML
- name: Save the configuration
cisco.ios.ios_config:
save_when: modified

## Slide 17
WATCH OUT
ios_command reads, ios_config writes
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
This is the distinction the exam will test and the one beginners get wrong.
ios_command runs commands in EXEC mode and returns their output. It cannot make a configuration change, and it will refuse configuration commands outright rather than silently failing.
ios_config enters configuration mode and applies lines, using parents to say which sub-mode they belong in. It compares against the running configuration first, so it is idempotent.
A playbook that reports success and changes nothing is very often ios_command where ios_config was meant.

## Slide 18
VERIFY
ansible-playbook -i inventory.yml vlan.yml –check –diff
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Linux or macOS
TASK [Create VLAN 40] **********************************************
changed: [SW1]
changed: [SW2]
ok: [SW3]
PLAY RECAP *********************************************************
SW1 : ok=2 changed=1 unreachable=0 failed=0
SW2 : ok=2 changed=1 unreachable=0 failed=0
SW3 : ok=3 changed=0 unreachable=0 failed=0

## Slide 19
CONCEPT
Read the recap, every time
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
–check is a dry run: Ansible reports what it would do and touches nothing. –diff shows the exact lines. Run this before every change to production, without exception.
In that output, SW3 reports ok rather than changed because it already has VLAN 40. That is idempotency visible in the recap, and it is also a useful audit: the difference between the two tells you which devices had drifted.
unreachable is a different failure from failed: unreachable means Ansible could not log in at all, failed means it logged in and the task did not work.

## Slide 20
COMMON PITFALLS · Check before you commit
Common pitfalls
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
• Tabs in YAML. A syntax error, and the message rarely says “tab”. Configure your editor to insert spaces.
• Missing ansible_connection: network_cli. Ansible tries to run Python on a switch and fails confusingly.
• ios_command where ios_config was meant. Reports success, changes nothing.
• No save_when. The change works until the device reloads.
• Wrong parents. Lines are applied in global configuration mode instead of under the interface, which either errors or does something you did not intend.
• Skipping –check. There is no undo across forty devices.

## Slide 21
COMMON PITFALLS · Check before you commit
Common pitfalls (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
• Credentials in the inventory file. Use vault or SSH keys.
• Running against all when you meant one group. Check the hosts: line before every run. It is the single most expensive typo available to you.

## Slide 22
BREAK & FIX · SYMPTOM
Chapter 31
The playbook reports success on all forty switches. After a power cut, eleven have lost the change.
A new VLAN was added across the access layer with a playbook. Every device reported changed, spot checks confirmed the VLAN existed, and the change was signed off. Three weeks later a power event reboots part of the estate, and eleven switches come back without VLAN 40. The twenty-nine that did not lose power still have it.
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 23
BREAK & FIX · YOUR MOVE
Chapter 31
The playbook reports success on all forty switches. After a power cut, eleven have lost the change.
What would you check first — and what do you expect to see?
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Notes: Pause here. Take two or three answers before advancing. The point is the prediction, not the command.

## Slide 24
BREAK & FIX · EVIDENCE
Chapter 31
show archive config differences nvram:startup-config system:running-config
SW1#
!Contextual Config Diffs:
+vlan 40
+ name GUEST
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Notes: Read it aloud. Ask what single field decides the answer.

## Slide 25
BREAK & FIX · YOUR MOVE
Chapter 31
What is the fault — and what does this output rule out?
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Notes: The elimination matters as much as the answer.

## Slide 26
BREAK & FIX · DIAGNOSIS
Chapter 31
Why it is doing that
Diagnosis. There is no save_when task. ios_config writes to the running configuration, exactly as typing the commands would — and like typing them, it does not save. Every switch was correctly configured and none of them wrote that configuration to startup-config.
The evidence pattern confirms it precisely: the split is not between devices that the playbook succeeded on and devices it failed on. It is between devices that rebooted and devices that did not. Twenty-nine switches still have the VLAN because they have been up the whole time and are still running the configuration Ansible applied. The eleven that power-cycled reloaded startup-config, which never contained it.
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 27
BREAK & FIX · DIAGNOSIS
Chapter 31
Why it is doing that
Any fault that correlates with reboots rather than with the change itself points at the running-versus-startup distinction.
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 28
BREAK & FIX · THE FIX
Chapter 31
Vlan.yml — as it was run
Ansible · YAML
---
- name: Add the guest VLAN everywhere
hosts: access_switches
gather_facts: false
tasks:
- name: Create VLAN 40
cisco.ios.ios_config:
lines:
- name GUEST
parents: vlan 40
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 29
BREAK & FIX · THE FIX
Chapter 31
Vlan.yml — corrected
Ansible · YAML
- name: Save the configuration
cisco.ios.ios_config:
save_when: modified
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 30
BREAK & FIX · THE FIX
Chapter 31
And the lesson
Fix. Add the save task and re-run.
save_when: modified writes only when the run actually changed something, so re-running against the twenty-nine devices that are already correct costs nothing. The eleven get the VLAN and a save.
The verification lesson. The spot check confirmed the VLAN existed — in the running configuration. It should have compared running against startup:
Any output at all from that command means unsaved changes are present. Making it the last step of every change — by hand or as a final Ansible task — closes this class of fault permanently.
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5

## Slide 31
LAB · CML OR GNS3, WITH A LINUX CONTROL NODE
Automating a change you would otherwise do forty times
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
Platform note. Ansible needs real SSH and a real Python environment on the control node. Packet Tracer cannot do this. Use CML or GNS3 with three or more IOS devices and a Linux VM, or install Ansible on your own machine and point it at the lab.
1. Install Ansible and the cisco.ios collection on the control node. Record the versions of both.
2. Configure SSH and a local user on three devices as in Chapter 23. Confirm you can log in by hand before involving Ansible at all — if this does not work, nothing after it will.
3. Write inventory.yml with two groups. Verify with ansible-inventory –list.
4. Run an ad-hoc ios_command for show version against one group. Then deliberately remove ansible_connection and run it again. Record the error and explain why it does not mention the real cause.

## Slide 32
LAB · CML OR GNS3, WITH A LINUX CONTROL NODE
Automating a change you would otherwise do forty times (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
1. Store the password with ansible-vault and run using –ask-vault-pass. Confirm the file is unreadable without the key.
2. Write audit.yml to gather facts and write a per-device report file on the control node. Confirm every task reports changed: false and explain why.
3. Write vlan.yml to add a VLAN and allow it on a trunk. Run with –check –diff first. Record the diff, then run for real.
4. Run it a second time with no changes. Confirm every device reports ok rather than changed. This is idempotency; write down what you would conclude if one device reported changed on the second run.

## Slide 33
LAB · CML OR GNS3, WITH A LINUX CONTROL NODE
Automating a change you would otherwise do forty times (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
1. Break 1. Reproduce the Break & Fix. Omit save_when, apply a change, reload a device, and confirm the loss. Then add the save task and repeat.
2. Break 2. Replace ios_config with ios_command for the VLAN task. Record exactly what Ansible reports and what the device shows.
3. Break 3. Introduce a tab character into the playbook. Record the error message and how long it takes you to find it.
4. Extension. Add a final task that runs the show archive config differences command from this chapter and fails the play if it returns anything. You now cannot leave a change unsaved.

## Slide 34
CHECKPOINT 1 of 6
What does agentless mean, and why does it decide the choice of tool for network devices?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 35
ANSWER
Checkpoint 1 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
What does agentless mean, and why does it decide the choice of tool for network devices?
It installs nothing on the managed device and connects over SSH. It decides the choice because you cannot install an agent on a Catalyst switch — so any agent-based tool (Puppet, Chef) is simply unavailable for network hardware, while Ansible needs only the SSH access already configured.

## Slide 36
CHECKPOINT 2 of 6
What is idempotency, and where do you see it in a play recap?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 37
ANSWER
Checkpoint 2 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
What is idempotency, and where do you see it in a play recap?
An operation produces the same result whether applied once or many times. In the recap you see it as ok rather than changed on a device that is already in the desired state — so a second run of the same playbook reports changed=0.

## Slide 38
CHECKPOINT 3 of 6
State the difference between ios_command and ios_config.
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 39
ANSWER
Checkpoint 3 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
State the difference between ios_command and ios_config.
ios_command runs EXEC commands and returns output; it cannot make a configuration change. ios_config enters configuration mode and applies lines. A playbook reporting success while changing nothing is very often the former where the latter was meant.

## Slide 40
CHECKPOINT 4 of 6
What does save_when: modified do, and what fails without it?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 41
ANSWER
Checkpoint 4 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
What does save_when: modified do, and what fails without it?
It writes the running configuration to startup-config, but only when that run actually changed something. Without it the change lives in the running configuration only and is lost at the next reload — which shows up weeks later as a fault correlating with reboots rather than with the change.

## Slide 42
CHECKPOINT 5 of 6
What is the difference between unreachable and failed in the recap?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 43
ANSWER
Checkpoint 5 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
What is the difference between unreachable and failed in the recap?
unreachable means Ansible could not log in to the device at all. failed means it logged in and the task did not work. They point at completely different problems.

## Slide 44
CHECKPOINT 6 of 6
What do –check and –diff do, and when would you omit them?
Discuss · then advance
Notes: Ask the room. Do not advance until somebody commits to an answer.

## Slide 45
ANSWER
Checkpoint 6 of 6
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
What do –check and –diff do, and when would you omit them?
–check is a dry run — it reports what it would do and touches nothing. –diff shows the exact lines. Omit them only when you have already run with them and are applying the change you just reviewed.

## Slide 46
CHAPTER SUMMARY
What to take away
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
• Ansible is agentless: it connects over SSH and installs nothing. That is why it works on switches, where Puppet and Chef cannot.
• Tasks are idempotent — they describe desired state, so running twice changes nothing the second time.
• Playbooks are YAML: spaces not tabs, - for list items, key: value with a space after the colon.
• The inventory names devices and groups, and must set ansible_connection: network_cli and ansible_network_os.
• ios_command reads; ios_config writes, with parents to select the sub-mode.

## Slide 47
CHAPTER SUMMARY
What to take away (continued)
CCNA 200-301 v2.0 · Chapter 31. Ansible and Configuration Management
5.5
• save_when: modified writes to startup-config. Without it the change survives only until the next reload.
• –check –diff is a dry run. Use it before every production change.
• In the recap, changed means it acted, ok means it was already correct, unreachable means it never logged in.

## Slide 48
Where we got to
• Ansible is agentless: it connects over SSH and installs nothing. That is why it works on switches, where Puppet and Chef cannot.
• Tasks are idempotent — they describe desired state, so running twice changes nothing the second time.
• Playbooks are YAML: spaces not tabs, - for list items, key: value with a space after the colon.
• The inventory names devices and groups, and must set ansible_connection: network_cli and ansible_network_os.
NEXT
Chapter 32 — AI in Network Operations